## Slide 1: Ensuring the same epoch for timestamping for gPTP
S2-2503746

## Slide 2: Background
At SA2#167, S2-2501748 raised the question “How to guarantee the DS-TT and NW-TT use the same epoch for the TSi/TSe calculation.” and proposed various potential solutions.
During the discussion it became clear that there is no consensus whether there is a problem that needs fixing or not. As a result, no conclusions were reached at SA2#167.
This paper analyses whether there is any issue to be solved and whether any specification updates are needed.

## Slide 3: Analysis: Epoch to be used for ingress and egress timestamps (TSi, TSe)
TS 23.501 clause 5.27.1.3 clearly states that the ingress and egress timestamps at NW-TT and DS-TT, which are used for residence time calculation, are based on the 5G clock:
  “Ingress and egress time stamping are based on the 5G system clock at NW-TT and DS-TT.”
Observation: Ingress and egress timestamps are based on the 5G system clock, i.e., the epoch of the 5G system clock.

## Slide 4: Analysis: Synchronization of gNB, DS-TT and NW-TT; epoch for 5G internal clock
TS 23.501 mandates gNB, DS-TT and NW-TT to be time synchronized to the same clock (5G internal system clock).
  See TS 23.501 clause 5.27.1.1: “UE, gNB, UPF, NW-TT and DS- TTs are synchronized with the 5G GM (i.e. the 5G internal system clock) which shall serve to keep these network elements synchronized.”
No timescale (end hence epoch) is mandated for 5G internal system clock
How UPF receives 5G internal system time is not specified.
  Could be based on PTP or other mechanisms as per TS 23.501 “The UPF and NW-TT may get the 5G internal system clock via the underlying PTP compatible transport network with mechanisms outside the scope of 3GPP.”
UE receives the 5G internal system clock using RRC (SIB or unicast RRC)
  RAN indicates the timescale of the 5G clock (-> GPS or localClock). For localClock the epoch is unknown.
  Epoch does not have any relevance to the UE for the residence calculation (see slide in Annex)
Observations
  gNB, DS-TT and NW-TT are time-synchronized to the same 5G clock.
  The mechanisms how gNB and NW-TT are time synchronized to the 5G clock are not specified (and can differ).
  UE receives 5G clock from the gNB either using GPS timescale or using an unknown timescale/epoch.
  No timescale (and hence no epoch) is standardized for the 5G system clock.

## Slide 5: Conclusion
Conclusion
The answer to the question raised by S2-2501748 (“How to guarantee the DS-TT and NW-TT use the same epoch for the TSi/TSe calculation”) is the following:
Given that as per TS 23.501:
  no timescale/epoch is mandated;
  gNB, DS-TT and NW-TT need to be time synchronized to the same 5G clock;
  ingress and egress timestamps are based on the 5G system clock, i.e., the epoch of the 5G system clock;
5GS deployments may use any time scale (and epoch) for the 5G system clock as long as deployments ensure by configuration that NW-TT uses the same timescale for the TSi timestamps as the time that the RAN provides to UE/DS-TT over RRC.
Way forward
Current specification text is technically correct.
An option could be to clarify in TS 23.501 that deployments have to ensure (e.g., based on NW-TT configuration) that NW-TT uses the same timescale for TSi timestamps as RAN uses for the 5G time provided to UEs in RRC.

## Slide 6: Backup

## Slide 7: Analysis: Does the residence time calculation by DS-TT depend on the epoch?
Background
At SA2#167 claims were made that DS-TT would need to consider the epoch of the TSi timestamp when calculating the residence time.
Analysis
TS 23.501 clause 5.27.1.2.2:
Upon reception of a downlink gPTP message, NW-TT makes an ingress timestamping (TSi) for each gPTP event (Sync) message […].
NW-TT […] modifies the gPTP message payload […] as follows:
  Adds TSi in the Suffix field of the gPTP packet as described in Annex H.
DS-TT then creates egress timestamping (TSe) for the gPTP event (Sync) messages for external TSN working domains. The difference between TSi and TSe is considered as the calculated residence time spent within the 5G system for this gPTP message expressed in 5GS time.
The DS-TT then […] modifies the payload of the gPTP message that it sends towards the downstream TSN node as follows:
  Adds the calculated residence time expressed in TSN GM time to the correction field.
Observations
  DS-TT determines the residence time by calculating the delta between TSi and TSe.
  TSI and TSe are based on 5G system clock and the UE receives 5G time using RRC (see earlier slides).
  DS-TT simply calculates the delta between ingress and egress time stamps without any other considerations of the epoch of the 5G clock or the time contained in gPTP messages.
Conclusion: The residence time calculation by DS-TT does not depend on the epoch of the 5G system clock or the epoch of the time contained in the gPTP messages.

## Slide 8: Analysis: Issues for NW-TT due to Ethernet hardware limitations when using GPS timescale?
Background
At SA2#167 claims were made that
  (some) Ethernet chips may only support a single timescale (single counter) per PTP domain for hardware timestamping;
  this would cause issues if the 5G clock is using the GPS timescale as that would require NW-TT to
    create the TSi timestamps based on GPS timescale
    other timestamps in gPTP messages using PTP timescale (if the external TSN GM uses PTP timescale).
Analysis
  In Rel-16 two scenarios are supported
    External TSN GM connected on N6
    NW-TT acting as a gPTP GM for distributing the 5G system clock (see TS 23.501 clause 5.27.1.3 Note 2).
  No issue for the “NW-TT acting as gPTP GM” scenario since in this case only one timescale needs to be supported (same timescale in gPTP Sync message and TSi timestamp).
  No issue for the “external TSN GM connected on N6” scenario
    NW-TT does not send Sync and Follow-up messages with its own time (as NW-TT is not acting as GM)
    NW-TT sends peer delay messages on N6 that include NW-TT timestamps but those timestamps typically use the NW-TT’s local clock (no requirement to use PTP timescale) (see 802.1AS clause 11.1.2)
Conclusion: No issues for NW-TT to use GPS timescale even if the NW-TT Ethernet hardware only supports a single timescale per PTP domain.