## Slide 1: GEO Voice: VoCP & VoUP evaluation
MediaTek Inc., ZTE, vivo
S2-2506460

## Slide 2
VoCP vs VoUP*
MME
SGW
RAN
UE
Voice over CP
(one more routing hop: MME)
Voice over UP
Voice over | R19 Control-Plane | R19 User-Plane | R20 Control-Plane
NAS (CP) Hdr | 7 Bytes | -- | 1 Byte ?
RRC (CP) Hdr | 2 Bytes | -- | 0 Byte ?
PDCP (UP) Hdr | -- | 1 Byte | --
Compared Overhead ** | CP: 9B (0.9 Kbps) | UP: 1B (0.1 Kbps) | CP’: 1B? (0.1 Kbps)
Deployed? | Deployed | SPEC exist, Not Deployed | No SPEC, Not Deployed
Dilemma of “enhance Control Plane”
  A non-technical argument that CP is better is:
    R19 CP is deployed (to be precise, only NW supporting small in-frequent data transfer is deployed), while
    R19 UP is not deployed yet
  But technically the UP is much better (R19 CP has 9B header, R19 UP only 1B), so in order to make the CP catchup UP performance, dramatic 3GPP upgrade & dramatic deployment upgrade are needed to reduce the 9B to 1B, ex:
    CP optimization in SA3 & CT1 to reduce the NAS header size dramatically (e.g., delete Integrity protection for NAS msgs, remove NAS headers…); and
    CP optimization in RAN2 to delete RRC header (also, very likely to design a new (UM) SRB for voice, if separation of IMS Signalling and IMS voice on different bearer/QoS is needed)
  We think that:
    IF the dramatic 3GPP upgrade & dramatic deployment upgrade are done.
    INDEED the R20 CP performance can become comparable (not better) to R19 UP.
    BUT, the R20 CP NW is not the existing R19 CP NW, it’s a totally new NW, so the benefit of leveraging existing NW vanishes.
    THEREFORE, spend time to make R19 CP into R20 CP doesn’t make sense when a good enough R19 UP is already on hands.
Proposal
  In our view, dramatic 3GPP upgrade & deployment upgrade to currently deployed R19 CP cost more than to directly deploy a R19 UP, so….
    we suggest SA2 to agree to down-select the UP as way forward for voice transfer.
* IMS Signaling over CP or UP can be a separate topic
dramatic 3GPP upgrade & dramatic deployment upgrade
Same performance
** assume ptime=80ms
Background
  There are many decisions to be made for GEO voice, including "CP vs UP", "IP vs Non-IP", “SIP encoding vs non-SIP encoding ", "One Bearer or Two Bearers", "One PDN or Two PDNs"... etc, in our view we need to follow "divide&conquer“ approach to deal with them separately, otherwise the problems universe will grow exponentially and increase the risk for finishing work timely.
  This paper focus on analysis between voice over "CP vs UP", ignoring other orthogonal issues above, which are considered as noise for this topic.
Upper Layers: IP (RTP/UDP/IP)RoHC or Non-IP (Proprietary RTP): ooBytes
Lower Layers: RLC + MAC : xxBytes
CP
vs
UP