## Slide 1
3GPP TSG SA WG3 (Security) Meeting #75 S3-141010
12-16 May 2014; Sapporo(Japan)
Source: Alcatel-Lucent, NTT DoCoMo
Title: Discussion document on SECAM contribution framework
Agenda item: 7.13
V1.0

## Slide 3: Examples of threats from contributions
Contribution title | Threat description text | Threat | Threat Category
Threat from root owned files being altered by other users | If files owned by root can be changed by other system users they might severely alter the secure intended operation of the system | Modification of system files | Tampering with data
Threats from the compromised UE or misbehaving UE | MME can be denial-of-service attacked by a compromised or misbehaving UE | Denial of Service from compromised UE, misbehaving UE | Denial of Service
Threats of User Identities | Leakage of these user's identities can lead to loss of privacy | Disclosure of user identities | Disclosure of Information

## Slide 4: Examples of threats from contributions(2)
Contribution title | Threat description text | Threat | Threat Category
Security threats on MME user account and password management | default user password may be provided on MME and may not be modified in time | Unauthorised access | Unauthorised access
 | User password may have low level strength | Unauthorised access | Unauthorised access
 | The attacker may get user password, and not detected by legal user (password history) | Unauthorised access | Unauthorised access
 | user password storage | Disclosure of sensitive information | Disclosure of information
 | user can login from several computers at the same time. |  | 
 | use brute force to get passwords | Unauthorised access | Unauthorised access

## Slide 5
Threat Category | Tampering, Removal of Data, Denial of Service, unauthorised Access, Disclosure of information ….
Threat | High level or compound threat e.g. Denial of Service from compromised UE or a misbehaving UE
 | Detailed threat e.g Root owned files being altered by other users , Root able to log on from the network
Security Objectives | e.g. Protection of resource exhaustion, Protected Communications, Hardening, Secure Storage, Secure MME Administration, SW integrity, System Monitoring, Privacy…..
Requirements | e.g. The system should conform to industry best practices for password management and login controls including logon attempt limits, enforced password length and complexity, expiration date, password history, and secured password files The system should enforce password history rules for user password changes The umask for root is highly restricted
Test case | Check the umask setting for root, and that it is at least set to 027. Run industry-grade OS benchmarking tool to check OS settings

## Slide 6: Challenges
Consistency in description of threats in contributions
Level of detail in threats
Differentiating threats, objectives and requirements and implementation witin contribution
Level of detail in requirements
Agreement on what constitutes a threat category, threat, security objective, requirement

## Slide 7: Rules of framework
Use an existing threat before attempting to create new one.
Threats should not include security objectives nor requirements (not implementation details)
(Try)map threat to one of the existing categories.
Threat should map to one (or more) security objectives
All requirements should map to one or more threats.
All requirements should map to one or more security objectives.