## Slide 1: 3GPP TSG SA WG3 (Security) Meeting #SA3-NextGen S3-161306 27-29 September 2016; San Diego, US revision of Source: InterDigital Title: Discussion on NextGen Security Architecture Document for: Discussion Agenda Item: 4.1 – Security Architecture
Abstract: This presentation aims to start a discussion about the need for the target NextGen security architecture to be flexible, allowing on-demand association between Core Network (CN) and RAN, and replacing transfer of credential with derivation of credential

## Slide 2: Need for New NextGen Security Architecture
The singularity of the use cases in existing 3GPP communication systems (e.g., voice in GSM, circuit voice and packet data in UMTS, and eMBB in EPS) makes the simplicity and inelasticity of the current Authentication Architecture acceptable. Such inelasticity and lack of options made it easier to standardize the 2G-4G Authentication Architecture
The Next Generation (5G) system is projected to have at least the following three major use cases: eMBB, URCC, mMTC. These use cases draw out the diversity of different service requirements, some of which conflict with each-other in terms of services and security requirements
NextGen system is intended to support not only these use cases but other emerging use cases. The multiplicity of use cases in NextGen drives the need for a flexible Security Architecture and Authentication Framework
EAP framework has been proposed as a Security Architecture and Authentication solutions for NextGen systems.

## Slide 3: EAP-influenced Architectural Model
EAP security architecture allows for crypto-agility by providing the ability to select inner EAP authentication methods (e.g., AKA, AKA’, TLS)
It is still far too rigid and requires passing of root keys/key material from the AAA Server (e.g., HSS) to the EAP Authenticator (e.g., CP-AU / MME) and from the Authenticator to RAN.
Such a rigid security architecture makes the communication system vulnerable to attacks targeting the shared secrets, authentication vectors, etc.
Its inelasticity also makes recovery from such attacks cumbersome.
An extension of such an inflexible architecture into NextGen use cases (e.g., exposing the security architecture to 3rd parties for authentication of the UE) is difficult and likely to lead to an impractical NextGen system.

## Slide 4: Expanded EAP Architectural Model
ME
Authenticator
(MME)
AAA
(HSS)
Keys are derived
USIM
Supplicant
(UE)
NodeB
(eNB)
Root Key,
HO key material
Auth. Vector(s), Root keys
Keys and authentication material forwarded
Keys and authentication material forwarded
HO key material
HO Keys and authentication material forwarded
Root Key Derived (Kasme)
Rigid coupling
Rigid coupling
HO key material
HO Keys and authentication material forwarded
The Security Association (SA) established between the AAA Server (HLR HSS in EPS ) and Authenticator (MME in EPS) is static and based on contractual agreements between roaming MNOs or set up as default in a non-roaming use case.
Such a rigid security architecture makes the communication system vulnerable to attacks targeting the shared secrets, authentication vectors, etc.
Its inelasticity also makes recovery from such attacks cumbersome
Extension of such an inflexible architecture into NextGen use cases (e.g., exposing the security architecture to 3rd parties for authentication of the UE) is difficult and likely to lead to an impractical NextGen system.

## Slide 5: NextGen Security Architecture with Loose Coupling between Functional Elements
Authenticator
(Anchor)
AAA
Keys are derived
Supplicant
(NG-UE)
NodeB
(gNB)
Root Key Derivation
Root Key
Derivation
Root Key
Derivation
HO key material
Keys and authentication material derived
HO Keys and authentication material derived
Keys and authentication material derived
NodeB keys and authentication material derived
Loose coupling
Loose coupling
HO key material
HO Keys and authentication material derived
Replacement of static Security Associations between the AAA Server (HLR HSS in EPS) and Authenticator (MME in EPS) with a flexible SA based on cryptographic properties allows for better adaptability to the NextGen use cases, enhanced resistance to attacks targeting the shared secrets, authentication vectors, etc., and an increased ability to recover from such attacks.
The NextGen security architecture has to be flexible to allow on-demand association between Core Network (CN) and RAN. It also has to provide for key derivation without the need to transport keys or key material (that may allow an adversary to obtain the keys), between AAA and Authenticator/Security Anchor, Authenticator/Security Anchor and NodeB/gNB, and during eNB/Security Anchor handovers.