## Slide 1: LI solution related to privacy based on UE generated verification hash (VH)
Nokia
Anja Jerichow

## Slide 2
create SUCI with ECIES (input SUPI and R)
create verification hash
VH = hash (SUCI,SUPI,R)
Registration request (SUCI, VH)
Auth-info Req AV (SUCI)
SIDF: deconcealment of SUCI
Extract SUPI, R
create VH*=hash(SUCI, SUPI, R)
Auth-info Resp (AV, VH*)
VH =?= VH*
Reject registration request or
initiate Auth req (RAND, AUTN)
Inform if rejected
UE
SEAF
AUSF – UDM/ARPF
RES*
AKA verif. …
5G ACA (revealing SUPI, R)
Calculate VH‘ itself, compare with VH and if equal
continue with key derivation from KSEAF/KAMF
5G AC

## Slide 3: Justification of solution
agreed basic principles of any solution (S3-180457) | UE generated verification hash solution based on S3-180083
SUPI will not be sent if NAS confidentiality is off | SUPI never sent in clear; hidden in SUCI and in verification hash (VH) NAS SMC not touched, no need to differenciate between NAS confidentiality on/off, no additional key hierarchy in NAS needed, no extra NAS messages needed
Solution will include a hash of SUPI + something sent by the UE to the VPLMN | verification hash VH = hash(SUCI,SUPI,R) provides sufficient proof for SEAF/AMF to check against SUPI once provided by home network R being additional input parameter for SUCI encryption scheme and used with in VH for providing sufficient randomness in collision-resistant hash generation VH is sent to VPLMN, but VPLMN can only check against SUPI once additional info from HPLMN provided First step proof: HPLMN provides self-calculated VH* from deconcealed SUCI and R Second step proof for LI: preferably, only after successful authentication, HPLMN reveals (SUPI, R) to VPLMN, which can now calculate a VH‘ itself (and compare with VH as received from UE)
Hash mis-match shall lead to no service to the UE, i.e. UE is locked out (except for emergency calls) | HPLMN sends VH* at time of provisioning the 5G AV, if VH and VH* mis-match, UE is locked out For emergency calls, null-SUCI is used advantage, VPLMN and UE can stop authentication process immediately, no challenge/response between UE and SEAF anymore
Acceptable cryptographic strength to be considered | Solution provides sufficient strengh for the purpose, depending on R, appropriate length to be specified Strong cryptographic hash function to be chosen with proper output length, no collision within time frame of AKA possible (e.g. SHA-256) Strong random generator to be chosen

## Slide 4: Assumptions
SUPI only revealed to the SN after AKA has been successful
Full AKA run starts with 5G-AIR and ends with 5G-ACA
Thus, only after or within 5G-ACA the SUPI needs to be provided to the VPLMN -> it is suggested to integrate it into 5G-ACA
Hash by UE provides sufficient proof for LI if HN provides SUPI (see SA3-LI LS response in S3-171063)

## Slide 5: Discussion of attacks/comments raised against this solution
ERI: opportunity for HN to calculate collision: HN calculates VH* = hash(SUCI, SUPI, R) and finds the same hash with SUPI‘,R‘ as input. Then VN would provide SUPI’ to LEA
  Finding a collision with a strong collision-resistant hash function and a large search space (R) would need unlimited time available by a malicious home network to do an exhaustive search. It is highly unlikely that such attack opportunity would become ever true. Complexity of finding a (SUPI, R) is high enough such that it is not possible to do an exhaustive search 2^128 within the timer validity for the provided AV.
  SHA-256 is a collision-resistant, strong cryptographic hash function
  AKA needs to be finished within seconds (otherwise timer for AV usage expires), thus, this attack scenario is not justifiable
ERI: HN denies service by providing the wrong VH* to the visited network, this is misleading the SN and UE to be attracted by a different HN
  If the assumption of a HN to be malicious is valid, each of the solutions has such problems. HN simply needs to provide wrong AV to deny service
Other comment raised: Solution relies on the UE, HN and VN all supporting the same hash function. This seems to make it difficult to move onto a new algorithm in the future.
  HN=VN=any network, thus, any calculation happens between UE and 'any network' and requires an update at both sides for any new algorithm, this is not specific to the verification hash method
  Updating algorithms is the same problem in each solution

## Slide 6: Discussion of attacks/comments raised against this solution
KPN: prefer a solution where a failed verification would cause an error that under normal operation would lead to a termination or failure of the authentication or connection setup. That means that it is possible to by pass the code doing the comparison and continuing as normal, even if VH and VH* are not equal. It is therefore doubtful whether this solution will survive a court case.
  Why would a serving network do a code by-pass if the hash comparison fails?
  Verification hash solution, if integrated in the AKA protocol as suggested, is becoming normal operation. Thus it would cause an error at the SN, i.e. exactly when mis-match (VH=/=VH*) or, if HN would lie in the first step, e.g. by replaying the VH sniffed over the air, SN would latest when HN provides SUPI, R (collision is ruled out!) find out the mismatch and shall not reject the UE.
  Since all these comparisons are part of AKA with clear termination, there is no bypass possibility – except one would now change the trust model (being SN the malicious entity continuing communication while ignoring the mismatch).
  Why should a malicious HN send a VH* not matching, but providing a valid AV?
  If the SN is malicious, why would it store a SUPI reported from a honest HN?
  A malicious SN could also ignore an error in NAS SMC.
  Court case can only be envisioned, if communication has been extablished successfully, in which case the verification hash comparison and AKA was successful.

## Slide 7
UE
SEAF
AUSF
UDM/ARPF
1. Generate SUCI (input parameters: SUPI, R)
and verification hash VH = hash(SUCI||SUPI||R)
2. N1 registration request (SUCI, VH) or 5G-GUTI
3. N12 5G-AIR with SUCI, SUPI, or 5G-GUTI
4. Auth-info Requ (SUPI/SUCI)
Store SUCI, VH
If SUCI, then de-conceal by SIDF and retrieve parameters (SUPI, R)
Calculate VH* = hash(SUCI||SUPI||R)
Select authentication method
Generate 5G HE AV based on SUPI
5G HE AV = RAND, AUTN, XRES*, KAUSF (and VH*)
5. Auth-info Resp (5G HE AV) (with VH*)
Calculate HXRES* from XRES*
Calculate KSEAF from KAUSF
Generate 5G AV =RAND, AUTN, HXRES*, KSEAF
Provide 5G AV and VH* in 5G-AIA
6. N12 5G-AIA
VH =? VH*
Check expiry time
Store HXRES* from 5G AV
7. Reject if mis-match (specific error) or
Auth-Req with RAND, AUTN
7. Auth-Confirm-reject if VH =/= VH*
Calculate Auth-Resp
8. Auth-Resp (RES*)
AKA verification: calculate HRES* HRES* =? HXRES*
9. 5G-AC (RES*)
Verification
RES*=? XRES*
10. 5G-ACA (with SUPI, R)
SEAF calculates VH‘ itself, compares with VH and if equal,
continue with key derivation from KSEAF/KAMF,
otherwise reject (another specific error code)
5G AKA procedure including
verification hash to fulfill LI
but keep privacy of SUPI;
also applicable to EAP-AKA'

## Slide 8: Advantages
Simple procedure
Separation of LI from normal operation: dedicated handling by verification hash for LI only
SUPI is never sent in clear over the air
Immediate & early stop of registration procedure if mis-match
No choice/no different handling for NAS
Saving of message exchanges (no Auth-Req & 5G AC) in case of first mis-match detection
Always the same behaviour of UE and UDM if privacy is switched on
Crypto can be chosen of acceptable strength to avoid collision (e.g. SHA-256)
Applicable to 5G AKA and EAP-AKA'