## Slide 1
Discussion on providing AS security during RRC connection establishment to protect slice identity.
3GPP TSG SA WG3 (Security) Meeting #94 S3-190399
28 January – 1 February 2019, Kochi (India)

## Slide 2
0. Background
Agreement in Release 15 with regard to the NSSAI in Access Stratum
  NSSAI availability in AS layer has been concluded in the SA2 129bis meeting and the S2-1813059 was agreed.
  This SA2 agreement was achieved based on the instruction by the LS from SA3 S3-183659.
Summary of agreement in Release 15:
  5GC provides a flag to UE, when UE registers to the 5GS, indicating whether the NSSAI can be included in the AS messages or not.
  If UE is allowed and includes the NSSAI in the AS message, the NSSAI is referred by the RAN to perform the network slice specific RAN functions. For example, AMF selection based on the NSSAI and/or Slice congestion control at the RAN.
  If UE is NOT allowed and does not include the NSSAI in the AS message, all R network slice specific RAN functions are disabled.
Observation:
  There is a trade-off in release 15 whether operators to have the NSSAI security protection on AS layer OR to have the network slice specific RAN functions.
  Operators cannot get both. This is the limitation in Release 15.

## Slide 3
1. Requirements (1/2)
Requirements from security perspective:
  S-NSSAI shall be send encrypted in the AS and NAS (SA1 guidance [1]).
Requirements from RAN perspective:
  S-NSSAI(s) is required during the RRC connection establishment to perform slice related overload control at NG-RAN.
  S-NSSAI(s) is required during the RRC connection establishment for following RAN related function:
    To check slice availability:
      A slice may not be deployed homogeneously in the network. Therefore a NG-RAN needs slice information to check if the slice is available at the location.  See 38.413 Slice Support List IE in the NG setup response message.

## Slide 4
1. Requirements (2/2)
Resource management between slices
  NG-RAN supports policy enforcement between slices as per service level agreements. It should be possible for a single NG-RAN node to support multiple slices. The NG-RAN should be free to apply the best RRM policy for the SLA in place to each supported slice.
Resource isolation between slices
  the NG-RAN supports resource isolation between slices. NG-RAN resource isolation may be achieved by means of RRM policies and protection mechanisms that should avoid that shortage of shared resources in one slice breaks the service level agreement for another slice. It should be possible to fully dedicate NG-RAN resources to a certain slice. How NG-RAN supports resource isolation is implementation dependent.
Optimal AMF selection procedure
  S-NSSAI(s) are required at the NG-RAN to perform optimal AMF selection at NG-RAN.

## Slide 5
2. Observation and problem Statement
  As described in the background slide the Rel-15 specification at any given time either fulfil the SA plenary requirement to not send Slice identity (S-NSSAI) without encryption or the RAN requirement to send S-NSSAI during RRC Connection establishment but the S-NSSAI is sent in plain text in the msg 5 (RRC Connection Setup Complete).
  The Rel-15 specification DOES NOT fulfil the requirements from both SA plenary and RAN requirements. The operator CAN NOT implement SA plenary requirement and RAN requirement at the same time.

## Slide 6
3. Release 16 discussion in SA2#129bis
  NEC provided the discussion paper S2-1812156 in SA2#129bis in order remove the limitation, as stated in the background section, in Release 16.
  This is of NEC’s view that there are a few mechanisms to satisfy both Security related slice requirements on AS layer and RAN related slice requirements at the same time.
  The outcome of the SA2 discussion was to discuss and investigate this issue in SA3 first.

## Slide 7
4. Proposal
SA3 should agree to provide NSSAI protection in Release-16.
Two options to do so:
  Create a CR as living document
  Agreeing a WID that creates a TR capturing rationale and a CR to TS 33.501 as final deliverable
    CR as living document can be kept along side
Proposed timelines:
  Finish CR to TS 33.501 by SA#85
  WID option:
    Conclude TR by SA#84 as well
    Send TR for approval for SA#85
Conference calls will have to be held
NEC happy to take the lead

## Slide 8
5. WID option
The WID should focus on solutions that meet the SA plenary and RAN criteria:
  S-NSSAI shall be send encrypted in the AS and NAS.
  S-NSSAI(s) is required during the RRC connection establishment to perform slice related overload control at NG-RAN.
  S-NSSAI(s) is required during the RRC connection establishment for AMF selection by RAN.
We propose to limit the scope of the WID to:
  Studying solutions for authenticated UEs only, i.e. for those cases where AS or NAS security context is available.
  Not to study solutions that require round trips to the home network
Output of the WID should be a TR and a CR to 33.501
A companion contribution proposes the WID

## Slide 9
7. References
[1] LS from SA: SP-180914 “Guidance on initial NAS message protection”.
[2] LS from RAN2: R2-1816022 “Reply LS on initial NAS security agreements”.
[3] LS from SA2: S2-1811568 “Reply LS on initial NAS security agreements”.
[4] S2-1812156: Coexistence of the AS security and slice information in the RAN during the RRC connection establishment procedure