## Slide 1: Working assumptions for Release 16 WIs
SA3 Chairman

## Slide 2: Background
This document collects the working assumptions based on the moderated round of email discussions initiated by the rapporteurs
The procedure for the moderated email discussions is described in S3-20wxyz
The working assumptions are made based on the available solutions and the balance between the camps
The working assumptions are used to form the basis of working agreements should concensus not be reached during the meeting. Further details here.

## Slide 3: 4.8 Security of the enhancement to the 5GC location services
Open issue #1: SSID and Bluetooth device name format
  WA 1: the finial work of eLCS WID shall be based on the “draft_S3-200720-r2_merger_with_702_750” in the draft folder of the SA3#98Bis-e meeting

## Slide 4: 4.9 Security Aspects of the 5G Service Based Architecture (1/2)
Open issue #1: SCP verification in NRF when hop by hop security is used for consumer authentication
  WA 1: SA3 to specify a requirement for NRF that when there is no e2e NF consumer authentication, NRF to check whether the SCP that generated the Access Token Request, is authorized to do that on behalf of the NF consumer. This check is based on configuration (or something similar).
Open issue #2: End to End authentication by NRF
  WA 2: SA3 to develop solution in Rel-16 for e2e authentication of NF consumer in NRF - It is agreed that there is a need for an application layer e2e authentication of NF consumer by NRF.

## Slide 5: 4.9 Security Aspects of the 5G Service Based Architecture (2/2)
Open issue #3: End to End authentication by NF producer
  No WA.
Open issue #4: Access token ownership verification in NF producer
  WA 3: SA3 to develop a solution for verification of access token ownership in NF producer. If there is no consensus on any solution, access token ownership verification in NF producer will be pushed to Rel-17.

## Slide 6: 4.10 Authentication and key management for applications … (1/3)
Question #1.1: Is there a need for adding AKMA subscription data parameter of “whether AKMA is allowed” per subscriber? (Yes or no)?
  WA 1: There is a need for adding AKMA subscription data parameter of “whether AKMA is allowed” per subscriber.
Question#1.2: Is there a need mandating support in the UE of AKMA feature? (Yes or No)?
  WA 2: There is no need mandating support in the UE of AKMA feature.

## Slide 7: 4.10 Authentication and key management for applications … (2/3)
Question#2.1: Do we need to introduce selection mechanism for selecting AAnF?
  WA 3: There is no need to introduce selection mechanism for selecting AAnF.
Question #2.2: Does AAnF (set) need to keep AKMA key material (Yes or no)?
  WA 4: AAnF (set) needs to keep AKMA key material (with further clarification of whether AAnF is stateful or stateless).

## Slide 8: 4.10 Authentication and key management for applications … (3/3)
Question #3: Does AKMA need to have Ua* independent KAF key refresh mechanism?
  No WA.
Open issue #4: KAKMA materials generation time
  No WA.
Open issue #5: AUSF stores A-KID to UDM or AAnF
  No WA.

## Slide 9: 4.11 Evolution of Cellular IoT security for the 5G System
Open issue #1: Protection of UE capability transfer for UEs without AS security
  No WA.
Open issue #2: Input parameters to the calculation of shortResumeMAC-I
  WA 1: SA3 aligns with the outcome of RAN2 discussions taking any security issue into account.

## Slide 10: 4.14 Security for NR Integrated Access and Backhaul
Question #1: Whether Dynamic computation of PSK (KIAB) to be supported to enable deployments without pre-configuration?
  WA 1: Dynamic computation of PSK (KIAB) shall be supported for IKEv2 PSK based authentication method in Rel-16
Question #2: To protect F1-C traffic, whether DTLS to be supported or not?
  No WA.

## Slide 11: 4.16 Security Aspects of 3GPP support for Advanced V2X Services (1/2)
Question #1: Which granularity of the user plane security should be applied? (PC5 unicast link or Service?)
  WA 1: Security protection per PC5 unicast link.
Question #2: Which UE should indicate the configuration of confidentiality and integrity protection?
  No WA.

## Slide 12: 4.16 Security Aspects of 3GPP support for Advanced V2X Services (2/2)
Question #3: Which message should be used to notify the configuration of the confidentiality and integrity protection? (PC5-S or PC5-RRC)
  No WA.
Question #4: Shall we define a solution for group ID privacy or not?
  WA 2: No specific solution for destination ID privacy for group-cast in Rel-16.

## Slide 13: Going forward
Chairman to discuss status and possibly declare tentative working agreements during the conf call scheduled on the 14th of May
Companies are then welcome to indicate or withdraw their sustained objections until the last challenge deadline on the 15th of May
Following the last challenge deadline, the chairman upholds or reverts any working agreements depending on the outcome of (2)
A decision is then taken on the target document accordingly