| 3G CHANGE REQUEST | Please see embedded help file at the bottom of this page for instructions on how to fill in this form correctly. |
| --- | --- |
|  | TS 33.105 | CR | Xxx | Current Version: | 3.0.0 |  |
| 3G specification number ( |  | ( CR number as allocated by 3G support team |
| For submission to TSG | SA | for approval | X | (only one box should |
| list TSG meeting no. here ( | for information |  | be marked with an X) |
| Form: 3G CR cover sheet, version 1.0 The latest version of this form is available from: ftp://ftp.3gpp.org/Information/3GCRF-xx.rtf |
| Proposed change affects: | USIM |  | ME | X | UTRAN | X | Core Network |  |
| (at least one should be marked with an X) |
| Source: | SA3 | Date: |  |
| Subject: | Description of layer on which ciphering takes place |
| 3G Work item: | UTRAN Security |
| Category: | F Correction |  |  |  |  |
|  | A Corresponds to a correction in a 2G specification |  |  |  |  |
| (only one category | B Addition of feature |  |  |  |  |
| shall be marked | C Functional modification of feature | X |  |  |  |
| with an X) | D Editorial modification |  |  |  |  |
| Reason for change: | Description of the layer on which ciphering takes place is inserted following agreement on this with RAN2. |
| Clauses affected: | New clause 6.6.9.3 |
| Other specs | Other 3G core specifications |  | ( List of CRs: |  |
| affected: | Other 2G core specifications |  | ( List of CRs: |  |
|  | MS test specifications |  | ( List of CRs: |  |
|  | BSS test specifications |  | ( List of CRs: |  |
|  | O&M specifications |  | ( List of CRs: |  |
| Other comments: |  |

<--------- double-click here for help and instructions on how to create a CR.

### 6.6.9	Ciphering procedures

#### 6.6.9.1	Starting of the ciphering and deciphering processes

The MS and the RNC must co-ordinate the instants at which the enciphering and deciphering processes start.

This procedure takes place under the control of the network some time after the completion of the authentication procedure (if any), or after the key CK has been made available at the RNC.

No information elements for which protection is needed must be sent before the ciphering and deciphering processes are operating.

The transition from clear text mode to ciphered mode proceeds as follows: deciphering starts in the RNC, which sends in clear text to the MS a specific message, here called "Start cipher". Both the enciphering and deciphering start on the MS side after the message "Start cipher" has been correctly received by the MS. Finally, enciphering on the RNC side starts as soon as a frame or a message from the MS has been correctly deciphered at the RNC.

[diagram to be added]

#### 6.6.9.2	Synchronisation

The enciphering stream at one end and the deciphering stream at the other end must be synchronised, for the enciphering bit stream and the deciphering bit streams to coincide.

Synchronisation is guarantied by driving UEA by an explicit time variable, COUNT, derived from an appropriate frame number available at the MS and at the RNC.

The diagram below summarises the implementation indications listed above, with only one enciphering/deciphering procedure represented (the second one for deciphering/enciphering is symmetrical).

[diagram to be added]

#### Layer for ciphering

The layer on which ciphering takes place depends on the Layer 2 mode of the data.  Data transmitted on logical channels using a non-transparent RLC mode (either Acknowledged Mode or Unacknowledged Mode) is ciphered in the RLC sub-layer of Layer 2.  Data transmitted on a logical channel using the transparent RLC mode is ciphered at the MAC sub-layer of Layer 2.

#### 6.6.9.4	Handover

Note:	It is expected that in case of inter-operator handover a handover agreement exists that covers all charging aspects. Agreements on cipher key transportation/re-use shall also be included.

1)	Intra-system

When a handover occurs, the CK is transmitted within the system infrastructure from the old RNC to the new one to enable the communication to proceed, and the synchronisation procedure is resumed. The key CK remains unchanged at handover.

2)	Inter-system

The following functionality has to be provided.

2G and other 3G mobile communications systems ® UMTS

The UMTS network entered by the user handing over will enable integrity protection. This will involve setting the integrity protection key. There are two options:

a)	Establishing the cipher key CK (with UMTS key format) using the UMTS authentication and key agreement mechanism.

b)	Deriving of cipher key (with UMTS key formats) from the existing cipher key (e.g. GSM formats).

UMTS ® 2G and other 3G mobile communications systems

a)	Establishing the system specific security key (e.g. in case of GSM: cipher key Kc with GSM key format) using the system specific key agreement mechanisms.

b)	Deriving the system specific security keys (e.g. in case of GSM: cipher key KC with GSM key format) from the UMTS cipher key.