# 3GPP TSG SA WG3 Meeting #104-e Ad-hoc                      	S3-213378

# e-meeting, 27 – 30 September 2021	                         revision S3-21abcd

# Source:	Huawei, HiSilicon

# Title:	Add X.4 Protection of UE data in transit between NFs for Annex X

# Document for:	Approval

Agenda Item:	4.10

# Decision/action requested

This contribution proposes to add X.4 protection of UE data in transit between NFs for Annex X

# References

[1]			3GPP TR 33.866: Study on security aspects of enablers for Network Automation (eNA) for the 5G system (5GS) Phase 2

# Rational

This contribution propose to add the security mechanism for data transferred between NFs that has been concluded in TR33.866[1].

# Detailed proposal

*************** Start of 1st Change ****************

# X.4     Protection of UE data in transit between NFs

According to clause 13.1.0, all network functions shall support mutually authenticated TLS and HTTPS. TLS shall be used for transport protection within a PLMN unless network security is provided by other means. Thus, communication between NFs is integrity, confidentiality and replay protected.

NFs shall obtain an access token from NRF for requesting analytics from an analytics function or providing analytics data to the analytics function. *************** End of 1st Change ****************