3GPP TSG-SA3 Meeting #104-e- Ad-hoc 	draft_S3-213407-r1

# e-meeting, 27 – 30 September 2021										              Revision of S3-20xxxx

# Source:	Huawei, HiSilicon

# Title:	User consent check for Generic Requirements for adapting procedures related to user consent

# Document for:	Approval

Agenda Item:	4.9

# 1	Decision/action requested

SA3 is kindly requested to approve the proposed changes on clause user consent check.

# 2	References

[1]	TR 33.867 v0.6.0 “Study on User Consent for 3GPP services”

# 3	Rationale

TR 33.867[1] has concluded the generic requirement for the procedures about user consent check in clause 8.5.2. Therefore, the contribution proposes to specify the conclusion in the annex for user consent accordingly.

# 4	Detailed proposal

*************** Start of 1st Change ****************

# X.2		User consent check

Editor's Note: This clause will describe how to check of user consent in order to provide guideline that if a new use case needs to check of user consent.

The following procedures may be enabled based on local policies and regulations:

Whenever a service is invoked by a service consumer directly, the service provider shall retrieve the user consent parameters from the UDM unless the parameters are available in the local UE context. The service provider shall decide to provide the service for the service consumer based on the user consent parameters.

Editor’s Note: The text may be revised based on conclusion in TR 33.867.

Editor’s Note: How the service provider knows the data processing purpose is FFS.

*************** End of 1st Change ****************