# 3GPP TSG-SA3 Meeting #104e-Ad-hoc 	S3-213443-r1

# e-meeting, 27 – 30 September 2021, Online

# Source:	Huawei, HiSilicon

# Title:	EC: Authentication and Authorization between EEC and ECS

# Document for:	Approval

Agenda Item:	4.6

# 1	Decision/action requested

This contribution proposes add the Authentication and Authorization between EEC and ECS.

# 2	References

[1] TR 33.839 v040

# 3	Rationale

It is proposed to add the Authentication and Authorization between EEC and ECS.

# 4	Detailed proposal

It is suggested to approve the following changes.

***************************Start of change ****************************

# 2	References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

-	References are either specific (identified by date of publication, edition number, version number, etc.) or non-specific.

-	For a specific reference, subsequent revisions do not apply.

-	For a non-specific reference, the latest version applies. In the case of a reference to a 3GPP document (including a GSM document), a non-specific reference implicitly refers to the latest version of that document in the same Release as the present document.

[1]	3GPP TR 21.905: "Vocabulary for 3GPP Specifications".

[2]	3GPP TS 33.210: "3G security; Network Domain Security (NDS); IP network layer security".

[3]	3GPP TS 33.501: "Security architecture and procedures for 5G System".

[4]	3GPP TS 33.187: "Security aspects of Machine-Type Communications (MTC) and other mobile data applications communications enhancements".

[xx]	3GPP TS 23.558: "Architecture for enabling Edge Applications."

***************************End of change****************************

## 6.2	Authentication and Authorization between EEC and ECS

6.2.1 General

The detailed service procedures between EEC and ECS are described in the TS 23.558 [xx]. The authentication and authorization between them is described in the following clause.

### 6.2.2 Procedure for the Authentication and Authorization between EEC and ECS

Pre-requisite:

- The EEC is provisioned with a credential to authenticate the ECS.

- The EEC may be provisioned with a certificate to be authenticated the ECS.

NOTE1: The EEC certificate provisioning is out scope of this document.

Figure 8.3.3.2.2-1: Service provisioning – Request/Response

1. The EEC and ECS shall establish the TLS with the service-side authentication. If the EEC has the certificate, TLS with mutual authentication may be performed.

2. The EEC sends the service request to the ECS, which may include the GPSI.

3. The ECS should authorize the EEC by its local authorization policy..

If the GPSI is received from the EEC, the ECS should verify the correctness of the  GPSI of the UE.

Editor’s Note: GPSI verification is to be added.

If the authorization success, the ECS processes the request.

4. The ECS sends the service response back the EEC.

***************************End of change****************************