3GPP TSG-SA3 Meeting #50 	(S3-080246

# Sanya, China, 25-29 February 2008

| CR-Form-v9.4 |
| --- |
| CHANGE REQUEST |
| ( | 33.203 | CR | 0126 | ( rev | 1 | ( Current version: | 8.1.0 | ( |
| For HELP on using this form look at the pop-up text over the ( symbols. Comprehensive instructions on how to use this form can be found at http://www.3gpp.org/specs/CR.htm. |

| Proposed change affects: ( | UICC apps( | x | ME | x | Radio Access Network |  | Core Network | x |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: ( | Introduction of support for 3GPP2 IMS Access Security |
| --- | --- |
| Source to WG: ( | Qualcomm Europe |
| Source to TSG: ( | SA WG3 |
| Work item code: ( | IMS-Sec |  | Date: ( | 16/01/2008 |
| Category: ( | B |  | Release: ( | Rel-8 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: R99 (Release 1999) Rel-4 (Release 4) Rel-5 (Release 5) Rel-6 (Release 6) Rel-7 (Release 7) Rel-8 (Release 8) Rel-9 (Release 9) |
| Reason for change: ( | At the joint 3GPP and 3PP2 workshop it was agreed that the Common IMS will include the cdma2000 access networks.This CR introduces text related to IMS access security from S.S0086-B to TS 33.203 as part of Common IMS. |
| Summary of change: ( | New Annex X is introduced for IMS access security from S.S0086-B to add support for use of IMS in cdma2000 networks. Additions to scope, references, definitions and abbreviations section to support cdma2000 access networks. |
| Consequences if ( not approved: | The Common IMS will not include IMS security related specification required for using IMS over cdma2000 access networks. |
| Clauses affected: ( | 1, 2, 3, Annex X (new) |
|  | Y | N |  |  |
| Other specs ( | Y |  | Other core specifications ( | TS 24.229 (3GPP2 X.S0013-004), TS 23.228 (3GPP2 X.S0013-002), TS 33.210 |
| affected: |  |  | Test specifications |  |
|  |  |  | O&M Specifications |  |
| Other comments: ( | This CR should be considered for approval along with the companion CR to TS 33.210 |

### *******************Begin Changes******************

# 1	Scope

The scope for this technical specification is to specify the security features and mechanisms for secure access to the IM subsystem (IMS) for the 3G mobile telecommunication system.

Since the scope also encompasses the use of these security features and mechanisms for secure access to IMS in the context of fixed broadband networks, and cdma2000 networks, Annex L and Annex X specify how the material in the main body and other normative Annexes of this document apply to the fixed broadband networks, and cdma2000 networks, respectively.

The IMS supports IP Multimedia applications such as video, audio and multimedia conferences using SIP, Session Initiation Protocol, as the signalling protocol for creating and terminating Multimedia sessions, cf. RFC 3261 [6]. This specification only deals with how the SIP signalling is protected between the subscriber and the IMS, how the subscriber is authenticated and how the subscriber authenticates the IMS.

### *******************Next Change******************

# 2	References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

- References are either specific (identified by date of publication, edition number, version number, etc.) or non-specific.

- For a specific reference, subsequent revisions do not apply.

- For a non-specific reference, the latest version applies. In the case of a reference to a 3GPP document (including a GSM document), a non-specific reference implicitly refers to the latest version of that document in the same Release as the present document.

[1]	3GPP TS 33.102: "3rd Generation Partnership Project; Technical Specification Group Services and System Aspects; 3G Security; Security Architecture".

[2]	3GPP TS 22.228: "3rd Generation Partnership Project; Technical Specification Group Services and System Aspects; Service Requirements for the IP Multimedia Core Network".

[3]	3GPP TS 23.228: "3rd Generation Partnership Project; Technical Specification Group Services and System Aspects; IP Multimedia (IM) Subsystem".

[4]	3GPP TS 21.133: "3rd Generation Partnership Project; T Technical Specification Group Services and System Aspects; Security Threats and Requirements".

[5]	3GPP TS 33.210: "3rd Generation Partnership Project; Technical Specification Group Services and System Aspects; 3G Security; Network domain security; IP network layer security".

[6]	IETF RFC 3261 "SIP: Session Initiation Protocol".

[7]	3GPP TS 21.905: "3rd Generation Partnership Project: Technical Specification Group Services and System Aspects; Vocabulary for 3GPP specifications".

[8]	3GPP TS 24.229: "3rd Generation Partnership Project: Technical Specification Group Core Network; IP Multimedia Call Control Protocol based on SIP and SDP".

[9]	3GPP TS 23.002: "3rd Generation Partnership Project: Technical Specification Group Services and System Aspects, Network Architecture".

[10]	3GPP TS 23.060: "3rd Generation Partnership Project: Technical Specification Group Services and System Aspects, General Packet Radio Service (GPRS); Service Description".

[11]	3GPP TS 24.228: "3rd Generation Partnership Project: Technical Specification Group Core Network; Signalling flows for the IP multimedia call control based on SIP and SDP".

[12]	IETF RFC 2617 (1999) "HTTP Authentication: Basic and Digest Access Authentication".

[13]	IETF RFC 2406 (1998): "IP Encapsulating Security Payload (ESP)".

[14]	IETF RFC 2401 (1998): "Security Architecture for the Internet Protocol".

[15]	IETF RFC 2403 (1998): "The Use of HMAC-MD5-96 within ESP and AH".

[16]	IETF RFC 2404 (1998): "The Use of HMAC-SHA-1-96 within ESP and AH".

[17]	IETF RFC 3310 (2002): "HTTP Digest Authentication Using AKA". April, 2002.

[18]	IETF RFC 3041 (2001): "Privacy Extensions for Stateless Address Autoconfiguration in IPv6".

[19]	IETF RFC 2402 (1998): "IP Authentication Header".

[20]	IETF RFC 2451 (1998): "The ESP CBC-Mode Cipher Algorithms".

[21]	IETF RFC 3329 (2003): "Security Mechanism Agreement for the Session Initiation Protocol (SIP)".

[22]	IETF RFC 3602 (2003): "The AES-CBC Cipher Algorithm and Its Use with IPsec".

[23]	IETF RFC 3263 (2002): "Session Initiation Protocol (SIP): Locating SIP Servers".

[24]	3GPP TS 33.310: "3rd Generation Partnership Project; Technical Specification Group Services and System Aspects; Network Domain Security (NDS); Authentication Framework (AF)".

[25]	3GPP TR 33.978: "3rd Generation Partnership Project; Technical Specification Group Services and System Aspects; 3G Security; Security Aspects Of Early IMS".

[26]	ETSI ES 282 001: "TISPAN - Telecommunications and Internet converged Services and Protocols for Advanced Networking (TISPAN); NGN Functional Architecture for NGN Release 1".

[27]	IETF RFC 3947 (2005): "Negotiation of NAT-Traversal in the IKE".

[28]	IETF RFC 3948 (2005): "UDP Encapsulation of IPsec ESP Packets".

[29]	IETF RFC 3323 (2002): "A Privacy Mechanism for the Session Initiation Protocol (SIP)".

[30]	IETF RFC 3325 (2002): "Private Extensions to the Session Initiation Protocol (SIP) for Asserted Identity within Trusted Network".

[31]	3GPP TS 23.167: "3rd Generation Partnership Project; Technical Specification Group Services and System Aspects; IP Multimedia Subsystem (IMS) emergency sessions”.

[32]	draft-ietf-sip-outbound-10 (July 2007): "Managing Client Initiated Connections in the Session Initiation Protocol (SIP)".

Editor's note: The above document cannot be formally referenced until it is published as an RFC.

[33]	IETF RFC 3268 (2002): "Advanced Encryption Standard (AES) Ciphersuites for Transport Layer Security (TLS)".

[34]	IETF RFC 2246 (1999): "The TLS Protocol Version 1.0".

[35]	RFC 3280 "Internet X.509 Public Key Infrastructure Certificate and Certificate Revocation List (CRL) Profile".

[aa]	3GPP2 X.S0011: "cdma2000  Wireless IP Network Standard".

[ab]	3GPP2 C.S0023: "Removable User Identity Module for Spread Spectrum Systems".

[ac]	3GPP2 C.S0069: "ISIM Application on UICC for Spread Spectrum Systems".[ad]                      3GPP2 S.S0055: "Enhanced Cryptographic Algorithms".

[ae]                      3GPP2 S.S0078: "Common Security Algorithms".

### *******************Next Change******************

# 3	Definitions, symbols and abbreviations

## 3.1	Definitions

For the purposes of the present document, the following terms and definitions apply.

Authenticated (re-) registration: A registration i.e. a SIP register is sent towards the Home Network which will trigger a authentication of the IMS subscriber i.e. a challenge is generated and sent to the UE.

Authentication vector: A quintet (as defined in TS 33.102 [1]) or an SD-AV.

Confidentiality: The property that information is not made available or disclosed to unauthorised individuals, entities or processes.

Data integrity: The property that data has not been altered in an unauthorised manner.

Data origin authentication: The corroboration that the source of data received is as claimed.

Entity authentication: The provision of assurance of the claimed identity of an entity.

Key freshness: A key is fresh if it can be guaranteed to be new, as opposed to an old key being reused through actions of either an adversary or authorised party.

ISIM – IM Subscriber Identity Module: For the purposes of this document the ISIM is a term that indicates the collection of IMS security data and functions on a UICC. The ISIM may be a distinct application on the UICC.

Security Domain: Networks that are managed by a single administrative authority.  Within a security domain the same level of security and usage of security services will be typical.

SIP Digest authentication vector (SD-AV) : Temporary authentication data that enables the IMS network to engage in SIP Digest with a particular user. An SD-AV consists of five elements: a) protection space user hint realm, b) protection space domain, c) the authentication algorithm, d) the quality of protection value qop and e) the hash of IMPI, realm and password H(A1).

Editor's Note: The inclusion of the domain parameter in the SD-AV is ffs.

## 3.3	Abbreviations

For the purposes of the present document, the following abbreviations apply, TS 21.905 [7] contains additional applicable abbreviations:

AAA	Authentication Authorisation Accounting

AKA	Authentication and key agreement

AS	Application Server

AV	Authentication Vector

CSCF	Call Session Control Function

HN	Home Network

HSS	Home Subscriber Server

IBCF	Interconnection Border Control Function

IM	IP Multimedia

IMPI	IM Private Identity

IMPU	IM Public Identity

IMS	IP Multimedia Core Network Subsystem

ISIM	IM Services Identity Module

MAC	Message Authentication Code

ME	Mobile Equipment

NAPT	Network Address and Port Translation

NAT	Network Address Translation

R-UIM	Removable User Identity Module

SA	Security Association

SEG	Security Gateway

SD-AV	SIP Digest Authentication Vector

SDP	Session Description Protocol

SIP	Session Initiation Protocol

TLS	Transport Layer Security

UA	User Agent

UE	User Equipment

### *******************Next Change******************

Annex X (Normative):
Application to cdma2000 networks

## X.1	Introduction

This annex specifies how the material in the main body and other normative annexes of this document apply to the cdma2000 networks. In case there is a conflict with another annex of this document, then the requirements in this annex shall override. The IP Connectivity Access Network (IP-CAN) for cdma2000 networks, called Packet Data Subsystem (PDS), is defined in [aa].

## X.2	Application of clause 4

In the cdma2000 networks, the IMS is essentially an overlay to the PDS and has a low dependency on the PDS. PDS can be deployed without the multimedia session capability. The IMS Security Framework is shown in Figure X.1.

IMS authentication keys and functions at the user side may be stored in some secure memory location on an UE according to the requirements in clause X.4. It shall be possible for the IMS authentication keys and functions to be logically independent to the keys and functions used for PDS authentication. However, this does not preclude common authentication keys and functions from being used for IMS and PDS authentication.

The IMS Security Framework also addresses the security of interfaces between the IMS and external network domains, for example, Multimedia IP-Networks as shown in Figure X.1. This is important since the service capability subsystem of the IMS includes application servers that reside on untrusted third-party networks, and which can access network functionality.

Figure X.1: The IMS security architecture

There are seven different security associations and different needs for security protection for IMS (including SIP AS nodes) and they are numbered 1 through 7 in Figure X.1.

1.	Provides mutual authentication between the UE and the S-CSCF. The HSS delegates the performance of subscriber authentication to the S-CSCF. However the HSS is responsible for generating keys and challenges. The long-term key in the secure memory of the UE and the HSS is associated with the user private identity (IMPI). The UE will have one (network internal) user private identity (IMPI) and at least one external user public identity (IMPU).

The security associations 2 through 5 are as defined in clause 4 except that requirements in Annex Y of TS 33.210 [5] shall apply for security protection.

6.   Provides security between a SIP-capable node residing in an external IP network, and the HSS. This security association is covered in Annex Y of TS 33.210 [5].  The SIP-capable node is a SIP Application Server and may also reside within the HN.  However, this security assoication is only applicable when the SIP AS resides in an external IP network.  If the SIP AS resides in the Home Network, then the security association 3 applies.

7.   Provides security between SIP-capable nodes located in different networks.  It differs from security association 4 in that the SIP-capable node here is the SIP Application Server.  Using SIP, this type of application server may communicate with network entities to offer service control and content, access functionality provided in the operator’s network, and manage bearers.  This security association is covered in Annex Yof TS 33.210 [5].  It is only applicable when the SIP AS resides in an external IP network.  If the SIP AS resides in the Home Network, then security association 5 applies.

There may exist other interfaces and reference points in IMS, which have not been addressed above. Those interfaces and reference points reside within the IMS, either within the same security domain or between different security domains. Annex Y of TS 33.210 [5] is intended to address security issues for all such interfaces. This document assumes that the IP-CAN supports secure communications via standard IETF protocols [14].

Mutual authentication shall be required between the UE and the HN.

The confidentiality and integrity protection for SIP-signaling is provided in a hop-by-hop fashion. The first hop i.e. between the UE and the P-CSCF is specified in clause X.3. The other hops, inter-domain and intra-domain are specified in Annex Y of TS 33.210 [5].

## X.3	Application of clauses 5 through 8

The user’s subscription is authenticated by the S-CSCF (home service provider). The security association between the UE and the first access point into the operator’s network (P-CSCF) is negotiated based on the protocol defined in RFC 3329 [21]. The options that may be negotiated using [21], which are defined in 3GPP specifications, are: tls and ipsec-3gpp. If the negotiated protocol is ipsec-3gpp and no NAT device is present between the UE and the P-CSCF then clauses 5 through 8 of the main body of this document shall apply. If the negotiated mechanism is “ipsec-3gpp” and a NAT device is present between the UE and the P-CSCF, then Annex M of this specification shall apply. If the negotiated mechanism is tls then Annex O of this specification shall apply.

NOTE1: RFC 3329 [21] also allows to negotiate the mechanisms digest, ipsec-ike, and ipsec-man for use between UE and P-CSCF. They are defined in SIP RFC 3261 [6].

NOTE2: RFC 3329 only defines the security mechanisms between the SIP client and the next-hop SIP entity, i.e. the P-CSCF. In particular, if SIP Digest is negotiated by means of RFC 3329 then Digest has to be run between UE and P-CSCF, with the P-CSCF acting as the server. So, RFC 3329 cannot be used to negotiate SIP Digest authentication in IMS, which occurs between UE and S-CSCF.

When using security mechanisms or protocols specified in this document (including ipsec-3gpp), the following exceptions shall apply:

-	The clause 8 on ISIM/USIM is replaced with the secure memory requirements in clause X.4 and the references to ISIM/USIM is replaced with secure memory.

-	The cdma2000 AKA algorithms are as specified in [ag] and [ah].

-	The references to TS 33.210 are replaced with requirements in Annex Y of TS 33.210 [5].

-	When no ISIM is present, the IMS identities (e.g., IMPI/IMPU) shall be derived from the Mobile Station Identity (MSID) used to access cdma2000 access networks as specified in Annex M of [8]. The MSID can be either IMSI or Mobile Indentification Number (MIN).

Editor’s note: Due to the following output from the C-IMS workshop (slide 7 of S3-080218)

  - “The workshop concluded it was appropriate to document in 3GPP specifications the data and the derivation of the data used in the various security process, but not the physical storage of that data”

the following text was controversial and hence could not be agreed

## X.4	Secure Memory within UE

For the purposes of this annex, the secure memory includes the collection of IMS security data and functions on a UE.

### X.4.1	Requirements on the Secure Memory of an IMS Capable UE

This clause identifies requirements on the secure memory to support IMS access security. It does not identify any data or functions that may be required on the secure memory for non-security purposes.

The secure memory shall include:

-	The IMPI;

-	At least one IMPU;

-	Home Network Domain Name;

-	Support for sequence number checking in the context of the IMS Domain;

-	The same enhanced AKA algorithms as specified in [ad] and [ae] for the secure memory;

-	An authentication key.

At UE power off, the existing SAs (session keys and related information) shall be deleted.

The IMS security data and functions described in this clause may be provided by an UIM, R-UIM [ab] or an ISIM [ac].

### *******************End Changes******************

# Comments

Document numbers are allocated by the Working Group Secretary.   Use the format of document number specified by the 3GPP Working Procedures.

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.  It consists of at least four digits, padded with leading zeros if necessary.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR was written and (normally) to which it will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to  http://www.3gpp.org/specs/specs.htm.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

SIM / USIM / ISIM applications.

Enter a concise description of the subject matter of the CR. It should be no longer than one line, but if this is not possible, do not enter hard new-line characters.  Do not use redundant information such as "Change Request number xxx to 3GPP TS xx.xxx".

One or more organizations (3GPP Individual Members) which drafted the CR and are presenting it to the Working Group.

For CRs agreed at Working Group level, the identity of the WG.  Use the format "xn" where 
	x = "C" for TSG CT, "R" for TSG RAN, "S" for TSG SA, "G" for TSG GERAN; 
	n = digit identifying the Working Group; for CRs drafted during the TSG meeting itself, use "P". 
Examples: "C4", "R5", "G3new", "SP".

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, A, B & C CRs for Release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See 
http://www.3gpp.org/ftp/Specs/html-info/WI-List.htm .

Enter the date on which the CR was last revised.  Format to be interpretable by English version of MS Windows ® applications, e.g. 19/02/2006.

Enter a single letter corresponding to the most appropriate category listed. For more detailed help on interpreting these categories, see Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR were to be rejected. It is mandatory to complete this section only if the CR is of category "F" (i.e. correction), though it may well be useful for other categories.

Enter the number of each clause which contains changes.   Be as specific as possible (ie list each subclause, not just the umbrella clause).

Tick "yes" box if any other specifications are affected by this change.  Else tick "no".  You MUST fill in one or the other.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.