## Slide 1
3GPP TSG-SA3 Meeting #67 S3-120455
Kyoto, Japan, 21-25 May 2012
Source: Nokia Corporation, Nokia Siemens Networks
Presentation for discussion
Agenda Item: 8.8
Spoofed Call detection and prevention –
Problems related to Calling Line Identification

## Slide 2
Technical background for Calling Line Identification
Possibilities of abuse
Commercial offerings
Legal aspects
Standardisation aspects
Suggested way forward
Table of Contents

## Slide 3
Calling Line Identification (CLI or CLID), also called Caller Identification (CID) or Calling Line Identity Presentation (CLIP) transmits and displays a caller’s number during call setup or ringing
Usual applications for CLI are for example:
  to display the original number of the user
to display a user’s presentation number, e.g. a doctor calling a patient out of hours who doesn’t want to disclose his private number but showing instead the number of his office
  to display any number: call centers acting on behalf of their customers (depending on national regulations)
  but: CLI can also be misused by means of CLI spoofing ranging from harmless to illegal, e.g.
  testing responsiveness of callee depending on presented caller’s number
  for Voice Phishing (Vishing) by displaying the forged number of a bank in order to steal user credentials (illegal)
More widespread use of VoIP running via public Internet has raised concerns about the reliability of CLI
Although CLI may be unreliable people use it to decide whether to accept a call or not
Problems related to CLI Introduction

## Slide 4
User Network
Calling Party Information provided  can verify that the number is within the user’s range
Calling Party Information not provided  provide the user’s default number
Special arrangement  no screening shall be performed
Problems related to CLI CLI on Protocol Level
CLI is handled by SS7 protocol for inter-telco-switch communication by means of the ‘Calling Number Party Information Element’ (according to Q.931, chapter 4.5.10)
Presentation Indicator
00: Presentation allowed {CLIR* not activated}
01: Presentation restricted {CLIR* activated}
10: Number not available due to interworking
11: Reserved
Screening Indicator
00: User-provided, not screened
01: User-provided, verified and passed
10: User provided, verified and failed
11: Network-provided
Calling Number Party Information Element
* Calling Line Identification Restriction

## Slide 5
Problems related to CLI Trustworthiness of CLI?
PABX
leased
lines
Private network of a corporation spreading over different sites and countries and using their own leased-line network
site 1,
country 1
site 3,
country 3
site 2,
country 2
GW
GW
prefix calling card service
Problems related to PABXs may be
that the corporation may provide a generic CLI for all (maybe thousands) connected callers
that corporation may route calls from multiple sites in different countries (with many different CLI values) via their own network to the cheapest public network access point. In this case the GW would need to verify every CLI value against a remote database (not practicable)
that the CLI value provided by a PABX may be spoofed by anyone able to reprogram the PABX because PABXs will often be trusted (see bullet before)
Prefix calling card services may not transmit the CLI of the original phone
GW
GW

## Slide 6
Problems related to CLI Trustworthiness of CLI?
GW
GW
operator not verifying CLI values
Problems related to VoIP networks may be
A VoIP-originated call could be traced back to the GW where it entered the mobile network. That GW could hold details about the caller but that could be an P-Asserted-Id (if available) or a SIP URI in case of VoIP
VoIP calls may be given a CLI of the user’s own choice
Calls may be assigned a CLI of a specific geographical number
CLI spoofing is the same problem as discussed with PABXs except that no expensive HW is required
As there is no general requirement of telco-GWs to reject incorrect CLIs, CLI can be spoofed by means of suitable programs, e.g. asterisk program emulating a PABX, if the operator does not verify CLIs
GW
GW
phone client
+ asterisk*
* Linux program emulating a PABX enabling to set CLI values
GW
PC +
phone client
VoIP network

## Slide 7
Commercially offered CLI spoofing have been available e.g. in the US at least since 2004. Today several companies offer a CLI spoofing service, e.g. SpoofCard (refer to web page from 2012-05-08).
Problems related to CLI CLI Spoofing – commercial offerings for fixed networks
Besides CLI spoofing, companies usually offer two more kinds of services, cf. example of SpoofCard:

## Slide 8
CLI spoofing - How does it work?
Problems related to CLI CLI Spoofing – commercial offerings for fixed networks
call your CLI spoofing service provider
insert your own phone number
insert the callee’s number
insert the CLI to display
ensure that sufficient credits are available
make the spoof call
(Apps for smartphones already available)
CLI spoofing services are often paid with credits
A realistic example:
~ 10$ for 60 credits
e.g. credits per minute for US calls: 1  ~ 16 cents/minute
e.g. credits per minute for US to German calls: 1 (fixed line), 3 (mobile)
large list of countries supported
 seems to expensive for bulk SPIT campaigns

## Slide 9
Problems related to CLI Potential Usages of CLI Spoofing
most commonly used example (mentioned at nearly all CLI spoofing services): business professionals such as doctors can return calls using their personal phones without disclosing their phone numbers which they prefer to keep private, but showing instead the number of their office
supervision or hoax in the personal sphere (may be harmless)
SPIT advertisement calls with wrong CLIs so that the originator cannot be traced back (in some countries illegal)
stalking with frequently varying presentation numbers to circumvent blacklists (illegal)
formerly possible: hack the voice-mail account of celebrities by calling their own number and spoofed own CLI (possible if voice mail account is not protected by a password and redirect to own voice mail is based on CLI) (illegal)
Voice Phishing (Vishing) by spoofing the original phone number of a bank and perhaps playing the original announcement of a bank in order to steal user credentials (illegal)

## Slide 10
Problems related to CLI Legal Aspects of CLI Spoofing
Is CLI spoofing illegal ?
No and yes, depends on the country and the usage of CLI spoofing services
What is done by the CLI spoofing service providers to prevent illegal usage?
  sensitive numbers like for example emergency numbers (US: 911) are blocked
legality is handled in contract conditions or FAQs with usual conditions being:
# users are responsible for legal usage (it is generally mentioned that CLI spoofing, voice disguising and call recording may be not allowed in all states or countries but without giving concrete information or instructions)
# personal data of users is kept secret unless publishing is enforced by law enforcement agencies
What is done by the authorities?
CLI spoofing may be illegal or not, depending on national legislation

## Slide 11
Problems related to CLI How is 3GPP affected ? (1)
Existing standardisation
TS 23.081 Annex A defines mapping rules of CLI parameters received via the NW-NW interface to CLI parameters to be sent to the MS.
Origin of problems is wider than just 3GPP networks and relates to ISUP also used in fixed PSTN.
TS 29.163 specifies the mapping of ISUP to IMS.
(refer to TS 29.163, clause 7.2.3.1.2.6 ‘Calling Party Number’, clause 7.2.3.1.2.7 ‘Generic Number’ and clause 7.2.3.2.2.3 ‘P-Asserted ID, From and Privacy header fields’)
 Cooperation with 3GPP CT3 (interworking) and 3GPP CT4 (CS domain) would be beneficial
As ISUP is under the control of ITU cooperation with ITU may be potentially useful for suggestions how to address CLI spoofing that could be included in 3GPP specs.

## Slide 12
Problems related to CLI How is 3GPP affected ? (2)
Possible solutions inside 3GPP networks
  the terminating network may solve the problem by accepting CLI values only from trusted networks
  only CLIs with Screening Indicators ‘Network provided’ or ‘User-provided, verified and passed’ may be forwarded to the terminal, others are discarded
Specification vs. operation
  Is new normative work required, or is this more a question of security configuration and operations?

## Slide 13
Suggested way forward
SA3 is asked to
take into account and further discuss the technical background presented here;
further clarify the role of 3GPP in general and SA3 in particular wrt this SID;
clarify the question ‘specification vs. operation’;
consider involving other 3GPP WGs, e.g. CT3 and CT4;
consider involving ITU as the owner of the ISUP standard (maybe at a later stage).