## Slide 1
Source:
Tim Woodward
Motorola Solutions
tim.woodward@motorolasolutions.com
+1-480-966-2688
R14 eMCPTT security
3GPP TSG SA3 MCSEC teleconference S3-170103
26 January 2017

## Slide 2: MCPTT enhancements and their security impacts
Two types of ‘Ambient listening’ call
Temporary group call – regroup call
Remotely initiated call
First to answer call
Enhanced MCPTT group call setup procedure with MBMS bearer

## Slide 3: Two types of ‘Ambient listening’ call
Initiated by 3rd party
  Authorized 3rd party “invites” target UE to a private or group call with no visible or audible indication at target UE.
    Private call: Authorized user initiates call with a PCK.
    Group call: Authorized user initiates call with GMK-ID and group ID.
    NO SECURITY IMPACT to call setup
  “Self initiated” by user on target UE
  User self initiates a private or group call without visible or audible indication at target UE.
    Private call: Target UE initiates call with a PCK.
    Group call: Target UE initiates call with GMK-ID and Group ID.
    NO SECURITY IMPACT to call setup
However, does ambient listening command require end to end protection?
  Actual command or parameter that instructs target UE to start a ambient listening call should be end to end protected from auth user to target UE.
  Stick ambient listening “flag” into MIKEY-SAKKE payload?

## Slide 4: Remotely initiated call
A remotely initiated MCPTT call allows an authorized user to cause a remote MCPTT UE to initiate a private or group call by itself, without its user explicitly initiating the call.
  Private call: Remote UE initiates call with a PCK.
  Group call: Remote UE initiates call with GMK-ID and group ID.
  NO SECURITY IMPACT to call setup.
  However, new message “remotely initiated MCPTT call request” must be secured.
  CSK protection of routing identities (authorized user and target UE).
  End to end encryption of command on remote UE’s public encrypt key.
  Signed with Auth user’s IBE private signing key
  Does message need end to end protection of the parameter?
    Stick remotely initiated “flag” into MIKEY-SAKKE payload?

## Slide 5: First-to-answer call setup
The flow may use a floor request in the MCPTT call request indicating that the originator will be given the floor when the call starts and eliminates the need for a separate initial floor request message during media plane establishment.
Alternatively the call initiation may be sent without the floor request, which allows the called party to request the floor first. For a MCPTT first-to-answer call without floor control, floor control is not established.
This feature requires a method to identify and distribute the key to be used in the call.
  Initiating user provides a list of users in the invite and needs private call security between the initiating UE and the UE that responds first.
  It might be possible to have each answering UE provide a PCK in the invite response and use the PCK from the first UE to answer.
  Could send multiple PCKs in the initial first-to-answer invite from the initiating UE as long as the list of users is small.

## Slide 7: Enhanced MCPTT group call setup procedure with MBMS bearer
When the MCPTT server initiates a new MCPTT call, the MCPTT server shall decide to use unicast bearers or broadcast bearers for the downlink media.
When using an MBMS bearer for application level control signalling, the announcement of an already active MBMS bearer could be part of the MCPTT group call setup.
The procedure can be used in the following scenarios
  Initiate a new call on unicast bearer
  Transfer an ongoing call from broadcast bearer to unicast bearers
  Pre-condition: There must be an active and announced MBMS bearer

## Slide 8
Instead of multicast, use unicast
Multicast call setup but use unicast for media.
Move ongoing call from multicast to unicast.
B
A
C

## Slide 9: Enhanced MCPTT group call setup procedure with MBMS bearer
Figure 10.10.6.2-1: Application Group paging over an MBMS bearer
(Scenario C)

## Slide 10: Enhanced MCPTT group call setup procedure with MBMS bearer
Instead of multicast, use unicast.
  So don’t send MBMS bearer announcement?
  Floor control is unicast (KFC), media is unicast (GCK).
Multicast call setup but use unicast for media.
  Send MBMS bearer announcement (MSCCK) to all UEs, then send call setup on multicast channel (MKFC). Media is sent unicast (GCK).
Move ongoing call from multicast to unicast.
  (from previous slide) MCPTT server sends “application group paging message”.
  MCPTT server and UE moves back to unicast for floor control (KFC) and unicast media (GCK).
Moving a UE from one MBMS bearer to another while engaged in a call.
  Send new MBMS bearer announcement (MSCCK) to UE?
  MCPTT server needs to know UE is moving (or has already moved) to the new MBMS service area. How does the MCPTT server know this?