3GPP TSG-SA WG3 LI Meeting #9 	Tdoc S3LI02_018r2

Amsterdam, Netherlands. 29 – 31 January 2002

| CR-Form-v4 |
| --- |
| CHANGE REQUEST |
| ( | 33.108 | CR | CRNum | ( rev | - | ( Current version: | 0.3.1 | ( |
| For HELP on using this form, see bottom of this page or look at the pop-up text over the ( symbols. |
| Proposed change affects: ( | (U)SIM |  | ME/UE |  | Radio Access Network |  | Core Network | x |
| Title: ( | Definition of the ULIC header in ASN.1 |
| Source: ( | Alcatel S.A. |
| Work item code: ( |  |  | Date: ( | 30 January 2002 |
| Category: ( | B |  | Release: ( | Rel-5 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: 2 (GSM Phase 2) R96 (Release 1996) R97 (Release 1997) R98 (Release 1998) R99 (Release 1999) REL-4 (Release 4) REL-5 (Release 5) |
| Reason for change: ( | Need to define a dynamic header for HI3 for packet switched networks.to handle new parameters |
| Summary of change: ( | HI3 UMTS PS ASN.1 defined |
| Consequences if ( not approved: | Difficulties to handle new parameters over HI3 interface |
| Clauses affected: ( | chapter 3.2 annex B B.5 is created annex C.1 GLIC v0 becomes ULIC v0 ULIC v1 is created (ASN.1 based) refer to new annex B.5 annex F annex F.4 is created |
| Other specs ( |  | Other core specifications ( |  |
| affected: |  | Test specifications |  |
|  |  | O&M Specifications |  |
| Other comments: ( | / |

How to create CRs using this form:

Comprehensive information and tips about how to create CRs can be found at: http://www.3gpp.org/3G_Specs/CRs.htm.  Below is a brief summary:

1)	Fill out the above form. The symbols above marked ( contain pop-up help information about the field that they are closest to.

2)	Obtain the latest version for the release of the specification to which the change is proposed. Use the MS Word "revision marks"  feature (also known as "track changes") when making the changes. All 3GPP specifications can be downloaded from the 3GPP server under ftp://ftp.3gpp.org/specs/ For the latest version, look for the directory name with the latest date e.g. 2001-03 contains the specifications resulting from the March 2001 TSG meetings.

3)	With "track changes" disabled, paste the entire CR form (use CTRL-A to select it) into the specification just in front of the clause containing the first piece of changed text.  Delete those parts of the specification which are not relevant to the change request.

## 3.2	Abbreviations

For the purposes of the present document, the following abbreviations apply:

ULIC	UMTS LI Correlation

../..

# B.5	Content of communication information (HI3)

HI3-PS {object-id to be defined }

DEFINITIONS IMPLICIT TAGS ::=

BEGIN

IMPORTS

LawfulInterceptionIdentifier,

GPRSCorrelationNumber,

TimeStamp,

FROM HI2-UMTS-PS { to be defined };

cC-PDU		[1] CC-PDU

CC-PDU	::= SEQUENCE

{

uLIC-header	[1] ULIC-header,

payload			[2] OCTET STRING

}

ULIC-header ::= SEQUENCE

{

version						[1]	Version,

lIID							[2] 	LawfulInterceptionIdentifier OPTIONAL,

correlation-Number		[3]	GPRSCorrelationNumber,

timeStamp					[4]	TimeStamp OPTIONAL,

sequence-number			[5]	INTEGER (0..65535),

t-PDU-direction			[6] 	TPDU-direction,

…

}

Version ::= ENUMERATED

{

version1(1),

…

}

TPDU-direction ::= ENUMERATED

{

from-target (1),

to-target (2),

unknown (3)

}

END

../..

Annex C (normative):
UMTS HI3 Interface

There are two possible methods for delivery of content of communication to the LEMF standardized in this document:

-	UMTS LI Correlation (ULIC) Header and UDP/TCP

-	FTP

Two versions of ULIC are defined: version 0 and version 1.

# C.1	UMTS LI Correlation Header version 0

## C.1.1	Introduction

The header and the payload of the communication between the intercepted subscriber and the other party (later called: Information Element) is duplicated. A new header (later called: ULIC-Header) is added  before it is sent to LEMF.

Data packets with the ULIC header shall be sent to the LEA  via UDP/IP or TCP/IP.

## C.1.2	Definition of ULIC Header version 0

ULIC header contains the following attributes:

- Correlation Number

- Message Type (a value of 255 is used for HI3-PDU’s).

- Direction

- Sequence Number

- Length

T-PDU contains the intercepted information.

|  |  | Bits |
| --- | --- | --- |
| Octets |  | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| 1 |  | Version (‘0 0 0’) | ‘1’ | Spare ‘1 1‘ | DIR | ‘0’ |
| 2 |  | Message Type (value 255) |
| 3-4 |  | Length |
| 5-6 |  | Sequence Number |
| 7-8 |  | not used (value 0) |
| 9 |  | not used (value 255) |
| 10 |  | not used (value 255) |
| 11 |  | not used (value 255) |
| 12 |  | not used (value 255) |
| 13-20 |  | correlation number |

# Figure C.1: Outline of GLIC header

-	For interception tunneling  the ULIC header shall be used as follows:

-	Version shall be set to 0 to indicate the first version of  ULIC header.

-	DIR indicates the direction of the T-PDU:

"1" indicating uplink (from observed mobile user) and

"0" indicating downlink (to observed mobile user).

-	Message Type shall be set to 255 (the unique value that is used for T-PDU within GTP [12]).

-	Length shall be the length, in octets, of the signaling message excluding the ULIC header. Bit 8 of octet 3 is the most significant bit and bit 1 of octet 4 is the least significant bit of the length field.

-	Sequence Number is an increasing sequence number for tunneled T-PDUs. Bit 8 of octet 5 is the most significant bit and bit 1 of octet 6 is the least significant bit of the sequence number field.

-	Correlation Number consists of two parts:-	GGSN-ID identifies the GGSN which creates the Charging-ID

Charging-ID is defined in [12] and assigned uniquely to each PDP context activation on that GGSN (4 octets).

The correlation number consist of 8 octets and guarantees a unique identification of the tunnel to the LEA over a long time. The requirements for this identification are similar to that defined for charging in [12], chapter 5.4. Therefore it is proposed to use the Charging-ID,  defined in [12] , chapter 5.4 as part of correlation number. The Charging-ID is signaled to the new SGSN in case of SGSN-change so the tunnel identifier could be used “seamlessly” for the HI3 interface.

| 0 |  |  |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  |  |  | 3 |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 0 | 1 |  |
| Charging –ID Octet 1 | Charging –ID Octet 2 | Charging –ID Octet 3 | Charging –ID Octet 4 | Octet 13-16 |
| GGSN-ID | Octet 17-20 |

Figure C.2: Outline of correlation number

The ULIC header is followed by a subsequent payload information element. Only one information element is allowed in a single signaling message.

|  | Bits |
| --- | --- |
| Octets | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| 1 – 20 | ULIC -Header |
| 21 –n | Information Element |

# Figure C.3: ULIC header followed by the subsequent payload Information Element

The Information Element contains the header and the payload of the communication between the intercepted subscriber and the other party.

## C.1.3	Definition of ULIC Header version 1

ULIC-header version 1 is defined in ASN.1 (ref [5]) (see annex B.5) and is encoded according to BER (ref [6]). It contains the following attributes:

- ULIC header version (version)
set to version1

- lawful interception identifier (lIID, optional)
sending of lawful interception identifier is application dependant; it is done according to national requirements

- correlation number	 (correlation-Number)

As defined in clause 6.1.3

- time stamp (timeStamp, optional), 
sending of time stamp is application dependant; it is done according to national requirements

- sequence number (sequence-number)

Sequence Number is an increasing sequence number for tunneled T-PDUs. Handling of sequence number is application dependent; it is done according to national requirements (e.g. unique sequence number per PDP-context).

- TPDU direction (t-PDU-direction) 
indicates the direction of the T-PDU (from the target or to the target).

The ULIC header is followed by a subsequent payload information element. Only one information element is allowed in a single signalling message (see annex B.5).

## C.1.4	Exceptional Procedure

With ULIC over UDP : the delivering node doesn’t take care about any problems at LEMF.

With ULIC over TCP : TCP tries to establish a connection to LEMF and re-sending (buffering in the sending node) of packets is also supported by TCP.

In both cases it might happen that  content of communication gets lost (in case the LEMF or the transit network between MF and LEMF is down for a long time).

## C.1.5	Other Considerations

The use of IPsec for this interface is recommended.

The required functions in LEMF are:

-	Collecting and storing of the incoming packets inline with the sequence numbers.

-	Correlating of CC to IRI with the use of the correlation number in the ULIC header.

# F.4	HI3 CC definition

HI3-PS {object-id to be defined }

DEFINITIONS IMPLICIT TAGS ::=

BEGIN

IMPORTS

LawfulInterceptionIdentifier,

GPRSCorrelationNumber,

TimeStamp,

FROM HI2-UMTS-PS { to be defined };

cC-PDU		[1] CC-PDU

CC-PDU	::= SEQUENCE

{

uLIC-header	[1] ULIC-header,

payload			[2] OCTET STRING

}

ULIC-header ::= SEQUENCE

{

version						[1]	Version,

lIID							[2] 	LawfulInterceptionIdentifier OPTIONAL,

correlation-Number		[3]	GPRSCorrelationNumber,

timeStamp					[4]	TimeStamp OPTIONAL,

sequence-number			[5]	INTEGER (0..65535),

t-PDU-direction			[6] 	TPDU-direction,

…

}

Version ::= ENUMERATED

{

version1(1),

…

}

TPDU-direction ::= ENUMERATED

{

from-target (1),

to-target (2),

unknown (3)

}

END

# Comments

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to http://www.3gpp.org/3G_Specs/3G_Specs.htm

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

Enter a concise description of the subject matter of the CR. It should be no longer than one line.

Enter the source of the CR. This is either (a) one or several companies or, (b) if a (sub)working group has already reviewed and agreed the CR, then list the group as the source.

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, B & C CRs for release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See http://www.3gpp.org/ftp/information/work_plan/

Enter the date on which the CR was last revised.

Enter a single letter corresponding to the most appropriate category listed below. For more detailed help on interpreting these categories, see the Technical Report 21.900 "3GPP working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR was to be rejected. It is necessary to complete this section only if the CR is of category "F" (i.e. essential correction).

Enter each the number of each clause which contains changes.

Enter an X in the box if any other specifications are affected by this change.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.

This is an example of pop-up text.