| CR-Form-v9.2 |
| --- |
| CHANGE REQUEST |
| ( | 33.107 | CR | CRNum | ( rev | - | ( Current version: | 7.5.0 | ( |
| For HELP on using this form look at the pop-up text over the ( symbols. Comprehensive instructions on how to use this form can be found at http://www.3gpp.org/specs/CR.htm. |

| Proposed change affects: ( | UICC apps( |  | ME |  | Radio Access Network |  | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: ( | WLAN optional IRI at AAA for re-authentication |
| --- | --- |
| Source to WG: ( | Nokia Siemens Networks |
| Source to TSG: ( | SA 3 LI |
| Work item code: ( |  |  | Date: ( | 26/04/2007 |
| Category: ( | B |  | Release: ( | Rel-8 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: R97 (Release 1997) R98 (Release 1998) R99 (Release 1999) Rel-4 (Release 4) Rel-5 (Release 5) Rel-6 (Release 6) Rel-7 (Release 7) Rel-8 (Release 8) |
| Reason for change: ( | Allow to send additional information and not only the first time |
| Summary of change: ( | Add a new trigger point for re-authentication at the AAA server. |
| Consequences if ( not approved: | This info couldn’t be provided |
| Clauses affected: ( | 9.3.2 & 9.4.1 |
|  | Y | N |  |  |
| Other specs ( | x |  | Other core specifications ( | 33.108 |
| affected: |  | X | Test specifications |  |
|  |  | X | O&M Specifications |  |
| Other comments: ( |  |

***First Change***

### 9.3.2	3GPP WLAN Interworking LI Events and Event Information

The following events are applicable to AAA Server:

-	I-WLAN Access Initiation; I-WLAN re-authentication (optional)

Note: The event I-WLAN Access Initiation is mandatory, I-WLAN re-authentication is optional, but the information is delivered via the same event definition.

-	I-WLAN Access Termination;

-	I-WLAN Tunnel Establishment;

-	I-WLAN Tunnel Disconnect;

-	Start of Intercept with I-WLAN Communication Active;

The following events are applicable to the PDG:

-	I-WLAN Tunnel Establishment;

-	I-WLAN Tunnel Disconnect;

-	Start of Intercept with I-WLAN Communication Active.

A set of possible elements as shown below is used to generate the events. Information associated with the events are transmitted from the PDG or AAA server to DF2.

Note – some of these parameters apply to the PDG and some apply to the AAA server.  Parameters sent from the PDG or AAA server is dependent on what is available at the network element.

***End first change***

***Second change***

### 9.4.1	I-WLAN Access Initiation / I-WLAN re-authentication

For I-WLAN Access Initiation or optional for I-WLAN re-authentication, a I-WLAN Access Initiation-event is generated. The elements, shown in Table 4, will be delivered to the DF2, if available, by the AAA server.

Table 4: I-WLAN Access Initiation / I-WLAN re-authentication – AAA Server

Observed MSISDN

Observed IMSI

Observed NAI

Event Type

Event Time

Event Date

Network Element Identifier

WLAN Operator Name

WLAN Location Name

WLAN Location Information

NAS IP/IPv6 Address

WLAN UE MAC Address

Visited PLMN ID

Session Alive Time

Failed Access reason

***End second change***

# Comments

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.  It consists of at least three digits, padded with leading zeros if necessary.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR was written and (normally) to which it will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to  http://www.3gpp.org/specs/specs.htm.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

SIM / USIM / ISIM applications.

Enter a concise description of the subject matter of the CR. It should be no longer than one line.  Do not use redundant information such as "Change Request number xxx to 3GPP TS xx.xxx".

One or more organizations (3GPP Individual Members) which drafted the CR and are presenting it to the Working Group.

For CRs agreed at Working Group level, the identity of the WG.  Use the format "x WGn" where 
	x = "CT" for TSG CT, "RAN" for TSG RAN, "SA" for TSG SA, "GERAN" for TSG GERAN; 
	n = digit identifying the Working Group; for CRs drafted during the TSG meeting itself, use "TSG x". 
Examples: "CT WG4", "RAN WG5", "GERAN WG3", "TSG SA".

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, B & C CRs for release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See http://www.3gpp.org/ftp/information/work_plan/ .

Enter the date on which the CR was last revised.  Format to be interpretable by English version of MS Windows ® applications, e.g. 19/02/2002.

Enter a single letter corresponding to the most appropriate category listed below. For more detailed help on interpreting these categories, see the Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR were to be rejected. It is mandatory necessary to complete this section only if the CR is of category "F" (i.e. correction), though it may well be useful for other categories.

Enter the number of each clause which contains changes.

Tick "yes" box if any other specifications are affected by this change.  Else tick "no".  You MUST fill in one or the other.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.