3GPP TSG SA WG3 LI Meeting #25  	SA3LI0y_0yyry

25-27 April 2007

Riga, Latvia

| CR-Form-v9.3 |
| --- |
| CHANGE REQUEST |
| ( | 33.107 | CR | CRNum | ( rev | - | ( Current version: | 7.5.0 | ( |
| For HELP on using this form look at the pop-up text over the ( symbols. Comprehensive instructions on how to use this form can be found at http://www.3gpp.org/specs/CR.htm. |

| Proposed change affects: ( | UICC apps( |  | ME |  | Radio Access Network |  | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: ( | IMS lawful interception solution based on media re-routing |
| --- | --- |
| Source to WG: ( | SA3-LI(ZTE Corporation) |
| Source to TSG: ( |  |
| Work item code: ( | SEC-LI |  | Date: ( | April, 2007 |
| Category: ( | B |  | Release: ( | 7 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: R97 (Release 1997) R98 (Release 1998) R99 (Release 1999) Rel-4 (Release 4) Rel-5 (Release 5) Rel-6 (Release 6) Rel-7 (Release 7) Rel-8 (Release 8) |
| Reason for change: ( | Solution in this CR will be different from the normal design in IMS service interception. Considering two things: There are so many kinds of communication deives in the IMS network, MGCF, MGW, BGCF, AGCF, AG, C-BGF, MRCF, CSCF, GSN and so on. It will be a huge workload to realize LI functions in these devices one by one. according to the current interception design in IP domain, more new internal interface appears: INI1b, CCTI, CCCI. When the devices supplied by different manufacturers(it always be), this internal interfaces will be very hard to negotiate, sometimes maybe impossible. So, we don’t have a very efficient solution in IMS LI now. Considering the other two things: IMS services will be controlled by CSCF, if we realize the interception function in CSCF, not so much kinds of equipments are involved, just on the CSCF, it will be easy to realize it. Communication is controlled by SIP protocol. As we know, SIP could be well extended. So it is convenient to realize some specific function for interception. So, re-route the media stream by the control of CSCF to a special equipment(media duplicator), and then duplicate the media to the mediation function could be a more feasible way. This solution will look like the following way: Here, we try to find a centralized and effective solution for interception which could be adopted according to national requirement when the normal method doesn’t work in some circumstance. This design could be the supplementary for the routine method. |
| Summary of change: ( | Addition of IMS lawful interception solution based on media re-routing |
| Consequences if ( not approved: | No complete solution for IMS interception |
| Clauses affected: ( | 7(Add clause 7B) |
|  | Y | N |  |  |
| Other specs ( |  | X | Other core specifications ( |  |
| affected: |  | X | Test specifications |  |
|  |  | X | O&M Specifications |  |
| Other comments: ( |  |

********** Modification ************

# 7B	Interception of IMS based on media re-routing

## 7B.1 realization configuration

The configuration of this realization is shown in Figure 1.  This  implementation could be taken as a national option.

Under the control of P-CSCF/S-CSCF, the target’s media stream could be first re-routed to a special equipment(media duplicator) and traverse to the destination. Communication content will be duplicated simultaneously by the media duplicator and sent to the DF3.

Figure 1 Interception configuration based on the media re-routing

********** End of Modifications ************

# Comments

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.  It consists of at least four digits, padded with leading zeros if necessary.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR was written and (normally) to which it will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to  http://www.3gpp.org/specs/specs.htm.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

SIM / USIM / ISIM applications.

Enter a concise description of the subject matter of the CR. It should be no longer than one line, but if this is not possible, do not enter hard new-line characters.  Do not use redundant information such as "Change Request number xxx to 3GPP TS xx.xxx".

One or more organizations (3GPP Individual Members) which drafted the CR and are presenting it to the Working Group.

For CRs agreed at Working Group level, the identity of the WG.  Use the format "xn" where 
	x = "C" for TSG CT, "R" for TSG RAN, "S" for TSG SA, "G" for TSG GERAN; 
	n = digit identifying the Working Group; for CRs drafted during the TSG meeting itself, use "P". 
Examples: "C4", "R5", "G3new", "SP".

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, A, B & C CRs for Release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See 
http://www.3gpp.org/ftp/Specs/html-info/WI-List.htm .

Enter the date on which the CR was last revised.  Format to be interpretable by English version of MS Windows ® applications, e.g. 19/02/2006.

Enter a single letter corresponding to the most appropriate category listed. For more detailed help on interpreting these categories, see Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR were to be rejected. It is mandatory to complete this section only if the CR is of category "F" (i.e. correction), though it may well be useful for other categories.

Enter the number of each clause which contains changes.   Be as specific as possible (ie list each subclause, not just the umbrella clause).

Tick "yes" box if any other specifications are affected by this change.  Else tick "no".  You MUST fill in one or the other.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.