## Slide 1: Location reporting within RAN
Nokia, Nokia Shanghai Bell

## Slide 2: "Opportunistic" location reporting in LTE (1)
Location information appended to other S1AP procedures ("opportunistic" reporting)
  PCell is appended to selected procedures on S1AP
    provided for all UEs, but only when S1AP signalling is needed for other purposes
  User Location Information (ULI) is appended to some other S1AP procedures (optionally)

## Slide 3: "Opportunistic" location reporting in LTE (2)
Events that trigger the S1AP procedures with PCell:
  Connection setup (INITIAL UE MESSAGE, UPLINK NAS TRANSPORT)
  Connection reconfiguration (UPLINK NAS TRANSPORT)
  Inter-eNB HO (HANDOVER NOTIFY, PATH SWITCH REQUEST)
  Connection re-establishment after a failure (eNB CP RELOCATION INDICATION)
  Connection termination (known from the last report or from the ULI, if included)

## Slide 4: "Opportunistic" reporting of PSCell reporting in EN-DC
Normally, PSCell is known in the Secondary Node (gNB) only
  Some changes are not reported to the Master Node (eNB)
When the serving cell is required, it is assumed PSCell is also required (if EN-DC is configured)
Improvements to the "opportunistic" appending of the PSCell:
  PSCell is added to the UPLINK NAS TRANSPORT, HANDOVER NOTIFY, PATH SWITCH REQUEST and ULI
    This enables receiving PCell and PSCell after an inter-eNB HO or connection reconfiguration; RAN3 will likely continue the discussion on providing PSCell after connection setup (INITIAL UE MESSAGE is sent before EN-DC can be configured)
  It shall be reported when the EN-DC is configured and the eNB knows the PSCell (i.e. when the PSCell is provided from the gNB over X2)
    Currently, the eNB shall request the gNB to append the PSCell to the X2AP signalling, but proposals to remove this requirements were made at the last RAN3 meeting (not treated due to focusing on more urgent issues)

## Slide 5: Location Report procedure in LTE
Location Reporting procedure
  The EPC may request User Location Information (ULI) for particular UE, either as a reponse to the request (once) or to be provided whenever the ULI changes (i.e. the PCell changes).
  ULI is provided in an independent message and contains the current serving cell at the eNB (PCell).

## Slide 6: PSCell in Location Report procedure in EN-DC
Improvements to the Location Reporting:
  PSCell was added to the LOCATION REPORT
  When the location reporting is requested for given UE, the eNB forwards the request to the gNB; the gNB shall start providing the PSCell over X2 whenever the PSCell changes (PSCell is appended to other X2AP signalling – in most cases, no extra X2 signalling is needed)
  The report is sent to the MME always when either the PCell or the PSCell changes  possibly more signalling over S1AP!

## Slide 7: Other NR-related DC options
For NR DC, the procedures for Location Reporting and for the "opportunistic" appending the location information are in principle the same.
  In NGAP, UE location is provided always within the ULI; hence, it was enough to add PSCell to ULI to get it reported in both solutions

## Slide 8: Conclusions
In the context of DC, the current RAN solution enables:
  Providing PCell and PSCell whenever either of them changes, when requested over S1AP for selected UE
    If used for all UEs, may trigger heavy RAN signalling
  Providing PCell and PSCell from any UE whenever an inter-MN HO is executed (or the user service is reconfigured)
    Some changes of PCell and/or PSCell may not be reported, e.g. intra-MN HO
Points raised at the last RAN3 meeting and not yet concluded:
  Shall the PSCell be reported over X2AP/XnAP only when requested from the MN?
  Shall the PSCell be reported for the initial call setup (after it is configured)?