## Slide 1: 3GPP SA4 Rel-18 Priorities
Qualcomm Incorporated
S4WS-210009
SA4 Rel-18 Workshop
August 17, 2021

## Slide 2: Guiding Principles
Standardization Priorities
Clear product and commercialization interests
App integration with non-vertical service framework
Leverage deployed multimedia technologies
Support for implementation and deployment (tools, reference s/w, interop,…)

## Slide 3: Rel-18
Rel-18 should start the “2nd cycle” of 5G evolution
  Rel-15/Rel-16 were both major, Rel-17 was fairly limited in scope
Rel-18 needs to accommodate studies for longer-term topics to be developed throughout Rel-19/20
  18 month duration preferred
  First release of “5G advanced”
Duration
2018 |  |  |  | 2019 |  |  |  | 2020 |  |  |  | 2021 |  |  |  | 2022 |  |  |  | 2023 |  |  |  | 2024 |  |  |  | 2025 |  |  |  | 2026 |  |  |  | 2027 |  |  |  | 2028 |  |  |  | 2029 |  |  | 
1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4
Rel-15
Rel-16
NSA
SA
Late Drop
Rel-17
Rel-18
Rel-19
Rel-20
Rel-21
eMBB
verticals
enhancements
2nd phase of 5G

## Slide 4: Summary of Rel-18 Priorities
Areas of work
SA4 Rel-17 Study Items: follow-up work
SA1 Stage 1 Items: follow-up work in SA4
Continuation of Rel-18 Work Items

## Slide 5: SA4 Rel-17 Study Items
Follow-up work

## Slide 6: Integration of new Video Codec into 5G
Background/Justification
  From TR 26.955, we expect to observe clear technical benefits for new video codecs compared to existing codecs.
  In particular, for services with more diverse needs of signal types (gaming, 4K, 8K, screen content) benefits in the range of 30-50% compression efficiency at the same quality can be observed for certain codecs
  3GPP beneficially adds interoperability and full characterization for relevant 3GPP scenarios.
Draft objectives
  Provide decoding capabilities, interoperability and signaling extensions for DASH/CMAF and RTP-based Video delivery
  Add new codec to TV Media Profiles for 4K-TV and 8K-TV
  Provide recommendations and requirements for support of new video codec in different 3GPP-defined services including 5G Media Streaming and MTSI
  Provide complete characterization results for new video codec based on TR 26.955 for all relevant scenarios
  Update TR 26.925 with typical traffic characteristics adding new information based on new video codec performance
  Work with relevant organizations to introduce common media profiles and reference material for new video codec-based media distributions.
Based on FS_5GVideo Study Item Recommendations

## Slide 7: 5G Augmented Reality Experiences (5G-STAR)
Expected Conclusions (not only for AR study, but also from XR study)
  AR/Rendering centric end-points need to be defined following the architecture below
  Generic Architecture for XR/AR end points need to be defined
  Operator and third-party services need to be supported
  5G Integration through different methods (OTT-based and IMS-based)
  Specific building blocks require more detailed specification work, for example new formats and signals
  Different and additional KPIs are of relevance: latency, power consumption, signal quality, etc.
Potential for (multiple) Stage 2 & 3 Work Items
  AR/XR architecture (Device and split-rendering, see next slide)
  Generic real-time streaming architecture (next slide)
  Support for AR/XR in different 3GPP services
  Traffic characteristics and QoS requirements
  Rendering and XR centric end-points
  Integration into 5G System
  AR/XR media formats
  AR/XR reporting and metrics
  XR System and cross-layer support (SA2/RAN)
Based on FS_5GSTAR Study Item Recommendations

## Slide 8: 5G Real-time Communication (5G-RTC)
Integration of third-party services/apps
  More components and specs are needed
  Similar to the approach done for 5G Media Streaming
Session Setup and Control
  SIP-based (TS 26.114)
  OTT and application based (webRTC model)
QoS and 5G Integration
  SIP/IMS-based (TS 26.114)
  OTT and Service-based (webRTC and 5GMS model)
Content Delivery and Media
  RTP/RTCP-based + Control (26.114 + webRTC?)
  Codecs are already in TS 26.114 and TS 26.511 – what else?
  May be split into two separate work tasks
End Points
  Direct output/input (speakers/displays/cameras/microphones)
  XR Rendering: scene rendering, e.g. glTF + MPEG-I SD
  XR Runtimes: pose, trackers, and sensors, e.g. OpenXR
Based on ITT4RT, FS_5GSTAR, Split Rendering, etc.
5G-RTC media receiver
5G-RTC media sender
Rendering End Points
Capturing Sources
Session Setup
Applications
QoS and System Integration

## Slide 9: 5G Media Service Enablers (5G-MSE)
Something like an SDK with APIs
A set of functions that may be used to develop applications on top of 5G Systems.
A set of robust features and functionalities which reduce the complexity of developing applications
Leverages system + radio optimizations/ features developed in SA2 & RAN
Supported by APIs to simplify and enable access to these functionalities
Supported by network interfaces to connect to the 5G System
Real-time communication
  5G-RTC Stack Receiver + Sender
  2D codecs up 2k
Raster-based Split Rendering
  5G-RTC Stack Receiver
  2D codecs up to 8k
  Audio functionalities
  Edge
  QoS Framework
Vector-based Split Rendering
  Builds on raster-based split rendering
  Add 3D media formats, transport, QoS
AR Split Compute
Real-time Cloud Gaming
XR Library
AI/ML Components
Bundling components into valuable functions and simplifying the access
Definition
Potential Examples

## Slide 10: Split-Rendering Stage 3
Background/Justification
  Rendering is quite complex, especially for advanced applications such as gaming and AR
  5G offers new capabilities such as low latency and edge processing
  Enable UE to share rendering with the edge for superior user experience
Draft Objectives
  Re-use of 5G-RTC components
    Media formats and codecs for split rendering
    Control and transport protocols for split rendering
  Re-use EDGE, STAR, and XRTraffic work
  Integrate split rendering in the 5GMS architecture
  Define split rendering context and context relocation
Based on FS_EMSA recommendations, 5GMS_EDGE, and FS_XRTraffic

## Slide 11: 5GMS Architecture/Stage 3 & 5MBS
Areas of interest
  Background traffic
  Live-Streaming and Context Aware Streaming
  Traffic Identification
  New Protocols
  Security and DRM
  Possibly new study topics
Background/Justification
  Justification see in TR 26.804
  Propose to extend TR 26.804 until the end of Rel-17 and start normative work for Rel-18 in 2022
Draft Objectives
  Provide updates to stage-2 as needed
  Provide updates to stage-3 as needed
Based on FS_5GMS_EXT Study Item Recommendations and not completed work in in 5MBS
Areas of interest
  Remaining issues from Rel-17
  Hybrid Services
  Support for 5MBS User Service and 5G Core
Background/Justification
  Justification see in TR 26.802
Draft Objectives
  Provide updates to stage-2 as needed
  Provide updates to stage-3 as needed
See also input from 5G-MAG

## Slide 12: SA1 Stage 1 Items
Follow-up SA4 work

## Slide 13: SI: AI/ML Media
Background/Justification
  Proliferation of AI-based media processing
  Edge opens new opportunities for inference in the network
  Exchange of trained models, update of model weights, and transmission of media data for processing generate significant traffic
Draft Objectives
  Traffic Characterization for AI/ML-based applications
  Identify gaps and enablers to support AI/ML applications
  Investigate protocols and formats for the exchange of AI models
  Recommend integration of AI/ML media processing with 5GMS and Edge
TR 22.874 5GS; Study on traffic characteristics and performance requirements for AI/ML model transfer

## Slide 14: Rel-18 SA4 Work Items
Continued support

## Slide 15: Continue to support in Rel-18
ATIAS (Terminal Audio quality performance and Test methods for Immersive Audio Services)
  Interest in developing and standardizing new terminal testing methodologies
IVAS_Codec (EVS Codec Extension for Immersive Voice and Audio Services)
  Currently scheduled to be completed in Rel-17, but could slip to Rel-18
  In this case, Rel-18 work would include everything needed for the service
    IVAS codec specifications
    Technical report on test results, complexity, memory, etc…
    Integration into 3GPP system and services