## Slide 1: XR and Gaming in 3GPP
Thomas Stockhammer
Location
Date
@qualcomm

## Slide 2: Agenda
3GPP Work on XR
XR Traffic
5G Video

## Slide 3: FS_XR5G (eXtended Reality (XR) in 5G)
Study:
  Define Extended Reality and Terms in 3GPP, including quality-of-experience with XR services
  Collects the technologies in the context of XR and their potential relation to 5G System
  Collects 23 use cases in the context of XR and 5G that are analyzed in terms of potential specification needs
  Breaks down the use cases in architectures, functions and interfaces
  Create specific conclusions on normative work in Rel-17
  Support other 3GPP groups on the definition of system and radio specifications for XR
Detailed Technical Report completed in March 2020
  TR 26.928: http://www.3gpp.org/ftp//Specs/archive/26_series/26.928/26928-g00.zip
The first comprehensive output from 3GPP on XR – Rel-16 (!).
Source sample text

## Slide 4: Terms and Definitions
3DOF
3DOF+
Windowed 6DOF
6DOF
Time Warp
SLAM
Presence
Tracking
Point Cloud
Meshes

## Slide 5
No | Use Case | Type | Experience | Delivery | Device
1 | 3D Image Messaging | AR | 3DoF+, 6DoF | Upload and Download | Phone
2 | AR Sharing | AR, MR | 6DoF | Local, Messaging Download and Upload | Phone
3 | Streaming of Immersive 6DoF | VR | 3DoF+, 6DoF | Streaming, Interactive, Split | HMD with a controller
4 | Emotional Streaming | 2D, AR and VR | 2D, 3DoF+, 6DoF | Streaming Interactive, Split | Phone and HMD
5 | Untethered Immersive Online Gaming | VR | 6DoF | Streaming, Interactive, Split | HMD with a Gaming controller
6 | Video Game Live Streaming | VR | 6DoF | Streaming, Split | 2D screen or HMD with a controller
7 | Real-time 3D Communication | 3D, AR | 3DoF+ | Conversational | Phone
8 | AR guided assistant at remote location (industrial services) | 2D video + AR | 6DoF (2D + AR) | Local, Streaming, Interactive, Conversational | 5G AR Glasses, 5G touchscreen computer or tablet
9 | Police Critical Mission with AR | AR, VR | 3DoF to 6DoF | Local, Streaming, Interactive, Conversational, Group Communication | 5G AR Glasses/Helmet, VR camera/microphone, Audio stereo headset, 5G accurate positioning
10 | Online shopping from a catalogue – downloading | AR | 6DoF | Download | AR Glasses, Rendering system, Tablet (or smartphone), Capture device
11 | Real-time communication with the shop assistant | AR | 6DoF | Interactive, Conversational | AR Glasses, Rendering system, Tablet (or smartphone), Capture device
12 | 360-degree conference meeting | AR, MR, VR | 3DoF | Conversational | Mobile / Laptop
13 | 3D shared experience | AR, MR, VR | 3DoF+, 6DoF | Conversational | Mobile / Laptop
14 | 6DOF VR conferencing | VR | 6DoF | Interactive, Conversational | VR gear with binaural playback and HMD video playback, Call server
15 | XR Meeting | AR, VR, XR | 6DoF | Interactive Conversational | Phone, HMD, Glasses, headphones
16 | Convention / Poster Session | AR, VR, MR | 6DoF | Interactive, Conversational | Phone, HMD, AR Glasses, VR controller/pointing device, headphones
17 | AR animated avatar calls | AR | 2D, 3DoF | Conversational | Phone, HMD, Glasses, headphones
18 | Online shopping from a catalogue – downloading | AR | 6DoF | Download | AR Glasses, Rendering system, Tablet (or smartphone), Capture device
19 | Front-facing camera video multi-party calls | AR | 3DoF | Conversational | Smartphone with front-facing camera, headset
20 | AR Streaming with Localization Registry | AR, Social AR | 6DoF | Streaming, Interactive, Conversational | AR glasses with binaural audio playback support
21 | Immersive 6DoF Streaming with Social Interaction | VR and Social VR | 3DoF+, 6DoF | Streaming, Interactive, Conversational, Split | HMD with a controller
22 | 5G Online Gaming Party | VR | 6DoF | Streaming, Interactive, Split, D2D | HMD with a Gaming controller
23 | Spatial Shared Data | AR | 6DoF | Streaming, Interactive, Conversational, Split | HMD, AR Glasses

## Slide 6
XR
XR
XR
XR
XR
XR
XR
XR
XR Network Resources
XR
XR5G-P1
XR5G-V1
XR5G-V2
XR5G-V3
XR5G-V4
XR
XR5G-P1
XR
XR
XR
XR
XR
XR5G-A3
XR
XR5G-A1
XR5G-A2
XR5G-A4
XR
XR5G-A5
5G Technology
XR
XR Engine
Tracking
VR
AR

## Slide 7: Immersiveness and Presence
Presence is the feeling of being physically and spatially located in an environment - feeling like you’re really there
  Presence is achieved when the involuntary aspects of our reptilian corners of our brains are activated. When the user reaches out to grab the virtual apple, becomes unwilling to step off a plank or feel nervous when walking on rooftops. According to Teo Choong Ching [10], there are four components relevant for feeling present, namely the
Selected technical requirements for visual presence
  Spatial Resolution: 2k by 2k per eye provides acceptable quality. 4k is considered a next step, 8k ultimate goal.
  Temporal Resolution: sustained frame rate of 90Hz and beyond, despite the usage of asynchronous time warping.
Latency
  Less than 20 ms motion-to-photon latency - from the time you move your head to when you see the display change.
  Minimize the time of pose-to-render-to-photon. Rendering content as quickly as possible. Less than 50ms for render to photon in order to avoid wrongly rendered content. For more details refer to clause 4.2.2.
Details in Clause 4.2.1 of TR 26.928

## Slide 8: Latencies and Delays
The roundtrip interaction delay is therefore the sum of the Age of Content and the User Interaction Delay.
  User interaction delay is defined as the time duration between the moment at which a user action is initiated and the time such an action is taken into account by the content creation engine.
  Age of content is defined as the time duration between the moment a content is created and the time it is presented to the user.
Latency Requirements
  Ultra-Low-Latency applications: roundtrip interaction delay threshold of at most 50ms latency.
  Low-Latency applications: roundtrip interaction delay threshold of at most 100ms latency.
  Moderate latency applications: roundtrip interaction delay threshold of at most 200ms latency.
  Non- critical latency applications: roundtrip interaction delay threshold higher than 200ms latency.
Details in Clause 4.2.2 of TR 26.928

## Slide 9: Split Rendering Architecture
Example: Split Rendering
5G NR
"Edge"

## Slide 10: Process contributing to delays
User Interaction Delay
  capture of user interaction in game client,
  delivery of user interaction to the game engine, i.e. to the server (aka network delay),
  processing of user interaction by the game engine/server,
Age of Content
  creation of one or several video buffers (e.g. one for each eye) by the game engine/server,
  encoding of the video buffers into a video stream frame,
  delivery of the video frame to the game client (a.k.a. network delay),
  decoding of the video frame by the game client,
  presentation of the video frame to the user (a.k.a. framerate delay).
Example: Split rendering - based on TR 26.928

## Slide 11: 5GXR Proposed Standardization Areas
In the short-term:
  Develop a flexible XR centric device reference architecture as well as a collection of device requirements and recommendations for XR device classes based on the considerations in clause 7.2. Device classes should include VR device for 6DoF streaming and XR online gaming (XR5G-V4), as well as AR devices (XR5G-A1, XR5G-A4 and XR5G-A5) => FS_5GSTAR
  Develop a framework and basic functionalities for Single-Buffer Split Rendering for Online Gaming according to the considerations in clause 7.4 => already addressed agreed study FS_EMSA and FS_XRTraffic
  Document typical XR traffic characteristics in TR26.925 based on the initial considerations in this report, in particular clause 7.7 and support other 3GPP groups in designing systems for XR services and applications => FS_XRTraffic
  Address simple extensions to MTSI to support basic XR conversational services based on the considerations in clause 7.5 ==> Ongoing work item ITT4RT
  Study detailed functionalities and requirements for glass-type AR/MR UEs with standalone capability according to clause 7.6 => FS_5GSTAR
Based on TR 26.928 @ 125 pages/14 MB, TR26.928v16.0.0

## Slide 12: XR Traffic

## Slide 13: Background
During SA4#107 the New Study Item on “Feasibility Study on Extensions to Typical Traffic Characteristics” in S4-200334 was agreed and afterwards approved in by SA plenary #87 in SP-200054.
The objective of the study includes :
  Collect and document traffic characteristics including for different services, but not limited to
    Downlink data rate ranges
    Uplink data rate ranges
    Maximum packet delay budget in uplink and downlink
    Maximum Packet Error Rate,
    Maximum Round Trip Time
    Traffic Characteristics on IP level in uplink and downlink in terms of packet sizes, and temporal characteristics. XR Services and Cloud Gaming based on the initial information documented in TR26.928 including.
  Provide the information from above including the following services
    Simple Single Buffer split rendering for online cloud gaming
    Cloud Gaming
    Other Traffic Models
Why is it not trivial to obtain such numbers?

## Slide 14: Split Rendering Architecture
Example: Split Rendering
5G NR
"Edge"
Downlink Latency
Uplink Latency
Downlink Latency

## Slide 15: Cloud Gaming Architecture
Example: Cloud Rendering
5G NR
"Edge"
Downlink Latency
Uplink Latency
Downlink Latency

## Slide 16: Options to obtain traffic models
Some options
  Realistic system setup with measurements
  Measurement of existing services
  Breakdown of the system in smaller pieces
  Very simple traffic models
Some approaches are impractible
Others are too simplistic

## Slide 17: Example Configurations/Parameters
Game:
  Type of game, state of game, multi-user actions, etc.
Formats:
  Rastered video signal
Encoder configuration
  Codec, bitrate, rate control, slices, low-latency encoding, error resilience, intra, etc.
Content Delivery Sender
  RTP options, Rate control, error resilience, etc.
Content Delivery Receiver
  Feedback, Error Concealment, Post correction
Transport Layer Assumptions
  Loss rates, necessary delays, bitrates
Quality Metric
  Packet losses, slice losses, etc.
Latency from rendering in the network to device display is typically in the range of 50-60ms
Latency for pose is lower typically 20ms, but Asynchronous Time Warp can be applied to compensate for the latest pose in the device

## Slide 18: Basic Challenges and Tasks
Evaluate basic system design options and their performance
Generate Traffic Models for the evaluation of RAN options
Provide guidelines for good parameter settings on encoding, content delivery and also for RAN configurations
Provide measurable but also meaningful quality metrics
Identify the capacity for such type of applications
Identify potential optimizations (codec, protocols, system, QoS, cross-layer, RAN)
Lot’s of opportunities, the beginning not the end.

## Slide 19
S-Trace
V-Trace
Content Encoding
Model
S-Trace
RAN
Simulation
Decoding Model
Content Model
Content Delivery
Model
P-Trace
Delivery
Receiver
Model
S‘-Trace
P‘-Trace
Quality Evaluation
V‘-Trace
U-Model
XR Device (Tracker, User Interaction)
XR Engine and Server
U‘-Model
Configuration
Configuration
Configuration
Configuration
Configuration
P‘-Trace
S‘-Trace
Configuration
RAN API
RAN API
Multiple Users
Multiple Users

## Slide 20: P-Traces
Name | Type | Semantics
number | BIGINT | Unique packet number in the delivery
time_stamp_in_micro_s | BIGINT | Availability time of packet for next processing step relative to start time 0 in microseconds (0 means lost).
size | BIGINT | packet size in bytes.
user_id | BIGINT | assigns an id to the user in order to differentiate
buffer | BIGINT | The associated eye buffer 1=left 2=right In general, differentiates application traffic for different buffers, for example audio, video, left eye, right eye. For example mapped to port or track.
delay | BIGINT | Delay observed of the packet in the last processing step (-1 means lost)
render_timing | BIGINT | the rendering generation timing associated to the media included in the packet.
number_in_unit | BIGINT | The number of the packet within the unit (slice), start at 1
last_in_unit | BIGINT | Indicates if this is the last packet in the slice/unit 0=no, 1=yes
type | BIGINT | The data type of the unit 0 unknown For video 1=intra 2=inter
importance | BIGINT | assigned relative importance information (higher number means higher importance)
index | BIGINT | Unique index increased by 1 and indexing this row in the S-Trace file.
s_trace | STRING | Reference to s_trace file containing information for each slice

## Slide 21: Initial Configurations (1)
Content Model:
  Game output with 2 eye buffers at 2Kx2K at 60 fps, 8bit.
  Content and Trace Preview is here: http://dash.akamaized.net/WAVE/3GPP/XRTraffic/Traces/Qualcomm-VR2
  No audio
Encoding Model
  HEVC model as defined in S4aV200575
  target bitrate 30 Mbit/s, equally split across eye buffers, independently encoded.
  Pre-encoding delay: Encoder pre-delay is varying between 10 to 20ms
  Encoding delay is modelled to vary with truncated Gaussian
Content Delivery Model
  Edge/Cloud to gNB bitrate is 1.5 media bitrate
Delivery receiver
  Slice loss model (1 lost packets per slice results in slice loss)
  Maximum latency for slice: 60ms (see TR 26.928, clause 4 and 6.2.5.1)
Fixed Parameters

## Slide 22: Initial Configurations (2)
Configurations
Configuration | Basic Content Parameters
VR2-1 | 8 slices per eye buffer, 1 slice per frame is intra coded, 30Mbit/s capped VBR with window 200ms, buffer sent at same time, 1500 byte max packet size
VR2-2 | 8 slices per eye buffer, 1 slice per frame is intra coded, 30Mbit/s capped VBR with window 200ms, buffer sent at same time, unlimited packet size
VR2-3 | 8 slices per eye buffer, 1 slice per frame is intra coded, 30Mbit/s CBR with window 1 frame, buffer sent at same time, 1500 byte max packet size packets
VR2-4 | 8 slices per eye buffer, 1 slice per frame is intra coded, 30Mbit/s CBR with window 1 frame, buffer sent at same time, unlimited packet size
VR2-5 | 1 slice per eye buffer, every 8th frame is intra coded, 30Mbit/s capped VBR with window 200ms, buffer sent at same time, 1500 byte max packet size
VR2-6 | 8 slices per eye buffer, 1 slice per frame is intra coded, 30Mbit/s capped VBR with window 200ms, buffers sent interleaved, 1500 byte max packet size
VR2-7 | 8 slices per eye buffer, 1 slice per frame is intra coded, 45Mbit/s capped VBR with window 200ms, buffer sent at same time, 1500 byte max packet size
VR2-8 | 8 slices per eye buffer, 1 slice per frame is intra coded, 45Mbit/s capped VBR with window 200ms, buffer sent at same time, unlimited packet size
More configurations are expected to be evaluated for performance with Test Channel Parameters

## Slide 23: Initial Configurations (3)
A model for the uplink traffic in a similar fashion also providing packet traces.
  XR Pose is sent uplink
  The uplink bitrate for the pose is 200 kbit/s CBR, with 4ms packet interval and packet size 100 byte. This means that the content is rendered with a pose of typically 10-15ms age.
  Details are in S4aV200575
  The E2E Requirements are
    Bitrate: 200 kbit/s
    PLR: 1e-3
Delay from UE to XR Server in the range of 10ms
Uplink

## Slide 24: Configuration example

## Slide 25: Results from VR2-7

## Slide 26: Quality of configurations are still tbd
Q-Trace
S-Trace
Test Channel
Decoding Model
P-Trace
Delivery
Receiver
Model
S‘-Trace
P‘-Trace
Quality Evaluation multiple users
V‘-Trace
Configuration
P‘-Trace
S‘-Trace
Configuration
RAN API
RAN API
Multiple Users
Quality Evaluation per user
Q-Trace
Test Channel and Evaluation

## Slide 27: 5G Video
Evaluating Video Codecs

## Slide 28: FS_5GVideo Feasibility Study on 5G Video Codec Characteristics
Summary:
  Study to collect relevant scenarios for (new) video codecs for 5G
  Collects reference sequences, anchors, metrics based on AVC and HEVC
  Creates a framework for video codec characterization in 5G
  Documents initial results for VVC and EVC – identifies potential normative work
Status
  60%, framework complete except reference sequences for CG
  Next steps: anchor generation for AVC/HEVC, metrics,
  Initial VVC and EVC results to follow – conclusions
  AV1 under discussion
Interested companies
  Qualcomm, Tencent, Interdigital, ATEME, Apple, AT&T, Fraunhofer, Samsung (to some extent), Orange, others
TR 26.955 contains all relevant information
Status is here.

## Slide 29
Reference Sequence
Anchor Configuration
Anchor Bitstream
Anchor Sequence
Metrics Computation
Reference Software
Encoder
Conforming
Decoder
Anchor Metrics

## Slide 30: Metrics
Name | Type | Semantics
parameter | BIGINT | the associated variation parameter as defined for the anchor, for example the QP
bitrate | DOUBLEPRECISION | The size of the file divided by the duration of the reference sequence in bit/s as defined in clause 5.5.1 with 2 decimal digits accuracy.
y_psnr | DOUBLEPRECISION | Peak signal to noise ratio for Y planes in dB as defined in clause 5.5.2 with 2 decimal digits accuracy.
u_psnr | DOUBLEPRECISION | Peak signal to noise ratio for U planes in dB as defined in clause 5.5.2 with 2 decimal digits accuracy.
v_psnr | DOUBLEPRECISION | Peak signal to noise ratio for V planes in dB as defined in clause 5.5.2 with 2 decimal digits accuracy.
ms_ssim | DOUBLEPRECISION | structural similarity between frames as defined in clause 5.5.2 with 4 decimal digits accuracy.
vmaf | DOUBLEPRECISION | Video Multimethod Assessment Fusion (VMAF) as defined in clause 5.5.2 with 2 decimal digits accuracy.
bitrate_log | DOUBLEPRECISION | The bitrate as documented by the encoder log. If not known, it is set to 0.
encode_time | DOUBLEPRECISION | Total time spent to encode the sequence with reference encoder in seconds. If not known, it is set to 0.
decode_time | DOUBLEPRECISION | Total time spent to decode the sequence with reference decoder in seconds. If not known, it is set to 0.

## Slide 31
Test Tuple Metrics
Anchor Metrics
Anchor Metrics
Test Metrics
Anchor Tuple Metrics
Anchor Metrics
Anchor Metrics
Anchor Metrics
Characterization Results