## Slide 1: [5G_RTP_Ph2] Minutes from offline on ETI
Saba Ahsan (Nokia)

## Slide 2: Outline
Participants: Saba Ahsan (Nokia), Razvan Andrei Stoica (Lenovo), Liangping Ma (Qualcomm), Rufael Mekuria [Huawei], Srinivas Gudumasu (Interdigital), Qi Pan--Huawei (Unverified), Gazi Illahi (Nokia), Yoshihiro Inoue (NTT), Imed Bouazizi (Qualcomm), Igor Curcio (Nokia), Serhan Guel (Nokia)
Input documents: 440, 441, 511, 512, 513, 510, 611

## Slide 3: User Plane
User Plane:
  Send ETI as part of a RTP HE
    1-bit flag – Needs to be sent at least with every packet that has to be upgraded (i.e., ETI=T flag must be set for each relevant packet)
    Signalling options:
      How it’s sent
        Use a reserved bit in one of the existing HE
        Have a new HE? (currently not a proposal)
          At least 3 bytes need to be sent
      How often it is sent
        Signalled with every PDU
          Since PDU set HE is signalled with every packet; a reserved bit from PDU set HE can be used.
        Signalled only when needed
          2 PDR rules are needed. If ETI=T it goes to 1st QoS-flow, if ETI is false it goes to 2nd QoS Flow
            If RTP HE is present and ETI=T, then boosting is True;
            If RTP HE is absent or RTP HE is present but ETI=F, then boosting is False;
            Caveat: We may need to check with SA2 if they have any reservations about this.
          Since dynamic traffic characteristics is signalled only when needed; a reserved bit from dyn. tra. char. can be used. We can have:
            Fixed fields in the dyn. Traf.char. HE; can create more overhead when not all fields are needed but simpler solution (less complexity for the UPF).
            Dynamic fields can reduce overhead but creates complexity.

## Slide 4: Control Plane
ETI can be enabled on the control plane:
  If sent as part of dyn. traffic characteristics RTP HE then
    Collectively as part of the dynamic traffic characteristics RTP HE
    Individually for each field in the dynamic traffic characteristics.

## Slide 5: Supporting Text from SA2 specs
23.501: "If UPF receives the PDRs with the Expedited Transfer Indication, it shall also detect "Expedited Transfer Indication" in the downlink packets "

## Slide 6: Summary
We should also study further how ETI is applicable to RTP streams. The text for this can be a CR to TR 26.822.
The text in green on slide 3 is generally agreeable, but there are concerns that we need to check with SA2. The only opportunity for that is in Fukuoka.
If dyn. traf. char. header is used for ETI, the question to use fixed header size vs. dynamic fields is still not agreeable.
We still need to finalize the control plane signalling but it may be dependent on our decision for the UP.