## Slide 1: Proposed new study on 3D Gaussian Splatting on 6G (FS_3DGS_6G_MED)
S4-251569
3GPP SA4#133-e
A.I. 17.2

## Slide 2: Overview of 3D Gaussian Splats
What it is
  A 3D point with a gaussian distribution
    A mean: a center point
    A variance: spread and size
What it is not
  A full 3D model (no explicit description of surfaces like meshes
Its representation format
  Consisting of a set of parameters describing the gaussian distribution
    Position, scale, orientation, color, transparency
spherical harmonics
defining the color depending on the orientation
(48 parameters)

## Slide 3: Why 3DGS matters
Photorealistic representation of 3D objects and scenes
  Unlike dense point clouds, the gaussian splats have a volume and overlap with each others (removing the holes in the rendering presentation)
  Support natively transparency (challenging in conventional 3D formats), suitable for non-solid assets (fire, cloud...)
Rendering simplification
  No need for polygon rasterizing, instead 2D blobs (projections) can be used with GPU techniques (optimized shaders)
  Low memory requirement compared to other 3D representation formats

## Slide 4: The study objectives (1/3)
Identify use cases for mobile devices that demonstrate the practical applications of 3DGS representation formats. Based on feasibility, a potential subset of the collected use cases will be prioritized, and the remainder of the study will focus on this selected subset.
Analyze state-of the-art 3DGS representation formats, including:
  Identify the relevance and complexity of the parameters of the primitives. This includes the size of the 3DGS model and the associated processing requirements, also considering expected evolution in size and complexity reductions and tradeoffs.
  Identify quality aspects related to 3DGS representations, including subjective and objective quality of reconstructions derived from these representations and define related quality parameters and evaluation criteria.
  Determine one or a few relevant 3DGS representation formats.
  If time permits investigated alternative representation formats with lower priority, and sufficient evidence needs be provided to demonstrate their efficiency.

## Slide 5: The study objectives (2/3)
Study and document content generation aspects including:
  Optical, computational and AI-based workflows on devices to support the generation of 3DGS representations
  Analysis of network-based processing and identification of the advantages and drawbacks of Edge/Cloud operations for generating 3DGS representations
Study and document rendering workflow aspects including:
  Device requirements and workflow to support 3DGS representation mapping to different device displays (e.g., 2D screens displays, light-field displays, HMDs, etc.).
  Consistent end-to-end quality across different capturing and rendering systems for 3DGS representations.
Map the relevant workflows to 3GPP services (such as messaging) and identify the media requirements to support the scenario.

## Slide 6: The study objectives (2/3)
Identify the target bitrates and potential traffic characteristics of 3DGS representations for the selected scenarios and investigate the associated compression aspects.
Identify needs and requirements for a potentially suitable standardization process, including data sets, training models, test data, etc. for 3DGS representations.
In parallel to the above objectives: Develop an end-to-end reference implementation for content delivery, covering the entire pipeline from content creation on a server or on the UE and, through compression, transmission, to rendering on a mobile device platform. This work could serve as a basis for future developments and be used in the evaluations carried out during this study.

## Slide 7: Additional information
  Preliminary work plan
    See attachment and next slide
  Anticipated normative work
    Provision of 3DGS support in Rel-21 for the most straightforward use cases (e.g., 3D messaging)
  Any intent to provide corresponding implementations
    Committed to contribute to a reference implementation of a 3DGS renderer on mobile platforms. Also expect contributions on the 3DGS content generation.
    3GPP System integration may rely on a Market Representation Partner (MRP) such as 5G-MAG
  Expected SA approval date
    September 2025 (Package 1) due to the amount of work and the potential coordination with MPEG.
  Indication of 5GA or 6G topic
    6G topic due to normative work only in release 21.
  Expected SWG(s)
    Primarily in VIDEO SWG. Joint sessions may be required when addressing the system aspects.
As requested in S4-251180 for new Rel-20 work proposal

## Slide 8: Preliminary work plan
2025 |  |  |  |  |  |  |  | 2026 |  |  |  |  |  |  |  |  |  |  |  | 2027 |  |  |  |  | 
May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Jan | Feb | Mar | Apr | May | Jun
#132 |  | #133-e |  |  |  | #134 |  |  | #135 |  | #135-e | #136 |  |  | #137e |  | #137e-b | #138 |  |  | #139 |  | #139e | #140 | 
SID
FS_3DGS-MED
Use cases
Mobile player
Rendering
Content generation
Traffic characteristics
Representation format
System integration
Capture
2. Representation
format
1. Use cases
3. Content generation
4. Rendering workflow
5. Workflow and 3GPP service
8. Reference implementation
5. Traffic characteristics
7. Standardization process
Standardization
3GPP services

## Slide 9: Thank you
Julien Ricard