## Slide 1: OMAF: Omnidirectional Media Application Format
Ye-Kui Wang
Director, Technical Standards
INCITS L3 Tutorial
August 15, 2016, Mountain View, CA, USA

## Slide 2
Basic framework of VR
VR related standardization activities
OMAF: when, who, what
OMAF architecture
Projection mappings in OMAF WD
VR signalling in ISO base media file format (ISOBMFF) and DASH
Viewport dependent VR video processing
Outline

## Slide 3: Basic framework of VR
There can different media formats (codec and metadata), and different signaling and transmission protocols
There can be different camera settings, with different optical parameters
What is rendered needs to be immersive to the user:
Visual: high pixel quantity and quality, broad FOV, stereoscopic display
Sound: high resolution audio, 3D surround sound
Intuitive interactions: minimal latency, natural UI, precise motion tracking
There can be different stitching and projection mapping algorithms
There can be different video codecs and different encoding schemes

## Slide 4: VR related standardization activities
MPEG has the following standardization activities related to VR
  OMAF, file formats, DASH, CICP
  Study of projection mappings’ impact on video coding efficiency by JVET
  Point cloud, light field, free viewport TV
  3D audio AR/VR extensions, 3D audio for 360o video, audio wave field
  MPEG media transport (MMT)
  MPEG-V media context and control, media orchestration, scene description and application engine, and media wearable
Other SDOs that also have some VR standardization activities
  3GPP, DVB, DECE, DASH-IF, W3C
  ITU-T- starting a new Question on Immersive Live Experience (ILE)
  The VR Interest Group – planning for a VR Forum
  The VR society (part of the Advanced Imaging Society)
  The Immersive Technology Alliance

## Slide 5: OMAF: when, who, what

## Slide 6: OMAF – when
Will probably be the first industry standard on virtual reality (VR)
MPEG started looking at VR and started the OMAF project in Oct. 2015
Technical proposals started in Feb. 2016
First working draft (WD) as an output of the Jun. 2016 MPEG meeting
Tentative plan: CD after the Oct. 2016 MPEG meeting, FDIS late 2017

## Slide 7: OMAF – who
Initiated mainly by Samsung
Early participants include Samsung, Nokia, Qualcomm, LG, and currently mostly driven by these companies
Other companies that attended relevant sessions (OMAF, FF, and DASH) as I remember include MediaTek, Huawei, Intel, Apple, Canon, Broadcom, Sharp, Dolby, Technicolor, Fraunhofer, Ricoh, InterDigital, TNO, Bitmovin, OwlReality

## Slide 8: OMAF – what
The focus of the first version of OMAF would be 360o video and associated audio
The scope of OMAF
  Projection mappings
  File format encapsulation and metadata signalling
    Extensions to ISO base media file format (ISOBMFF) needed
  DASH encapsulation and metadata signalling
    Extensions to DASH needed
  Codec and coding configurations
  Guidelines of viewport dependent VR media processing, based on either of the following
    Viewport dependent video encoding and decoding
    Viewport dependent projection mapping

## Slide 9: OMAF architecture
Capturing
Encoding
DASH media requesting and reception
Network
Head/eye tracking
Sphere stitching
Projection
File composing
B
A
D
C
E
DASH encapsulation
F
File parsing
Decoding
E’
F’
Rendering
D’
Stitching
M2
M1
G
G’
Streaming
A: Real-world scene
B: Multiple-sensors-captured video or audio
C: Sphere video
D/D’: Projected video
E/E’: Coded video or audio bitstream
F/F’: ISOBMFF file
G/G’: DASH media presentation
M1: Projection mapping etc. metadata
M2: Metadata info of current FOV
Formats to be standardized in OMAF: E/F/G, incl. signalling of M1 in F/G.
For audio, the entire stitching process is not needed, and D is the same as B.

## Slide 10: Projection mappings in OMAF WD
Value | geometry_type
0x00 | Reserved
0x01 | Sphere
0x02 | Squished Sphere
0x03 | Cylinder
0x04 | Platonic Solid
0x05 | Truncated Pyramid
0x06 | Segmented Sphere
0x07 | Direct Fisheye
0x08-0xFF | Reserved
Value | num_surface
0x00 | Reserved
0x01 | Cube (6 surfaces)
0x02 | Octahedron (8 surfaces)
0x03 | Icosahedrons (20 surfaces)
0x04-0xFF | Reserved
Number of surfaces of platonic solid
Most of these projection mappings have different variations, and some of them (type 4 and 5) can dynamically change over time!

## Slide 11
Sphere – equi-rectangular

## Slide 12
Squished sphere

## Slide 13
Cylinder

## Slide 14: Cube map
Left
Front
Up
Down
Right
Bottom
Notes: Could be moved to backup slides

## Slide 15
Octahedron
①
②
③
④
⑤
⑦
⑥
⑧
①
⑤
②
⑥
③
⑦
④
⑧

## Slide 16
Icosahedron
1
⑤
2
8
12
11
16
14
13
6
7
9
10
3
15
17
18
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
⑤
4
5
19
20

## Slide 17
Truncated pyramid
F
R
L
T
D
B
F
B
D
R
T
L

## Slide 18
Segmented sphere

## Slide 19
Direct fisheye

## Slide 20: VR signalling in ISOBMFF and DASH

## Slide 21: VR signalling in ISOBMFF
To indicate that one or more video tracks contain VR video/audio
To signal information needed for decoding, rendering, and whatever optimization

## Slide 22: A backward compatible VR signalling in ISOBMFF
Using a new box directly in a video track to contain the VR video information has a backward compatibility issue.
  A file player that does not recognize the box would just ignore it and play the video track as a normal video track and hence result in a weird presentation.
The trick to solve this problem is to use the post-decoder requirements mechanism in the ISOBMFF:
  The generic sample entry ‘resv’ is used to replace the original sample entry type.
  A Restricted Scheme Info box is added to the sample description, leaving all other boxes unmodified.
  The original sample entry type is stored within an Original Format box contained in the Restricted Scheme Info box.
  A new box is defined to contain the VR video metadata information and this new box is included in the Restricted Scheme Info box.

## Slide 23: Info needed for decoding, rendering, and optimization
The projection mapping used
  Equi-rectangular, cupe map, …
Video/audio codec used and their configurations
  Codec, profile, (tier), level
  Spatial resolution, frame rate, bit rate
  Tiled or not?
  Multi-layer? Simulcast?
  3D or not?
Metadata for optimization of transmission, decoding, and rendering

## Slide 24: VR signalling in DASH
To indicate that one or more video DASH adaptation sets or representations contain VR video
  Again, preferably in a backward compatible way, e.g., by defining a new EssentialProperty descriptor and/or a new DASH profile
To signal information needed for clients (and intelligent edge servers or proxies) to
  Choose and request an appropriate VR video representation at the beginning
  Adapt to viewport/FOV change and network condition change
  Info needed for decoding, rendering, and optimization

## Slide 25: Viewport dependent VR video processing

## Slide 26
At any moment, only a portion of the entire coded sphere video is rendered
For VR to be really immersive, bandwidth and processing complexity remain two of the biggest changes

## Slide 27: Viewport dependent video processing
To tackle the bandwidth and processing complexity challenges
To utilize the fact that only a part of entire encoded sphere video is rendered at any moment
Two areas can be played with to reduce needed bandwidth and to reduce video decoding complexity
  To play with (viewport dependent) video encoding, transmission, and decoding
  To play with a viewport dependent projection mapping scheme

## Slide 28: VR/360 video encoding and decoding schemes
The conventional approach
Simple Tiles based Partial Decoding (STPD)
ScaLable coding based Partial Decoding #1 (SLPD#1)
ScaLable coding based Partial Decoding #2 (SLPD#2)
SiMulcast coding based Partial Decoding #1 (SMPD#1)
SiMulcast coding based Partial Decoding #2 (SMPD#2)
A comparison of the approaches
Signalling and encapsulation of tiles based VR video bitstreams

## Slide 29: VR/360 video encoding and decoding – conventional
Each picture is in a format after a particular type of projection mapping, e.g., equi-rectangular or cube-map
The video sequence is coded as a single-layer bitstream, with TIP used
The entire bitstream is transmitted, decoded, and rendered
…
Temporal inter prediction (TIP)

## Slide 30: Simple Tiles based Partial Decoding (STPD)
Transmission and decoding
Temporal inter prediction (TIP)
…
Encoding and storage
…
The video sequence is coded as a single-layer bitstream, with TIP and motion-constrained tiles used
Only a part of bitstream (the minimum set of motion-constrained tiles covering the current viewport/FOV) is transmitted, decoded, and rendered
Compared to the conventional scheme:
  Lower decoding complexity (or higher resolution under the same decoding complexity)
  Lower transmission bandwidth
  Same encoding and storage costs
  The latency between user head turning and user seeing the new viewport is really problematic today

## Slide 31: ScaLable coding based Partial Decoding #1 (SLPD#1)
The video sequence is coded as a multi-layer scalable bitstream using SHVC, with both TIP and ILP used
Each Enhancement Layer (EL) is split into motion-constrained tiles
The Base Layer (BL) does not need to be split into independent areas
The BL can have less frequent random access points (RAPs) than an EL
Only part of an EL needs to be transmitted and decoded
Compared to the conventional scheme:
  Lower decoding complexity (or higher resolution under the same complexity)
  Lower transmission bandwidth
  Higher encoding and storage costs
Temporal inter prediction (TIP)
Inter-layer prediction (ILP)
…
…
Encoding and storage
Transmission and decoding
…
…

## Slide 32: ScaLable coding based Partial Decoding #2 (SLPD#2)
The video sequence is coded as a multi-layer scalable bitstream using SHVC, without TIP but with ILP used
Each Enhancement Layer (EL) is split into motion-constrained tiles
The Base Layer (BL) does not need to be split into independent areas, and still uses TIP
The BL does not need to have frequent RAPs, and an EL does not need to have RAPs at all
Only part of an EL needs to be transmitted and decoded
Compared to SLPD#1:
  Lower delay in showing high quality video in FOV
  Possibly higher transmission bandwidth (due to no use of TIP)
…
…
Encoding and storage
Transmission and decoding
…
…
Temporal inter prediction (TIP)
Inter-layer prediction (ILP)

## Slide 33: SiMulcast coding based Partial Decoding #1 (SMPD#1)
The video sequence is coded as multiple independent/simulcast bitstreams of different resolutions, with TIP but without ILP used
Each higher resolutions is split into motion-constrained tiles
The lowest resolution stream can have less RAPs than a stream of a higher resolution
Only part of a higher resolution stream needs to be transmitted and decoded
Compared to SLPD#1:
  Higher transmission bandwidth (due to no use of TIP)
…
…
Encoding and storage
Transmission and decoding
…
…
Temporal inter prediction (TIP)
Inter-layer prediction (ILP)

## Slide 34: SiMulcast coding based Partial Decoding #2 (SMPD#2)
The video sequence is coded as multiple independent/simulcast bitstreams of different resolutions, with TIP but without ILP used
Each of the resolutions is split into motion-constrained tiles
A lowest resolution stream should have the same frequency of RAPs as stream of a higher resolution
Only part of each resolution, including the lowest, needs to be transmitted and decoded
Compared to SMPD#1:
  No transmission/decoding of some part of the lowest resolution
  But requires more RAPs at the lowest resolutions
…
…
Encoding and storage
Transmission and decoding
…
…
Temporal inter prediction (TIP)
Inter-layer prediction (ILP)

## Slide 35: A comparison of the VR coding schemes
 | Conventional | STPD | SLPD#1 | SLPD#2 | SMPD#1 | SMPD#2
TIP | Y | Y | Y | N | Y | Y
ILP | n\a | n\a | Y | Y | N | N
Need to be tiled | N | Y | N for BL 1 Y for ELs | N for BL Y for ELs | N for BL Y for ELs | Y for both BL and ELs
Latency 2 acceptable | Y | N | Y | Y | Y | Y
RAP 3 | N | Y | N for BL Y for ELs | N for both BL and ELs | N for BL Y for ELs | Y for both BL and ELs
Clean viewport switching 4 | n\a | n\a | Y | Y | Y | N
1 For simplicity, the lowest resolution and other resolutions are denoted as BL and ELs, respectively, in the table, regardless of scalable or simulcast coding.
2 The latency is the latency between user turning head and (fully) seeing the new viewport.
3 The "RAP" row indicates whether frequent random access points are needed because of the latency between user turning head and (fully) seeing the new viewport (in addition to RAPs required by other purposes).
4 The "Clean viewport switching" row indicates, during viewport switching, whether the sender can immediately stop sending the tiles that cover the old viewport and that are from the highest resolution.

## Slide 36: SLPD#1 vs Conventional (on decoding complexity or VR video capability)
Assumptions for the comparison
  Two different spatial resolutions, the lower resolution being half in each direction of the higher resolution
  At any moment an FOV up to 180ox120o (corresponding to about 1/3 of the sphere surface) is displayed to the user, thus 1/3 of the EL in a two-layer case and the entire BL are transmitted, decoded and rendered for SLPD#1.
    In majority of cases, the FOV would be smaller, which will favor SLPD#1 more against Conventional
SLPD#1 vs Conventional
  For the same resolution of the projection-mapped video, the number of pixels to be decoded in SLPD#1 would be 1-(1/3+1/4) = 5/12 = 41.7% less
    This means significantly lower decoding capability requirement and less power consumption
  Or alternatively, for the same decoding capability, the resolution can be handled by SLPD#1 would be 12/7 = 171.4% of that for the conventional approach
    This for example would allow using of a video decoder with capability 4096x2160 to handle a VR video resolution of 7680x1920, which is 166.7% of 4096x2160.

## Slide 37: Preliminarily bandwidth comparison of SLPD#1 vs Conventional
Bethlehem |  | Scuba | 
Equi-rectangular | Cube map | Equi-rectangular | Cube map
- 19.7% | -23.9% | -27.9% | -31.8%
BD-rate reduction
Chart: Scuba (cube map)
| 41331.979200000002 | 20401.14 | 10682.771199999999 | 5854.5623999999998
Conventional | 39.4782 | 36.227 | 33.6459 | 31.3186
SHVC | 39.3982 | 36.1527 | 33.5638 | 31.2143
Chart: Scuba (equi-rectangular)
| 42838.033600000002 | 25466.5016 | 14321.510399999999 | 8132.7719999999999
Conventional | 40.958 | 37.5264 | 34.3863 | 31.8138
SHVC | 40.8414 | 37.4238 | 34.3014 | 31.6942
Chart: Bethlehem (cube map)
| 14078.053599999999 | 7550.5047999999997 | 4221.2528000000002 | 2455.7552000000001
Conventional | 42.4122 | 39.8276 | 37.4149 | 35.1238
SHVC | 42.273 | 39.6585 | 37.2182 | 34.9155
Chart: Bethlehem (equi-rectangular)
| 13110.6 | 8340.6592000000001 | 5006.26 | 2959.0360000000001
Conventional | 44.1669 | 41.0776 | 38.2219 | 35.7395
SHVC | 43.8995 | 40.8005 | 37.9452 | 35.4549
Scuba
Bethlehem

## Slide 38: Signalling and encapsulation of tiles based VR video bitstreams
File format
  Use the tiled storage of HEVC and layered HEVC (L-HEVC) in clause 10 of ISO/IEC 14496-15
  Preferably, the tile tracks should be used, each carrying one motion-constrained tile.
  The alternative is to use the tile region sample group mapping design, but would need the use lots of byte ranges, at access unit level, for streaming over DASH.
DASH
  Each track carrying one motion-constrained tile is encapsulated into one DASH representation.
  All the representations of different resolutions and carrying different regions are included in one adaptation set.
  The mapping of the spatial regions to the representations is signalled by at adaptation set level.

## Slide 39
Basic framework of VR
VR related standardization activities
OMAF: when, who, what
OMAF architecture
Projection mappings in OMAF WD
VR signalling in ISO base media file format (ISOBMFF) and DASH
Viewport dependent VR video processing
Outline