## Slide 1
Discussion Paper
IRP definition for LSA
RED Technologies
S5-163124
3GPP TSG|WG-5 Meeting #107
23-27 May 2016, Tenerife (Spain)

## Slide 2
Use cases summary
The following high-level use case are expected to be specified:
Use case 1 : LC initialization
Use case 2 : LSA spectrum resource availability change
Use case 3 : Network deployment update
Use case 4 : Loss of connectivity with the LR

## Slide 3
Architecture overview
Configure and
activate cells
Cells parameters
cells parameters
Constraints on cells parameters
LSRAI
2. Compute constraints on cells parameters
NM
LC
LR
Constraints on cells
parameters
Constraints accepted
LSA-1
Add / remove
/ modify cells

## Slide 4
Possible technical solution, using IRPs
Configure and
activate cells
Cells parameters
cells parameters
Constraints on cells parameters
LSRAI
2. Compute constraints on cells parameters
NM (IRP Manager)
LC (IRP Agent)
LR
Constraints on cells
parameters
Constraints accepted
LSA-1
Add / remove
/ modify cells
Each cell can be stored as a Management Object
Possible operations :
createMO / modifyMO / deleteMO
Possible operation:
Confirm(transactionID)
Possible operation:
Notify (transactionID, constraints)

## Slide 5
Possible functional split
The LC:
Acts as an IRP Agent
Stores a Management Object for each cell deployed.
Determines constraints on parameters.
LC
NM
IRP
Manager
IRP
Agent
The NM:
Acts as an IRP Manager
Creates / Modifiy/ Delete a Management Object in the LC for each cell deployed / updated / removed.
Receives a notification when new constraints on parameters are identified by the LC.
Configures cells according to the constraints on parameters.
Confirms to the LC when constraints on parameters provided to the NM are satisfied.

## Slide 6
Proposal
Agree on the high-level use cases
Discuss the proposed use of IRP, and agree on a way forward