## Slide 1: IMS Offline Charging Improvement – Use Cases SA5 #110 – Reno, USA November 14 - 18, 2016
S5-166284

## Slide 2: Problem
Today MNOs need to collect certain IMS offline charging information from IMS network elements that is not currently covered by any 3GPP standards
    No AVPs or corresponding CDR fields defined
  To do this we must create proprietary AVPs and corresponding CDR extensions and then negotiate with the network element vendors to implement these
    This affects not just the relevant CTF network element but also (often) downstream elements
  Very time consuming and expensive when MNOs must negotiate with vendors to accommodate these non-standardized charging parameters

## Slide 3: Today we must use proprietary AVPs and CDR fields to capture IMS offline charging information
Charging Trigger Function
(CTF)
Charging Data Function
(CDF)
Attribute Value Pairs
Accounting Request
Standardized AVPs
Proprietary AVPs
Charging Data Record (CDR)
Standardized Fields
Proprietary
Extensions
Mapping

## Slide 4: Solution Possibilities
We could overhaul the IMS Offline Charging specifications and standardize the missing parameters
    Big job, very time consuming, more development cost for vendors, lacks flexibility
    Could be a possible long term solution
  We could extend Service-Specific-Info AVP/CDR to arbitrary Network Elements
    SSI is a container created to handle the exact problem we are addressing here, but dealing only with Application Server parameters, not general network elements
    At SA5 #109 (San Francisco) some expressed a preference to keep SSI associated only with Application Servers
  Create a new container just like SSI but applicable to any Network Element
    Call it NSI (Network-Specific-Info)
    Simple solution – AVP with generic Data and Type fields plus corresponding CDR fields. MNO would provision data fields after deployment

## Slide 5: NSI would be analogous to SSI – a standardized “container” for MNOs to provision charging data that does not have a standardized AVP/CDR
Service-Specific-Info ::= <AVP Header: 1249>
[Service-Specific-Data]  AVP Code 863
UTF8 String
[Service-Specific-Type]  AVP Code 1247
Unsigned 32
Network-Specific-Info ::= <AVP Header: TBD>
[Network-Specific-Data]  AVP Code TBD
UTF8 String
[Network-Specific-Type]  AVP Code TBD
Unsigned 32

## Slide 6: Use Cases: What are some examples network elements (CTFs) and data that require proprietary ACRs/CRDs today?
Interfacing an Interconnect Carrier
    Network Element = IBCF
    The IBCF CDRs must identify the carrier in order to accomplish access charge verification or terminating access charging
    Today we must use a proprietary AVP/field (same for the rest of these examples)
    The IBCF is configured with the carrier access ID in the name of the adjacency component interfacing with a particular carrier. That adjacency name needs to be recorded in the CDR in order to identify the carrier involved
  Capturing the SIP Diversion Header
    Network Element = IBCF
    Necessary to identify when a call that traverses the IBCF has been forwarded
    Other examples of data we capture: Contact Header, Route Header, Proprietary Headers
  Capturing Disconnect Direction
    Network Element = IBCF
    Needed to identify whether a session was disconnected/rejected from the originating or terminating end, or was disconnected internally
    These CDRs are used extensively in our troubleshooting process
  Capturing Ingress/Egress Octets
    Network Element = IBCF
    Octets captured on each side of the IBCF for each media stream in a given session
    Current AVPs not sufficient for tracking at media type level (e.g., audio and video)

## Slide 7: Conclusion
Proposal: Define a new standardized AVP/CDR container that the MNO can provision with whatever IMS charging info is needed
    Call it “Network-Specific-Info”
    Exactly analogous to Service-Specific-Info but make it applicable to IBCF and other network elements (not just App Server)
This approach enables us to define containers that can be used to carry SIP headers and IMS charging information that has NOT been given a standard 3GPP defined AVP
This approach does NOT prevent future definition of new standard AVPs to carry this information, but it does provide an agile, near-term solution without requiring repeated vendor negotiations, development, testing, and deployment