## Slide 1: Managing 3GPP 5G networks using ONAP Zero-Touch Automation - Madrid - March 26-28, 2019
Jean-Michel CORNILY, Orange
On behalf of 3GPP / SA5

## Slide 2: Objectives
Provide a comprehensive solution for the Management and Orchestration of 3GPP 5G networks using ONAP
No gap, no overlap between ONAP and 3GPP

## Slide 3: 3GPP Structure

## Slide 4: 3GPP Releases
Rel-16 Study phase
Q2
Q3
Q4
2019
Q2
Q3
Q4
Q1
2020
Q1
Rel-16 Study and Normative phase
Rel-16 freeze
Rel-16 ASN.1
Rel-15 freeze (incl 5G SA)
Rel-15 late drop freeze
2018
Q1
2017
Q4
Rel-15 NSA (option-3) freeze
Rel-15 NSA (option-3) ASN.1
Rel-15 ASN.1 (incl 5G SA)
Rel-15 late drop ASN.1
“Early drop”
“Main drop”
“Late drop”

## Slide 5: 3GPP System
SA5 scope

## Slide 6: 3GPP 5G Management Concepts
Methodology to produce Technical Specifications
  Concepts, Use Cases, Requirements – Stage 1
  Protocol-neutral Information Model – Stage 2
  Protocol-specific Solution Set(s) – Stage 3
How?
Managing what?
 Management
Services
 Network Resource
Model

## Slide 7: 5G Network Resource Model
5G network may comprise:
Stand Alone / Non-Stand Alone
Single / Dual Connectivity
NG-RAN Non Split / 2-Split / 3-Split options
5G Core Network Service-Based Architecture
Network Slicing

## Slide 8: 5G Management Services
From a Reference Point-Based management architecture to a Service-Based Management Framework
Management Services (MnSs)
  Provisioning Services
    Provisioning services
    Provisioning data report services
  Fault Supervision MnSs
    Fault supervision data report services
    Fault supervision control services
  Performance Assurance MnSs
    Performance measurement job control services
    Performance data file reporting services
    Performance data streaming services

## Slide 9: Positioning ONAP wrt. 3GPP MnSs
3GPP Management
Services consumers
3GPP Management
Services producers
(e.g. VNFs, PNFs, EMS)
Management
Service
Service Interface
Management
Service
Service Interface
Management
Service
Service Interface
Management
Service
Service Interface
ONAP R3 (Casablanca) architecture

## Slide 10: ONAP DCAE collection framework
Aims at collecting all sorts of events from xNFs (but not only)
In ONAP R1 and R2:
  VES (VNF Event Stream) Collector, via REST / HTTPS / JSON API
  SNMP Trap Collector, via SNMP
In ONAP R3:
  Data File Collector, to support Bulk PM, to support 3GPP bulk data file collection
  VES-HV (High-Volume) Collector, to support Real-Time Performance Measurement (RTPM), using Google Protocol Buffer (GPB)

## Slide 11: How 3GPP will use ONAP DCAE Collectors
3GPP Performance Assurance services | Candidate consumers in ONAP R3 | Candidate 3GPP Rel-16 solution sets
Performance data file reporting services | VES JSON Collector (for FileReady notification) | Protocol: REST Payload: JSON
 | Data File Collector (for PM file upload) | Protocol: FTP File content: XML
Performance data streaming services | VES JSON Collector for low-medium volume PM | Protocol: REST Payload: JSON
 | HV Collector for real-time (less than 1 minute) high volume PM (TCP, GPB) | Protocol: TCP Payload: ASN.1 Binary (TBC)
3GPP Fault Supervision services | Candidate consumers in ONAP R3 | Candidate 3GPP Rel-16 solution sets
Fault supervision data report services | VES JSON Collector for alarm notifications under normal conditions | Protocol: REST Payload: JSON
 | HV Collector for alarm notifications under alarm flooding conditions | Protocol: TCP Payload: ASN.1 Binary (TBC)

## Slide 12: Collecting 5G network events
ONAP | 3GPP | Proposed action
DCAE Collector(s) as recipient(s) of any sorts of events from 5G xNFs. Address of DCAE Collector(s) configured at xNF instantiation time and/or later. | Based on Subscribe / Notify paradigm and filtering conditions. N-to-M relationship b/w notification emitters and recipients. | AI 3GPP: Specify a solution to model the association between 5G NRM IOC instances and the address(es) of ‘notification consumer(s)’, configurable via ‘NF Provisioning Management Service’.
Type of event | JSON VES Collectors’ address list | HV VES Collectors’ address list | Data File Collectors’ address list
‘fault’ | {VES Coll#1 IP@} |  | 
‘measurement’ | {VES Coll#1 IP@} | {HV Coll#1 IP@} | 
‘heartbeat’ | {VES Coll#1 IP@} |  | 
… |  |  | 

## Slide 13: Introducing ‘Fault3GPP’ as new type of 3GPP Specific Record (1/2)
To be introduced in
ONAP -
for 3GPP
purposes
Fault3GPP
3GPP alarm
notification
parameters
3GPP Specific Records

## Slide 14: Introducing ‘Fault3GPP’ as new type of 3GPP Specific Record (2/2)
3GPP alarm notification parameters
ONAP VES common event header fields
‘Fault3GPP’ fields

## Slide 15: 3GPP Fault Management operations
 | ONAP | 3GPP | Proposed action
Retrieving missing alarms | Not addressed by ONAP | getAlarmList () – used to deal with alarm loss. Two modes of operation: Synchronous mode: the list of missing alarms is returned synchronously with the operation Asynchronous mode: the list of missing alarms is returned via alarm notifications. In this mode of operation, the only information returned synchronously is the status of the operation. | AI ONAP: Introduce Use Case and operation getAlarmList to APPC API, where: APPC is consumer of getAlarmList() operation DCAE is consumer of alarm notifications Only asynchronous mode is supported
Acknowledging Alarms | Not addressed by ONAP | acknowledgeAlarms () – used to indicate that the activity to resolve the problem has started | AI ONAP: Introduce Use Case and operations to APPC API
Clearing Alarms | Not addressed by ONAP | clearAlarms () – used for clearing alarms | 
Setting comments | Not addressed by ONAP | setComments () - used to set comments to alarms | 

## Slide 16: Performance Assurance
 | ONAP | 3GPP | Proposed action
Control of Performance Management (e.g. measurement start time, end time, Granularity Period, Reporting Period, measurements to be collected, etc.) | Parameters are provisioned (as other xNF configuration parameters) at instantiation time and/or later | Based on PM job (createMeasurementJob (), stopMeasurementJob (), …) | AI 3GPP: Extend 5G Network Resource Model with Measurement Control classes / attributes, to represent PM control capabilities.

## Slide 17: Using new ‘Perf3GPP’ type of Technology Record for 3GPP PM data streaming
Introduced in
ONAP Dublin -
for 3GPP
purposes – see next slide
Fault3GPP
3GPP alarm
notification
parameters
3GPP Specific Records
Perf3GPP
3GPP PM
meas data

## Slide 18: Collecting 3GPP PM measurement data
Bulk PM data file
  VES Collector receives FileReady notification
  Data File Collector retrieves PM data file
PM data streaming
  VES Collector
    JSON schema for PM records
  HV Collector
    ASN.1
Same as here
shall be available here

## Slide 19: OA&M Data Communication Management
 | ONAP | 3GPP | Proposed action
Heartbeat | Used by xNFs to communicate information about their health | No equivalent in 5G (Rel-15) ‘Communication Surveillance’ IRP (Integration Reference Point) applies to pre-5G technologies. | AI 3GPP: define a new management service (consumer would be VES Collector)

## Slide 20: Provisioning Services
 | ONAP | 3GPP | Proposed action
CRUD operations | NETCONF / YANG as option | YANG NRM | AI 3GPP: Add NETCONF-based solution set for Provisioning Services.
CRUD notifications | Not supported in R3. Discussions in R4 context (UC ‘PNF plug-and-play’) | Supported (REST / JSON) | AI ONAP: Introduce ‘Config3GPP’ as new 3GPP Specific Record in VES API AI 3GPP: Specify a new REST JSON Solution Set for: objectCreationNotification objectDeletionNotification attributeValueChangeNotification

## Slide 21: 3GPP SA5 OpenAPI Specifications
Contained in annex of the 3GPP Technical Specification which specifies the corresponding MnS
Also stored as separate physical files, accessible at http://www.3gpp.org/ftp/Specs/2018-12/Rel-15/OpenAPI/
  TS 28xxx series
  .json files
  One file per Management Service
  Publicly available

## Slide 22: Some useful links
TS 28.530 – Management and orchestration; Concepts, use cases and requirements (http://www.3gpp.org/ftp//Specs/archive/28_series/28.530/)
TS 28.522 – Management and orchestration; Architecture framework (http://www.3gpp.org/ftp//Specs/archive/28_series/28.533/)
TS 28.541 – Management and orchestration; 5G Network Resource Model (NRM); Stage 2 and stage 3 (http://www.3gpp.org/ftp//Specs/archive/28_series/28.541/)
TS 28.532 – Management and orchestration; Generic management services (http://www.3gpp.org/ftp//Specs/archive/28_series/28.532/)
TS 28.545 - Management and orchestration; Fault Supervision (FS) (http://www.3gpp.org/ftp//Specs/archive/28_series/28.545/)
TS 28.550 – Management and orchestration; Performance assurance (http://www.3gpp.org/ftp//Specs/archive/28_series/28.550/)

## Slide 23: Thank you!