## Slide 1: Integrating 3GPP 5G management framework with ONAP Zero-Touch Automation - Madrid - March 26-28, 2019
Jean-Michel CORNILY, Orange
On behalf of 3GPP / SA5

## Slide 2: Objective / Expectation
Specify how to integrate 3GPP and ONAP for the Management and Orchestration of 3GPP 5G networks
ONAP and 3GPP shall:
  complement each other
  not overlap

## Slide 3: Content
3GPP in a nutshell
3GPP Management Framework
Integrating 3GPP Management Framework with ONAP
  Positioning
  Fault & Performance Management
    General
    FM
    PM
  Provisioning (Config. Management)
  Misc.
Useful links

## Slide 4: 3GPP Structure
3GPP in a nutshell
3GPP Management Framework
Integrating 3GPP Management Framework with ONAP

## Slide 5: 3GPP Releases
Rel-16 Study phase
Q2
Q3
Q4
2019
Q2
Q3
Q4
Q1
2020
Q1
Rel-16 Study and Normative phase
Rel-16 freeze
Rel-16 ASN.1
Rel-15 freeze (incl 5G SA)
Rel-15 late drop freeze
2018
Q1
2017
Q4
Rel-15 NSA (option-3) freeze
Rel-15 NSA (option-3) ASN.1
Rel-15 ASN.1 (incl 5G SA)
Rel-15 late drop ASN.1
“Early drop”
“Main drop”
“Late drop”
3GPP in a nutshell
3GPP Management Framework
Integrating 3GPP Management Framework with ONAP
To be checked, after SA#83, if there is a new version available

## Slide 6: 3GPP System
In SA5 scope
3GPP in a nutshell
3GPP Management Framework
Integrating 3GPP Management Framework with ONAP

## Slide 7: 3GPP 5G Management Concepts
Methodology to produce Technical Specifications
  Concepts, Use Cases, Requirements – Stage 1
  Protocol-neutral Information Model – Stage 2
  Protocol-specific Solution Set(s) (REST/JSON, YANG, etc.) – Stage 3
How?
Managing what?
 Management
Services
 Network Resource
Model
3GPP in a nutshell
3GPP Management Framework
Integrating 3GPP Management Framework with ONAP

## Slide 8: 5G Network Resource Model
5G network may comprise:
Stand Alone / Non-Stand Alone
Single / Dual Connectivity
NG-RAN Non Split / 2-Split / 3-Split options
5G Core Network Service-Based Architecture
Network Slicing
Examples taken from NG-RAN NRM
3GPP in a nutshell
3GPP Management Framework
Integrating 3GPP Management Framework with ONAP

## Slide 9: 5G Management Services
From a Reference Point-Based management architecture to a Service-Based Management Framework
Management Services (MnSs)
  Provisioning Services (CM)
    Provisioning services
    Provisioning data report services
  Fault Supervision MnSs
    Fault supervision data report services
    Fault supervision control services
  Performance Assurance MnSs
    Performance measurement job control services
    Performance data file reporting services
    Performance data streaming services
3GPP in a nutshell
3GPP Management Framework
Integrating 3GPP Management Framework with ONAP

## Slide 10: Positioning ONAP wrt. 3GPP MnSs
3GPP Management
Services consumers
3GPP MnS producers
(e.g. VNFs, PNFs, EMF)
Management
Service
Service Interface
Management
Service
Service Interface
Management
Service
Service Interface
Management
Service
Service Interface
ONAP R3 (Casablanca) architecture
3GPP in a nutshell
3GPP Management Framework
Integrating 3GPP Management Framework with ONAP
Positioning - Fault & Performance Management - Provisioning

## Slide 11: ONAP DCAE collection framework
Aims at collecting all sorts of events from xNFs (but not only)
In ONAP R1 and R2:
  VES (VNF Event Stream) Collector, via REST / HTTPS / JSON API
  SNMP Trap Collector, via SNMP
In ONAP R3:
  Data File Collector, to support Bulk PM, to support 3GPP bulk data file collection
  VES-HV (High-Volume) Collector, to support Real-Time Performance Measurement (RTPM), using Google Protocol Buffer (GPB)
3GPP in a nutshell
3GPP Management Framework
Integrating 3GPP Management Framework with ONAP
Positioning - Fault & Performance Management - Provisioning

## Slide 12: How 3GPP will adapt to ONAP DCAE Collectors
3GPP Performance Assurance services | Candidate consumers in ONAP R3 | Candidate 3GPP Rel-16 solution sets
Performance data file reporting services | VES JSON Collector (for FileReady notification) | Protocol: REST Payload: JSON
 | Data File Collector (for PM file upload) | Protocol: FTP File content: XML
Performance data streaming services | VES JSON Collector for low-medium volume PM | Protocol: REST Payload: JSON
 | HV Collector for real-time (less than 1 minute) high volume PM (TCP, GPB) | Protocol: TCP Payload: ASN.1 Binary (TBC)
3GPP Fault Supervision services | Candidate consumers in ONAP R3 | Candidate 3GPP Rel-16 solution sets
Fault supervision data report services | VES JSON Collector for alarm notifications under normal conditions | Protocol: REST Payload: JSON
 | HV Collector for alarm notifications under alarm flooding conditions | Protocol: TCP Payload: ASN.1 Binary (TBC)
3GPP in a nutshell
3GPP Management Framework
Integrating 3GPP Management Framework with ONAP
Positioning - Fault & Performance Management - Provisioning

## Slide 13: Subscribe vs. No Subscribe to 3GPP events
ONAP | 3GPP | Proposed action
DCAE Collectors as recipients of any sorts of events from 5G xNFs. Address of DCAE Collectors configured at xNF instantiation time and/or later. | Based on Subscribe / Notify paradigm and filtering conditions. N-to-M relationship b/w notification emitters and recipients. | AI 3GPP: Specify a solution to model the association between 5G NRM IOC instances and the address(es) of ‘notification consumers’, configurable via ‘NF Provisioning Management Service’.
Type of event | JSON VES Collectors’ address list | HV VES Collectors’ address list | Data File Collectors’ address list
‘fault’ | {VES Coll#1 IP@} |  | 
‘measurement’ | {VES Coll#1 IP@} | {HV Coll#1 IP@} | 
‘heartbeat’ | {VES Coll#1 IP@} |  | 
… |  |  | 
3GPP in a nutshell
3GPP Management Framework
Integrating 3GPP Management Framework with ONAP
Positioning - Fault & Performance Management - Provisioning

## Slide 14: Introducing ‘Fault3GPP’ as new type of Technology Specific Record
Fault3GPP
3GPP alarm
notification
parameters
3GPP Specific Records
3GPP in a nutshell
3GPP Management Framework
Integrating 3GPP Management Framework with ONAP
Positioning - Fault & Performance Management - Provisioning

## Slide 15: Defining JSON schema for ‘Fault3GPP’
3GPP in a nutshell
3GPP Management Framework
Integrating 3GPP Management Framework with ONAP
Positioning - Fault & Performance Management - Provisioning

## Slide 16: Fault Management operations
 | ONAP | 3GPP | Proposed action
Retrieving missing alarms | Not addressed by ONAP | getAlarmList () – used to deal with alarm loss. Two modes of operation: Synchronous mode: the list of missing alarms is returned synchronously with the operation Asynchronous mode: the list of missing alarms is returned via alarm notifications. In this mode of operation, the only information returned synchronously is the status of the operation. | AI ONAP: Introduce Use Case and operation getAlarmList to APPC API, where: APPC is consumer of 3GPP getAlarmList() operation DCAE is consumer of 3GPP alarm notifications Only asynchronous mode is supported
Acknowledging Alarms | Not addressed by ONAP | acknowledgeAlarms () – used to indicate that the activity to resolve the problem has started | AI ONAP: Introduce Use Case and operations to APPC API
Clearing Alarms | Not addressed by ONAP | clearAlarms () – used for clearing alarms | 
Setting comments | Not addressed by ONAP | setComments () - used to set comments to alarms | 
3GPP in a nutshell
3GPP Management Framework
Integrating 3GPP Management Framework with ONAP
Positioning - Fault & Performance Management - Provisioning

## Slide 17: OA&M Data Communication Management
 | ONAP | 3GPP | Proposed action
Heartbeat | Used by xNFs to communicate information about their health | No equivalent in 5G (Rel-15) ‘Communication Surveillance’ IRP (Integration Reference Point) applies to pre-5G technologies. | AI 3GPP: define a new Management Service (consumer would be VES Collector)
3GPP in a nutshell
3GPP Management Framework
Integrating 3GPP Management Framework with ONAP
Positioning - Fault & Performance Management - Provisioning

## Slide 18: Collecting 3GPP PM measurement data
Bulk PM data file
  VES Collector receives FileReady notification
  Data File Collector retrieves PM data file
  3GPP and ONAP aligned already
PM data streaming
  VES Collector
    JSON schema for PM records
  HV Collector
    ASN.1
Re. REST/JSON PM data streaming, 3GPP will define a new Solution Set and may reuse ONAP Dublin VES pmMeasResult events schema.
3GPP in a nutshell
3GPP Management Framework
Integrating 3GPP Management Framework with ONAP
Positioning - Fault & Performance Management - Provisioning

## Slide 19: Defining new ‘Perf3GPP’ as new type of Technology Specific Record for 3GPP PM data streaming
Fault3GPP
3GPP alarm
notification
parameters
3GPP Specific Records
Perf3GPP
3GPP PM
meas data
3GPP in a nutshell
3GPP Management Framework
Integrating 3GPP Management Framework with ONAP
Positioning - Fault & Performance Management - Provisioning

## Slide 20: Performance Management control
 | ONAP | 3GPP | Proposed action
Control of Performance Management (e.g. measurement start time, end time, Granularity Period, Reporting Period, measurements to be collected, etc.) | Parameters are provisioned (as other xNF configuration parameters) at instantiation time and/or later | Based on PM job (createMeasurementJob (), stopMeasurementJob (), …) | AI 3GPP (Ongoing): Extend 5G Network Resource Model with PM control classes / attributes.
3GPP in a nutshell
3GPP Management Framework
Integrating 3GPP Management Framework with ONAP
Positioning - Fault & Performance Management - Provisioning

## Slide 21: Provisioning Services
 | ONAP | 3GPP | Proposed action
CRUD operations | NETCONF / YANG as option | YANG NRM | AI 3GPP: Add NETCONF-based solution set for Provisioning Services.
CRUD notifications | Not supported in R3. | Supported (REST / JSON) | AI ONAP: Introduce ‘Config3GPP’ as new 3GPP Specific Record in VES API AI 3GPP: Specify a new REST JSON Solution Set for: objectCreationNotification () objectDeletionNotification () attributeValueChangeNotification () Working assumption: VES Collector would be the consumer of CRUD notifications.
3GPP in a nutshell
3GPP Management Framework
Integrating 3GPP Management Framework with ONAP
Positioning - Fault & Performance Management - Provisioning

## Slide 22: 3GPP SA5 OpenAPI Specifications
Contained in annex of the 3GPP Technical Specification which specifies the corresponding MnS
Also stored as separate physical files, accessible at http://www.3gpp.org/ftp/Specs/2018-12/Rel-15/OpenAPI/
  TS 28xxx series
  .json files
  One file per Management Service
  Publicly available
3GPP in a nutshell
3GPP Management Framework
Integrating 3GPP Management Framework with ONAP
Positioning - Fault & Performance Management - Provisioning
To be checked, after SA#83, if this has been approved

## Slide 23: Some useful links
TS 28.530 – Management and orchestration; Concepts, use cases and requirements (http://www.3gpp.org/ftp//Specs/archive/28_series/28.530/)
TS 28.522 – Management and orchestration; Architecture framework (http://www.3gpp.org/ftp//Specs/archive/28_series/28.533/)
TS 28.541 – Management and orchestration; 5G Network Resource Model (NRM); Stage 2 and stage 3 (http://www.3gpp.org/ftp//Specs/archive/28_series/28.541/)
TS 28.532 – Management and orchestration; Generic management services (http://www.3gpp.org/ftp//Specs/archive/28_series/28.532/)
TS 28.545 - Management and orchestration; Fault Supervision (FS) (http://www.3gpp.org/ftp//Specs/archive/28_series/28.545/)
TS 28.550 – Management and orchestration; Performance assurance (http://www.3gpp.org/ftp//Specs/archive/28_series/28.550/)
TR 28.890* - Management and orchestration; Study on integration of Open Network Automation Platform (ONAP) and 3GPP management for 5G networks (http://www.3gpp.org/ftp//Specs/archive/28_series/28.890/)
New Work Item Description
To be updated, after SA#83, with link to the new Work Item
* Completed in 03/2019

## Slide 24: Thank you!