## Slide 1: Discussion on management data analytics for 5G network and network slice in Rel-16 and Rel-17 Huawei

## Slide 2
3GPP SA5: MDAS related standardization in Rel-16 (TS 28.533, TR 28.861)
Finalize the architectural related discussion regarding the management data analytics service
Study the relation between the management data analytics, SON, management function and network function.
References: TS 28.533, TR 28.861
Figure: 4.6.1: Service based architecture for management data analytics
Figure A.7.1: MDAS provided at different levels
[TS 28.533]
[TS 28.533]
[TR 28.861]
Figure 4.1.5-1 Management Data Analytics Service and SON functions

## Slide 3
3GPP SA5: MDAS related standardization in Rel-16 (TS 28.861, TR 28.805)
Illustration of relation with SON functions:
These analytics services (i.e., MDAS) can be made available and consumed by other management and SON functions. [From TR 28.861]
SON functions may utilise the services provided by the management data analytics (i.e., MDAS) to conduct their functionalities and control actions. [From TR 28.861]
SON function collects the performance data …to identify the traffic patterns for the NSIs, and predict the demand for network resources per every NSI for a given time and location. This information is analysed, for example, with assistance of the MDAS [From TR 28.861]
Illustration of relation with service management functions:
For 5G network MDAS may collect and analyse the user QoE information. Service QoE of given CSI is an analytic result of user QoE information. [From TR 28.805]
Service quality assurance and optimization of the services… Analytics hosted by the MDAF may be utilized for processing of the network data to derive and analyze the performance indicators. [From TR 28.805]
MDA-Assisted network provisioning contributing to SLA assurance . [From TR 28.805]
The MDAS of the customer may assist for the conversion of resource capability into service capability, or the customer may request services and analysis from the MDAS of the NSaaS provider. . [From TR 28.805]
Solution for MDA-Assisted SLA assurance…MDA-Assisted network optimization [From TR 28.805]
References: TR 28.861, TR 28.805

## Slide 4
3GPP SA2: NWDAF standardization in Rel-16 (TS 23.288)
Figure 4.2-1: Data Collection architecture from any NF
Figure 4.2-2: Network Data Analytics Exposure architecture
  Illustration of TS 23.288:
  6 Procedures to Support Network Data Analytic
  6.2 Procedures for Data Collection
All available data encompass:
- OAM global NF data,
- behaviour data related to individual UEs or UE groups…
- other NF data available in the 5GC (e.g. NRF)
  6.3 Slice load level related network data analytics
  6.4 Observed Service experience related network data analytics
  6.5 NF load analytics
  6.6 Network Performance Analytics
  6.7 UE related analytics
    6.7.2 UE mobility analytics
    6.7.3 UE Communication Analytics
    6.7.4 Expected UE behavioural parameters related network data analytics
    6.7.5 Abnormal behaviour related network data analytics
  6.8 User Data Congestion Analytics
  6.9 Potential QoS Change analytics
References: TS 23.288

## Slide 5
3GPP SA2: New SID of eNA phase 2 in Rel-17 (SP-190557)
  Justification
    …In order to improve the NWDAF related work initiated in Rel-15 and Rel-16, it looks beneficial to further investigate solutions for supporting network automation leveraging 5GC information exposure and network data analytics.
  Objective
    …This study focuses on analytics for 5GC NFs with the target to support in their decision making, or in other way assist with applications, UE or session related analytics…
    Objective 1: objective is to study the potential enhancements and new scenarios for network data analytics, including:
      The remaining key issues from R16 (…KI#11: NWDAF-Assisted predictable network performance … KI#14: How to ensure that slice SLA is guaranteed…)
      Rel-16 NWDAF features enhancement: (…Enabling real-time or near real-time NWDAF communication…)
      New Use Cases/key issues: (NWDAF analytics exposure to applications for example, in Smart City applications Smart City applications, …Interaction between NWDAF and AI Model &Training Service…)
    Objective 2: NWDAF Deployment Options
      Multiple NWDAF Instances Deployment
      NWDAF and AI Model &Training Service Deployment
References: SP-190557 eNA phase 2

## Slide 6
3GPP RAN: RAN Centric data collection and utilization in Rel-16 (TR 37.816)
  Study on RAN-centric data collection and utilization for LTE and NR [TR 37.816]
RAN3 conclusions
The following SON features are recommended by RAN3 to be specified in normative phase:
- Capacity and Coverage Optimization
- PCI Selection
- Mobility Optimization
- Load Sharing and Load Balancing Optimization
- RACH Optimisation
- Energy Saving
Recommendations for each feature are described in the dedicated conclusion section for each use case.
RAN2 conclusions
MDT and L2 measurements are recommended by RAN2 to be specified in normative phase, detailed recommendations are described in the dedicated section for MDT and measurements.
References: TR 37.816

## Slide 7
3GPP RAN: RAN Centric data collection enhancement discussion in Rel-17 (SP-190575)
  Release 17 planning
  2. Work Areas with email discussion to start in Sept contd’
[RAN_datacollection_enh] (moderator: CMCC)
  Includes SON and MDT
  To start based on Release 16 scope and status (leftovers, etc…)
  Data collection to enable AI is part of this discussion
References: SP-190575 Report from RAN#84;
Source: RAN Chairman

## Slide 8
Proposal in SA5 (Rel-16 & Rel-17)
Propose a new Rel-17 SID in SA5 (to be finalized before Jun.2020):
Align the use case and scenario discussion with SA2/RAN on the data analytics
Investigate the coordination mechanism between management close loop and control close loop
Identify potential new scenarios which suit for management data analytics
Provide management solution to compliment the work with other related groups
WG | TS/TR number | Title | Rel-16 Status
SA2 | TS 23.288 | Architecture enhancements for 5G System (5GS) to support network data analytics services | Published
RAN3 | TR 37.816 | Study on RAN-centric data collection and utilization for LTE and NR | Under discussion
SA5 | TS 28.533 | Management and orchestration; Architecture framework | Under discussion
WG | TS/TR number | Title | For info at TSG# | For approval at TSG# | Rel-17 Status
SA2 | TBD (SID SP-190557) | R17 eNA Phase 2 | SA#86 Dec 2019 | SA#87 Mar 2020 | Rel-17 SID approved
RAN3 | TBD (Rel-17 Planning in SP-190575) | R17 RAN_datacollection_enh | TBD | TBD | Rel-17 work area with email discussion to start in Sep 2019
SA5 |  | MDA for 5G network and network slice | SA#87 Mar 2020 | SA#88 June 2020 | Rel-17 New proposal to SA5#126
Propose for Rel-16 work in SA5 (to be finalized before Dec.2019):
Align the architecture discussion with SA2 and update 28.533
Align the use case and scenario discussion with SA2 Rel-16 deliverables and provide management analytics information

## Slide 9
Thanks!