3GPP TSG-SA5 Meeting #130e 	S5-202399

# e-meeting, 20 April – 29 April 2020														revision of S5-202258

# Source:	Ericsson, Deutsche Telekom, Nokia

# Title:	Communication service assurance stage 2 solution

# Document for:	Approval

Agenda Item:	6.4.7

# 1	Decision/action requested

In this box give a very clear / short /concise statement of what is wanted.

# 2	References

[1]	3GPP TS 28.535: Management and orchestration; Management Services for Communication Service Assurance; Requirements

[2]	3GPP TS 28.541: Management and orchestration; 5G Network Resource Model (NRM); Stage 2 and stage 3 (Release 16)

[3]	3GPP TS 28.622: Telecommunication management; Generic Network Resource Model (NRM) Integration Reference Point (IRP); Information Service (IS) (Release 16)

# 3	Rationale

This contribution proposes to add text for closed loop assurance stage 2 solution.

The solution shown in Figure 1 describes a management service that can provide control services based on input such as goal, permissible deviation of the goal and other essential information, and reports the actual devation from the goal. The management service includes configuration (control) interface for the provisioning of the guidance to the assurance management service regarding policies and constraints to network resources before a control loop is active, for example changing the resource allocation in RAN by configuring the RRM policy. Both the management service and the control loop report the result of their actions.

Figure 2: Assurance management service

Figure 2: Assurance Control service

Figure 3: Assurance Control Loop

The assurance management service manages each control loop that is configured by the assurance control service. Each time a control loop is created, a run-time instance of an Assurance Control Loop is born and managed by the Assurance Management Service. Figure 1 shows how the Assurance Management Service interacts with information (observations) from the Mobile Network i.e. collection of performance measurements, alarms, MDT trace events and the provisioning of the mobile network resources in RAN and CN (NRM).

The Assurance Control Service is shown in Figure 2 is configured to lifecycle manage the instance of Assurance Control Loops shown in Figure 3. An instance of a control loop performs the following steps Monitor, Analyse, Decide, Execute. The goal is input to the loop and the loop execution effectiveness is reported as output. The control loop adjust the properties of a Managed Entity (NSI, NSSI etc..) to assure that the performance is of the controlled entity is within the bounderies of the goal.

# 4	Detailed proposal

First change

# 2	References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

-	References are either specific (identified by date of publication, edition number, version number, etc.) or non-specific.

-	For a specific reference, subsequent revisions do not apply.

-	For a non-specific reference, the latest version applies. In the case of a reference to a 3GPP document (including a GSM document), a non-specific reference implicitly refers to the latest version of that document in the same Release as the present document.

[1]	3GPP TR 21.905: "Vocabulary for 3GPP Specifications".

[2]	ETSI GS ZSM 002 V1.1.1 (2019-08): “Zero-touch network and Service Management (ZSM); Reference Architecture”

[3]	3GPP TS 28.550: "Management and orchestration; Performance assurance”

[4]	3GPP TS 28.545: "Management and orchestration; Fault Supervision (FS) "

[a]	3GPP TS 28.622: "Telecommunication management; Generic Network Resource Model (NRM) Integration Reference Point (IRP); Information Service (IS)".

[b]	3GPP TS 28.541: "Management and orchestration; 5G Network Resource Model (NRM); Stage 2 and stage 3"

[c]	3GPP TS 28.532: "Management and orchestration; Management services".

[d]		3GPP TS 32.302: "Telecommunication management; Configuration Management (CM); Notification Integration Reference Point (IRP); Information Service (IS)".

Second change

### 4.1.x	Model

#### 4.1.x.1 	Imported and associated information entities

##### 4.1.x.1.1 	Imported information entities and local labels

| Label reference | Local label |
| --- | --- |
| TS 28.622 [a], IOC, Top | Top |
| TS 28.622 [a], IOC, SubNetwork | SubNetwork |
| TS 28.622 [b], ProxyClass, ManagedEntity | ManagedEntity |
| TS 28.541 [b], dataType, ServiceProfile | ServiceProfile |
| TS 28.541 [b], dataType, SliceProfile | SliceProfile |

#### 4.1.x.2	Class diagram

#### 4.1.x.2.1	Relationships

Figure 4.1.x.2.1.1: Assurance management NRM fragment

#### 4.1.x.2.2	Inheritance

Figure 4.1.x.2.2.1: Assurance management inheritance relationships

#### 4.1.x.3	Class definitions

##### 4.1.x.3.1	AssuranceControlLoop

###### 4.1.x.3.1.1	Definition

This IOC represents the capabilities of a control loop, these include:

- to automatically adjust a ManagedEntity (for example a network slice) to meet the objective described in AssuranceControlLoopGoal

- to report the effectiveness of an AssuranceControlLoop

- state management of an AssuranceControlLoop

###### 4.1.x.3.1.2	Attributes

| Attribute name | Support Qualifier | isReadable | isWritable | isInvariant | isNotifyable |
| --- | --- | --- | --- | --- | --- |

Editor’s Note: attribute constraints are FFS

###### 4.1.x.3.1.3	Constraints

Editor’s Note: attribute constraints are FFS

###### 4.1.x.3.1.4	Notifications

The common notifications defined in clause 4.1.x.5 are valid for this IOC, without exceptions or additions.

##### 4.1.x.3.2	AssuranceControlLoopGoal <<ProxyClass>>

###### 4.1.x.3.2.1	Definition

| This IOC represents the <<dataType>> ServiceProfile and <<dataType>> SliceProfile, defined in network slice NRM in [b]. |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |

###### 4.1.x.3.2.2	Attributes

The attributes are defined in network slice NRM in [b].

###### 4.1.x.3.2.3	Attribute constraints

The attribute constraints are defined in network slice NRM in [b].

###### 4.1.x.3.2.3	Notifications

The notications of IOCs using the <<dataType>> ServiceProfile or <<dataType>> SliceProfile are defined in network slice NRM in [b].

#### 4.1.x.4	Attribute definitions

##### 4.1.x.4.1	Attribute properties

The following table defines the properties of attributes that are specified in the present document.

| Attribute Name | Documentation and Allowed Values | Properties |
| --- | --- | --- |
| Attribute related to role |  |  |

Editor’s Note: attribute definitions are FFS

##### 4.1.x.4.2	Constraints

Editor’s Note: attribute constraints are FFS

#### 4.1.x.5	Common notifications

##### 4.1.x.5.1 Alarm notifications

This clause presents a list of notifications, defined in TS 28.532 [c], that an MnS consumer may receive. The notification header attribute objectClass/objectInstance, defined in TS 32.302 [d], shall capture the DN of an instance of a class defined in the present document.

##### 4.1.x.5.2 Configuration notifications

This clause presents a list of notifications, defined in TS 28.532 [c], that an MnS consumer may receive. The notification header attribute objectClass/objectInstance, defined in TS 32.302 [d], shall capture the DN of an instance of a class defined in the present document.