3GPP TSG-SA5 Meeting #132e	S5-204245

e-meeting 17th 28th August 2020

# Source:	Huawei

# Title:	Add confidence indicator for MDAS analysis

# Document for:	Approval

Agenda Item:	6.6.3

# 1	Decision/action requested

The group is asked to approve the proposal.

# 2	References

[1]	3GPP TR 28.809 v0.4.0: “Study on enhancement of Management Data Analytics (MDA)”

# 3	Rationale

It is proposed that MDAS should report confidence in the analysis report, similar to the behaviour of NWDAF.

# 4	Detailed proposal

This contribution proposes to make the following changes in [1].

1st Change

## 6.99.x	Confidence indicator in analysis results

A consumer of MDAS should treat the results of Management Data Analytics with caution. A decision based on analytics should take into account the degree of confidence of the analysis result, especially in the case when multiple analysis results are based on different models or different source data.

Therefore it is proposed that the result of Management Data Analytics should contain an attribute which indicates the degree of confidence of the analysis.

End of changes