3GPP TSG-SA5 Meeting #132e 	S5-204476d1

# e-meeting 17th 28th August 2020

Title:	Reply LS from SA5 to GSMA on NG.116 support of different access types

Response to:	[S5-204012 / 5GJA13_117r4] LS on NG.116 support of different access types

Release:	Release 17

Work Item:	EMA5SLA

Source:	3GPP SA5

To:	GSMA 5GJA

Cc:	3GPP SA2

Contact Person:

#### Name:	Kai ZHANG

Tel. Number:

E-mail Address:	kai.zhangkai@huawei.com

Send any reply LS to:	3GPP Liaisons Coordinator, mailto:3GPPLiaison@etsi.org

Attachments:	none

1. Overall Description:

3GPP SA5 would like to thank GSMA 5GJA for their LS on NG.116 support of different access types.

To align with NG.116v2.0 in which the GST attribute "supportedAccessTech" has been removed, SA5 has deleted the obsolete attribute "supportedAccessTech" from 3GPP Network Resource Model (NRM) ServiceProfile.

SA5 has also introduced NB-IoT support in the ServiceProfile to support the GST attribute "NB-IoT Support" which describes whether NB-IoT is supported in the RAN in the network slice.

If the future versions of NG.116 (the current version is NG.116v3.0) provide additional clarity on which attributes are restricted to the 3GPP access networks only, 3GPP SA5 will be glad to be informed.

2. Actions:

To GSMA 5GJA:

SA5 respectfully requests GSMA 5GJA to take this information into account.

3. Date of Next TSG-SA WG5 Meetings:

SA5#133e	12 – 21 October 2020	Online

SA5#134e	16 - 25 November 2020	Online

# Comments

See comment in the email