## Slide 1
3GPP TSG SA WG5 #132e
August 17th - 28th 2020, Online
Source: | Samsung
Title: | GST Translation and Configuration
Document for: | Discussion
Agenda Item: | 6.5.5
Abstract of the contribution: This document discusses the handling of GST in network slice management including its translation into ServiceProfile, SliceProfile and configurable parameters for NFs.
S5-204347

## Slide 2: What we have now…
GST capture:
  All GST attributes should be captured in ServiceProfile
Serviceprofile
  Serviceprofile is the requirement for a service
Sliceprofile
  Sliceprofile is the requirement for a slice
Domain (CN, RAN, TN) Sliceprofile
  Domain sliceprofile holds the requirements for a Domain Sliceprofile
  Example: CN SliceProfile:- Number of Terminals
Configurable Parameters
  Managed Function configurable parameters
  Example: Number of Terminal per AMF.

## Slide 3: Additional Mechanisms to be defined
Categorization
  Differentiating ServiceProfile attributes among those which will results in configuration parameter with those which will not.
Translation
  Translation of ServiceProfile attributes into SliceProfile attributes. In presence of multiple SliceProfile, identifying which SliceProfile(s) will get the requirements.
  Defining the mechanism to convert appropriate SliceProfile attributes into configuration parameters including: identifying the existing methodology (e.g TAC, MTU) to which the attribute could map and configuring the entity with the appropriate parameter/requirement.
  The segregation of the requirements among the multiple instances of target entity in a particular slice.
Configuration
  Defining the mechanism to configure
Enforcement
  Defining the enforcement mechanism for all the attributes present in ServiceProfile/SliceProfile.

## Slide 4: Categorization

## Slide 5: GST Categorization
Categorizing GST attributes into two categories: Configurable and Non-configurable Attributes
  Configurable Attributes: Downlink throughput per network slice, Number of terminals, Maximum supported packet size etc.
  Non-configurable Attributes: Group communication support, Session and Service Continuity support, Supported device velocity, Area of Service etc.
Attribute Translation.
  Configurable Attributes will be translated into configuration parameter for NF.
  Non-configurable Attributes will be translated into slice subnet feature/capability.
Attribute Enforcement
  Configurable Attributes will be enforced at runtime by individual NF.
  Non-configurable Attributes will be enforced at slice provisioning by OSM (NSMF/NSSMF).
GST Attributes
Performance
Quality
Coverage
Feature
Configurable Attributes
Non-Configurable Attributes
Configurable Parameters
Network Function
configuration
enforcement
OAM
(NSMF/NSSMF)
enforcement

## Slide 6: GST Categorization (Contd…)

## Slide 7: Translation

## Slide 8: GST Translation
GST to ServiceProfile Translation
  All GST attribute should be captured in the SeviceProfile
ServiceProfile to SliceProfile Translation
  All ServiceProfile attribute should be captured in one or multiple SliceProfile. This is because a slice-subnet (root NSSI) is a reflection of the slice itself. Following are some examples.
    Attribute “Radio spectrum” will be translated into RAN-SliceProfile only.
    Attribute “Number of terminals” will be translated into CN-SliceProfile only.
    Attribute “Isolation” will be translated into all CN-SliceProfile, RAN-SliceProfile and TN-SliceProfile.
SliceProfile to Configurable Parameter Translation
  Not all SliceProfile attribute will be translated into configurable parameter. Following are some examples
    Attribute “Number of terminals” will be translated into “maxNumberofUE” per slice for AMF.
    Attribute “Downlink throughput per network slice: maximum” will be translated into “maxDlThptPerSlice” for UPF.

## Slide 9: ServiceProfile to SliceProfileTranslation
Root-SliceProfile
Area of Service
energyEfficiency
Isolation
MC Support
User Mgmt Open
dLThptPerSlice
Number of terminals
Deterministic comm.
Radio spectrum
…
CN-SliceProfile
Area of Service
energyEfficiency
Isolation
MC Support
User Mgmt Open
dLThptPerSlice
Number of terminals
Deterministic comm
Radio spectrum
…
RAN-SliceProfile
Area of Service
energyEfficiency
Isolation
MC Support
User Mgmt Open
dLThptPerSlice
Number of terminals
Deterministic comm.
Radio spectrum
…
ServiceProfile
Area of Service
energyEfficiency
Isolation
MC Support
User Mgmt Open
dLThptPerSlice
Number of terminals
Deterministic comm.
Radio spectrum
…
TN-SliceProfile
Area of Service
energyEfficiency
Isolation
MC Support
User Mgmt Open
dLThptPerSlice
Number of terminals
Deterministic comm
Radio spectrum
…
Configurable Parameters
maxNumberofUE
maxNumofPDUSessionPerSlice
minDlThptPerSlice
minUlThptPerSlice
maxDlThptPerSlice
…
Configurable Parameters
minDlThptPerSlice
minUlThptPerSlice
maxDlThptPerUe
maxULThptPerUe
…
Note: The list of attributes is not show as exhaustive list for the sake of brevity

## Slide 10: SliceProfile to Configurable Parameter Translation
GST Attributes | ServiceProfile Attribute | SliceProfile Attribute | Configurable Parameter | Configured/Enforcing Entity IOC
Number of terminals | maxNumberofUE | maxNumberofUE | maxNumberofUE | 5GC Function
Number of connections | maxNumberofConns | maxNumofPDUSessionPerSlice | maxNumofPDUSessionPerSlice | 5GC Function
Downlink throughput per network slice: guaranteed | minDlThptPerSlice | minDlThptPerSlice | minDlThptPerSlice | 5GS UP Function
Uplink throughput per network slice: guaranteed | uLThptPerSlice | minUlThptPerSlice | minUlThptPerSlice | 5GS UP Function
Downlink throughput per network slice: maximum | dLThptPerSlice | maxDlThptPerSlice | maxDlThptPerSlice | 5GC Functions
Uplink throughput per network slice: maximum | uLThptPerSlice | maxUlThptPerSlice | maxUlThptPerSlice | 5GC Functions
Simultaneous use of the network slice | sliceSimultaneousUse | sliceSimultaneousUse | sliceSimultaneousUse | 5GC Function
Downlink throughput per UE | dLThptPerUe | maxDlThptPerUe | maxDlThptPerUe | 5GS UP Function
Uplink throughput per UE | uLThptPerUe | maxULThptPerUe | maxULThptPerUe | 5GS UP Function
Maximum supported packet size | maxPktSize | maxMTUSize | maxMTUSize | 5GC Functions

## Slide 11: Configuration

## Slide 12: Configuration based on Traffic Projections
MDAS assisted division of available Quota.
  Traffic analytics report from MDAS can be used to segregate available quota among different instances of a NF present in a slice.
    For example, MDAS can provide total number of projected terminal or subscription for each NF instance in the slice. Based on the projections the total available quota can be divided among the multiple NF instances in the slice. The NF instance serving more users or require to serve more users in future will have more quota then other NF instances in the slice.
Provisioning of Configurable Parameter
  NRM shall enable capturing GST requirements/restrictions for appropriate NFs.
  Generic provisioning management service should be used for provisioning.

## Slide 13: Enforcement

## Slide 14: Configurable Attribute Enforcement
Configurable Attributes
  Enforcement will be done by NF at the run time. The details of enforcement procedure is out-of-scope for SA5.
  The initial configuration can be changed any time based on measurement and KPIs, if required.

## Slide 15: Non-Configurable Attribute Enforcement
Non-configurable attributes
  Enforcement will be done by NSMS/NSSMS at the time of Slice Provisioning. The Slice subnet will be allocated only if it can satisfy the requirements provided in SliceProfile.
  The available slice-subnet inventory need to be maintained with respect to support for each Non-configurable Attribute.

## Slide 16: For Endorsement
The group is requested to endorse the following
  Having an ANNEX to define the configurable parameters resulting from the SliceProfile translations. [S5-204379]
  To document configurable parameters as part of 5G NRM.
    Either S-NSSAI <<dataType> can include all configurable parameters [S5-204359] Or,
    sNSSAIList can be replaced with sNSSAIInfo containing S-NSSAI and configurable parameters [S5-204364]
  To expand SliceProfile to get attributes from ServiceProfile
    Either respective SliceProfile for CN and RAN should be defined with appropriate attributes from ServiceProfile for each [S5-204348] Or,
    All ServiceProfile attributes will go into SliceProfile, [S5-204350]

## Slide 17
Thanks

## Slide 18: Back-up

## Slide 19: Enforcement of Configurable Attributes/Parameters

## Slide 20: Enforcement: Downlink throughput per network slice.Maximum
Enforcement of “Uplink throughput per network slice.Maximum” will be done in the same way and it is not shown for brevity.

## Slide 21: Enforcement: Downlink throughput per network slice.Guaranteed
Enforcement of “Uplink throughput per network slice.Guaranteed” will be done in the same way and it is not shown for brevity.

## Slide 22: Enforcement: Number of terminals

## Slide 23: Enforcement: Number of connections

## Slide 24: Enforcement: Downlink throughput per UE
It is expected that Slice-AMBR will be configured as another attribute per S-NSSAI in Slice Selection Information - indicating per-UE-per-Slice maximum throughput allowed for the UE (across all its PDU Sessions belonging to that slice). The Slice-AMBER will include both Uplink and Downlink throughput

## Slide 25: Enforcement: Maximum supported packet size

## Slide 26: Enforcement: Simultaneous use of the network slice

## Slide 27: Enforcement of Non-Configurable Attributes/Parameters

## Slide 28: Enforcement: Non-Configurable Attributes