3GPP TSG SA WG5 (Telecom Management) Meeting #133e 	S5-205199

# e-meeting 12th - 21th October 2020

# Source:	SA5 Vice Chair (Huawei), SA5 Chair

# Title:	Rel-16/Rel-17 5G management OAM Stage2 and Stage3 Mapping Status

# Document for:	Discussion and Endorsement

# Agenda Item:	6.1

# 1	Decision/action requested

The group is asked to discuss and endorse.

# 2	References

[1]	3GPP TS 28.532

[2]	3GPP TS 28.550

[3]	3GPP TS 28.541

[4]	3GPP TS 28.313

[5]	3GPP TS 28.622/623

# 3	Rationale

This contribution is targeted to address the following action item:

| 131e.1 | How to handle the alignment of stage 2 and stage 3. | Rel-16 | Leaders |
| --- | --- | --- | --- |

The following diagram illustrates the SA5 provided management services and the management service components categorized by different features.

This contribution provides an overview of current status of Rel-16 stage2 and stage3 alignment.

# 4	Detailed proposal

The following text show the current stage 2 and stage 3 status according to different management services. If the group agrees on the content, it’s proposed to capture this information in SA5 specification.

# Stage 2 / Stage 3 mapping status

Note: All the names in () next to each TS indicate the responsible expert to coordinate and check that all the related stage 3 code is provided.

### A.1 Tradition operational MnS and model driven MnS

Note: Add description to show the difference between the two MnS.

- The operational MnS approach uses the corresponding operation to compose a MnS.

- The model driven MnS approach uses the combination of CRUD opeation and the related models to compose a MnS.

### A.2 Details of stage 2 and stage 3 mapping information

A.2.1 Provisioning Management:

Introduction: Provision Management only adopts Model-driven approach

| Management Service Component A | RestFul (YAML) | Netconf |
| --- | --- | --- |
| CRUD Operation (createMOI/ getMOIAttributes/ modifyMOIAttributes/ deleteMOI) | TS 28.532 (Olaf) | TS 28.532 (Balazs) |

Gaps: Completed stage 3 solution sets for both RestFul and Netconf.

| Management Service Component A | RestFul (YAML) |
| --- | --- |
| Notification (notifyMOICreation/ notifyMOIDeletion/ notifyMOIAttributeValueChanges/ notifyEvent/ notifyMOIChanges) | TS 28.532 (Olaf) |

Gaps: Completed stage 3 solution sets for RestFul.

| Management Service Component B | YAML | YANG | XML |
| --- | --- | --- | --- |
| Generic NRM (generic network resource model) | TS 28.623 (Ping Jing) | TS 28.623 (Balazs) | TS 28.623(is it completed?) |
| NR NRM | TS 28.541 (Xu Ruiyue) | TS 28.541(Balazs) | TS 28.541(?) |
| 5GC NRM | TS 28.541 (Ping Jing) | TS 28.541(Balazs) | TS 28.541(?) |
| Network Slice | TS 28.541 (Xu Ruiyue) | Not defined | TS 28.541(?) |

Gaps:

Stage 3 YAML:

- Completed stage 3 solution sets for Generic NRM YAML.

- NR NRM/5GC NRM/network Slice need to be checked, including the IOC and the corresponding attributes. Actions for (Xu Rui yue/ Ping Jing) to check.

Stage 3 YANG:

- Generic NRM/NR NRM/5GC NRM need to be checked, including the IOC and the corresponding attributes. Actions for (Balazs) to check.

- Stage 3 XML: TBD

A.2.2 Fault Supervision:

Introduction: Fault supervision includes fault management control and fault management notification.

- Fault management control: So far two alternative implementions are captured in SA5 specifications which are model driven approach and operation approach.

- Fault management notification: Only operation approach is captured in SA5 specifications.

A.2.2.1 Fault management control (model-driven approach):

| Management Service Component A | RestFul (YAML) | Netconf |
| --- | --- | --- |
| CRUD Operation (see A.2.1 Provisioning Management) | TS 28.532 | TS 28.532 |

Gaps: see A.2.1

| Management Service Component B | YAML | YANG | XML |
| --- | --- | --- | --- |
| Generic NRM (FMControl) | TS 28.623 (Olaf) | TS 28.623 (Balazs) | TS 28.623 (?) |

Gaps:

Stage 3 YAML:

- Completed YAML stage 3 solution sets.

- Stage 3 YANG:

- Need to be checked (Balazs)

- Stage 3 XML: TBD

A.2.2.2 Fault management control (operation approach):

| Management Service Component A | RestFul (YAML) |
| --- | --- |
| subscribe/unsubscribe/getAlarmList/getAlarmCount/ setComment/ acknowledgeAlarms/unacknowledgeAlarms/clearAlarms/ | TS 28.532 (Olaf) |

Gaps:

Completed Restful stage 3 solution sets.

A.2.2.3 Fault management notification (operation approach):

| Management Service Component A | RestFul (YAML) |
| --- | --- |
| notifyNewAlarm/notifyChangedAlarm/notifyAlarmListRebuilt/ notifyCorrelatedNotificationChanged/notifyClearedAlarm/notifyAckStateChanged/notifyComments/notifyPotentialFaultyAlarmList/notifyChangedAlarmGeneral | TS 28.532 (Olaf) |

Gaps:

Completed Restful stage 3 solution sets.

A.2.3 Performance assurance:

Introduction: Performance assurance includes performance management control, performance threshold control, performance streaming and performance data file reporting.

- Performance management control: So far two alternative implementions are captured in SA5 specifications which are model driven approach and operation approach.

- Performance threshold control/performance streaming/performance data file reporting: adopts operation approach only.

A.2.3.1 Performance management control (model-driven approach)

| Management Service Component A | RestFul (YAML) | Netconf |
| --- | --- | --- |
| CRUD Operation (see A.2.1 Provisioning Management) | TS 28.532 | TS 28.532 |

Gaps: see A.2.1

| Management Service Component B | YAML | YANG | XML |
| --- | --- | --- | --- |
| Generic NRM (PerfMetricJob/ ThresholdMonitor) | TS 28.623 (Olaf) | TS 28.623 (Balazs) | TS 28.623 (?) |

Gaps:

Stage 3 YAML:

- Completed YAML stage 3 solution sets.

Stage 3 YANG:

- Completed YANG stage 3 solution sets.

- Stage 3 XML: TBD

A.2.3.2 Performance management control (operation approach):

| Management Service Component A | RestFul (YAML) |
| --- | --- |
| createMeasurementJob/stopMeasurementJob/ listMeasurementJobs | TS 28.550 (Yao Yizhi) |

Gaps: Completed YAML stage 3 solution sets.

3.4 Performance data reporting (operation approach):

| Management Service Component A | RestFul (YAML) |
| --- | --- |
| notifyThresholdCrossing | TS 28.532 (Yao Yizhi) |

Gaps: Completed YAML stage 3 solution sets.

A.2.3.5 Component B and C

| Management Service Component B (same as 1) | JSON | YANG | XML |
| --- | --- | --- | --- |
| Generic NRM (generic network resource model) | TS 28.623 | TS 28.623 | TS 28.623 |
| NR NRM | TS 28.541 | TS 28.541 | TS 28.541 |
| 5GC NRM | TS 28.541 | TS 28.541 | TS 28.541 |
| Network Slice | TS 28.541 | Not defined | TS 28.541 |

Gaps: see A.2.1

| Management Service Component C | ASN.1 | XML | GPB? |
| --- | --- | --- | --- |
| PM/KPI file format | TS 32.436 | TS 28.532 (Yao Yizhi) | Not defined in Rel-16 |
| PM/KPI stream format | TS 28.550 (Yao Yizhi) | Not defined in Rel-16 | Not defined in Rel-16 |

Gaps: Completed.

A.2.4 Heartbeat:

A.2.4.1 Heartbeat control (model-driven approach)

| Management Service Component A | RestFul (YAML) | Netconf |
| --- | --- | --- |
| CRUD Operation (see A.2.1 Provisioning Management) | TS 28.532 | TS 28.532 |

Gaps: see A.2.1

| Management Service Component B | YAML | YANG | XML |
| --- | --- | --- | --- |
| Generic NRM (HeartbeatControl) | TS 28.623 (Olaf) | TS 28.623 (Balazs) | TS 28.623 (?) |

Gaps:

Stage 3 YAML:

- Completed YAML stage 3 solution sets.

Stage 3 YANG:

- Completed YANG stage 3 solution sets.

- Stage 3 XML: TBD

A.2.4.2 Heartbeat notification (operation approach)

| Management Service Component A | RestFul (YAML) |
| --- | --- |
| notifyHeartbeat | TS 28.532 (Olaf) |

Gaps:tdoc for SA5#133e

A.2.5 Streaming data reporting service:

A.2.5.1 streaming control (operation approach):

| Management Service Component A | RestFul (YAML) |
| --- | --- |
| establishStreamingConnection / terminateStreamingConnection/ reportStreamData/ addStream /deleteStream/getStreamInfo/getConnectionInfo | TS 28.532 (Anatoly) |

Gaps: Completed YAML stage 3 solution sets.

A.2.6 File data reporting service:

A.2.6.1 file data reporting (operation approach):

| Management Service Component A | RestFul (YAML) |
| --- | --- |
| listAvailableFiles/notifyFileReady/ notifyFilePreparationError/subscribe/ unsubscribe/notifyThresholdCrossing | TS 28.532 (Yao Yizhi) |

Gaps: Completed YAML stage 3 solution sets.

A.2.7 Trace/MDT:

A.2.7.1 TraceControl NRM (model-driven approach)

| Management Service Component A | RestFul (YAML) | Netconf |
| --- | --- | --- |
| CRUD Operation (see A.2.1 Provisioning Management) | TS 28.532 | TS 28.532 |

Gaps: see A.2.1

| Management Service Component B | YAML | YANG | XML |
| --- | --- | --- | --- |
| Generic NRM (TraceJob) | TS 28.623 (Anatoly) | TS 28.623 (Balazs) | TS 28.623 (?) |

Gaps:

Stage 3 YAML:

- Completed YAML stage 3 solution sets.

Stage 3 YANG:

- Completed YANG stage 3 solution sets.

Stage 3 XML: TBD

| Management Service Component C | ASN.1 | XML | GPB |
| --- | --- | --- | --- |
| Trace/MDT file format | Not defined in Rel-16 | TS 32.423 (Anatoly) | Not defined in Rel-16 |
| Trace/MDT streaming format | Not defined in Rel-16 | Not defined in Rel-16 | TS 32.423 (XiaoMing Gao) |

Gaps:

Stage 3 ASN.1: both file format and streaming format are not defined in Rel-16

Stage 3 XML: streaming file format is not defined in Rel-16.

Stage 3 GPB: file format is not defined in Rel-16.

A.2.8 QoE:

QoE only applies to UMTS/LTE in Rel-16.

| Management Service Component C | ASN.1 | XML | GPB |
| --- | --- | --- | --- |
| QoE file format |  |  |  |

Gaps: refer to SA4 specifications (TS 26.247/26.114).

A.2.9 SON:

A.2.9.1 SON control (model-driven approach)

| Management Service Component A | RestFul (YAML) | Netconf |
| --- | --- | --- |
| CRUD Operation (see A.2.1 Provisioning Management) | TS 28.532 | TS 28.532 |

Gaps: see A.2.1

| Management Service Component B | YAML | YANG | XML |
| --- | --- | --- | --- |
| SON NRM (PCI, MRO, RACH, ANR) | TS 28.313/28.541 (Joey Chou/Shixiaoli/Per?) | TS 28.313/28.541 (Joey Chou/Shixiaoli/Per?) | TS 28.541 (?) |

Gaps:

Completed YAML stage 3 solution sets?

Completed YANG stage 3 solution sets?

A.2.10 Energy Saving Management:

A.2.10.1 ES control (model-driven approach)

| Management Service Component A | RestFul (YAML) | Netconf |
| --- | --- | --- |
| CRUD Operation (see A.2.1 Provisioning Management) | TS 28.532 | TS 28.532 |

Gaps: see A.2.1

| Management Service Component B | YAML | YANG | XML |
| --- | --- | --- | --- |
| ES NRM | TS 28. 541 (Jean-Michel/Shixiaoli) | TS 28.541 (Jean-Michel/Shixiaoli/Balazs) | TS 28.541 (?) |

Proposal-3: Leaders recommendation: discontinue XML SS for ES NRM from Rel-16.

Gaps:

Stage 3 YAML:

- Completed YAML stage 3 solution sets.

Stage 3 YANG:

- Completed YANG stage 3 solution sets.

Stage 3 XML:

- Completed XML stage 3 solution sets.

A.2.11 COSLA:

| Management Service Component A | RestFul (YAML) | Netconf |
| --- | --- | --- |
| CRUD Operation (see A.2.1 Provisioning Management) | TS 28.532 | TS 28.532 |

Gaps: see A.2.1

| Management Service Component B | YAML | YANG |
| --- | --- | --- |
| COSLA NRM (AssuranceControlLoop/ AssuranceGoalStatus/ AssuranceControlLoopGoal/ ObservationTimePeriod) | TS 28. 536 (Jan) | ? |

Gaps:

A.2.12 Inventory Management:

| Management Service Component A | RestFul (YAML) | Netconf |
| --- | --- | --- |
| CRUD Operation (see A.2.1 Provisioning Management) | TS 28.532 | TS 28.532 |

Gaps: see A.2.1

| Management Service Component B | YAML | YANG |
| --- | --- | --- |
| Inventory NRM | TS 28.633(not complete) | TS 28.633(not complete) |

Gaps:

- The solution set for inventory NRM are not available for both YAML and YANG.

# Stage 2 / Stage 3 alignment principle

- Supported stage 3 SS types:

- The supported stage 3 SS types are YAML,YANG and XML for Management service component A and component B.

- The supported stage 3 SS types are support of one of the 3 types (ASN.1 or GPB or XML) for Management service component C.

- Rule for whether one or more SS has to be provided for every stage 2 item

For every Stage 2 item in a CR/pCR, it must be accompanied by one or more CRs/pCRs with the corresponding Stage 3 definition(s) for at least one of the 3 existing SS types (YAML , YANG and XML). All missing such Stage 3 definitions must be recorded in this living document.

| Management Service Component A | RestFul (YAML) | YANG | XML |
| --- | --- | --- | --- |
| ABC | X |  |  |

End