3GPP TSG SA WG5 Meeting 134-e 	TDoc S5-206064rev2

electronic meeting, online, 16th - 25th November 2020

# Source:	Huawei

# Title:	pCR 28.811 Add cross-operator concept

# Document for:	Approval

Agenda Item:	6.5.2

# 1	Decision/action requested

The group is asked to approve the proposal.

# 2	References

[1]	3GPP TR 28.811 v0.1.0: “Management and orchestration; Network Slice Management Enhancement”

# 3	Rationale

This contribution addresses the following Editor’s Note:

The study should clarify the meaning of “cross-operator network slice management” and use a better term if possible.

# 4	Detailed proposal

This contribution proposes to make the following changes in [1].

1st Change

# 1	Scope

The present document describes potential enhancements to network slice management.

The present document considers the following issues:

- The potential network slice information model and management service enhancements to support multi-operator network slice management use case.

- The potential new management capabilities to support end to end network slicing.

Editors’s Note: The study should clarify the meaning of “end to end network slicing” and use a better term if possible.

2nd Change

## 4.x	Multi-operator relationships in network slice management

Multi-operator network slice management refers to scenarios where multiple network operators are involved in providing a network slice.

The following figure is a subset of 28.530 [4] Figure 4.8.1, with focus on the relationship between the Communication Service Provider and Network Operator.

Figure 4.x.1: High-level model of roles

However, 28.530 [4] does not describe the fact that multiple Network Operators may be involved. The following figure considers another scenario where Network Operator A may source network resources from another Network Operator B.

Figure 4.x.3: Multi-operator scenario

End of changes

# Text boxes

Provider

Client

Provider

Client

Communication Service Customer

Communication Service Provider

Network Operator

Provider

Client

Communication Service Provider

Network Operator

Provider

Provider

Provider

Client

Provider

Client

Communication Service Customer

Communication Service Provider

Network
Operator 1

Network
Operator 2

Network
Operator n

Provider

Provider

Client

Client

Provider

Client

Communication Service Customer

Communication Service Provider

Network
Operator 1

Network
Operator 2

Provider

Provider

Client

Client

Provider

Client

Communication Service Customer

Communication Service Provider

Network
Operator 1

Network
Operator 2

Provider

Provider

Client

Client

Communication Service Provider

Network
Operator A

Network
Operator B