3GPP TSG SA WG5 Meeting 134-e		S5-206177

# electronic meeting, online, 16th - 25th November 2020

# Source:	China Mobile, Huawei

# Title:	pCR 28.100 Add definition for network and service management scenario types

# Document for:	Approval

Agenda Item:	6.4.1

# 1	Decision/action requested

The group is asked to discuss and approval.

# 2	References

[1]	3GPP draft TS 28.100: “Levels of autonomous network v0.1.0”.

[2]	3GPP TR 28.810: “Study on concept, requirements and solutions for levels of autonomous network v17.0.0”

# 3	Rationale

The following Editor’s note is described in clause 5.1 use case. In order to have common understanding, this contribution proposes to add concept for telecom network and communication service planning, deployment, maintenance and optimization which can be used in the following clauses in TS 28.100[1].

Editor's note: this clause will contain the typical management use cases corresponding to telecom network and communication service planning & designing, deployment, maintenance and optimization phases.

# 4	Detailed proposal

It proposes to make the following changes to TS 28.100[1].

1st Change

## 3.1	Terms

For the purposes of the present document, the terms given in 3GPP TR 21.905 [1] and the following apply. A term defined in the present document takes precedence over the definition of the same term, if any, in 3GPP TR 21.905 [1].

Autonomous Network: telecommunication system (including management system and network) with autonomy capabilities which is able to be governed by itself with minimal to no human intervention.

Autonomous Network Level: describes the level of autonomy capabilities in the autonomous network.

Network and Service Planning: processes of designing and making plans for new or enhanced network or service based on the business, market, product and customer service requirements.

Network and Service Deployment: processes of allocation, installation, configuration, activation and verfication of specific network and service.

Network and Service Maintenance: processes of monitoring, analysing and healing of the network and service issues.

Network and Service Optimization: processes of monitoring, analysing and optimizing the network and service performance.

End of changes