3GPP TSG SA WG5 Meeting 134-e		S5-206215

# electronic meeting, online, 16th - 25th November 2020

# Source:	Huawei, China Mobile

# Title:	Update Clause 4.1.3 Intent categorizes based on management scenario types

# Document for:	Approval

Agenda Item:	6.4.2

# 1	Decision/action requested

The group is asked to discuss and approval.

# 2	References

[1]	3GPP draft TS 28.312: “Management and orchestration; Intent driven management services for mobile networks v0.1.0”.

# 3	Rationale

In clause 4.1.3 Intent categorizes based on management scenario types, following Editor’s note is described. This contribution proposes to update clause 4.1.3 to address the following Editor’s note:

Editor’s Note: the detailed intent categorizes for different kinds of management scenario types need to be further discussed, for example, whether the Intent for network and service design/planning and Intent for network and service maintenance is needed.

# 4	Detailed proposal

It proposes to make the following changes to TS 28.312[1].

1st Change

### 4.1.3	Intent categorizes based on management scenario types

Different types of intents are applicable for different types of management scenarios.

- Intent for network and service design/planning:

- Intent for network and service deployment: Intent for network and service deployment enable consumer to express the network or service instance to be deployed. Examples of intent for network and service deployment are “Provisioning radio network in the specified area with specified frequency information, transport information, and radio information (e.g. range of PCI, Cell Id), network capacity and performance information” or “provisioning radio service in the specified area with certain service characteristics (e.g. SLS)”.

- Intent for network and service assurance: Intent for network and service assurance enable consumer to express intents for network and service assurance, which including the following two sub-groups:

  - Intent for network and service maintenance: Intent for network and service maintenance enable consumer to express the network and service status (e.g. performance, alarm, issue) to be monitored or the network and service issues to be addressed. Examples of intent for network and service maintenance are “Monitoring coverage performance in the specified area by geographic grid granularity” or “Addressing the certain weak coverage issues in specified area”.

  - Intent for network and service optimization: Intent for network and service optimization enable consumer to express the performance objectives of network and service to be improved. Examples of intent for network and service optimization are “Optimize radio network in the specified area with certain RAN UE throughput objectives (e.g. target average RAN UE DL throughput, target percentage of UE with the RAN UE DL throughout less than 5Mbps)” or “Optimize radio network in the specified area with certain coverage objectives (e.g. target coverage ratio, target average RSRP)”.

Editor’s Note: The Intent for network and service design/planning is FFS.

End of changes