## Slide 1: Why use YANG-Push in 3GPP? SA5#138e, 23 – 31 August, 2021
ERICSSON
for information

## Slide 2: Solution Sets
We have 2 solution sets OpenApi and YANG/Netconf
Solution sets include: NRM/Models, Operations, Notifications
Notifications
  General: Alarms, FileReady, Heartbeat, etc.
  DataChange
  Both can be handled, but focus here is on data change notifications

## Slide 3: Data Change Notifications for YANG
Currently in 28.532
  Stage 2 and stage 3 for OpenAPI
  No usable solution for YANG
    It is not possible to use current data change notifications for YANG because a lot of things are not specified
Proposal
  Use RFC8639, 8641 - YANG-Push
  It fulfills the 3GPP requirements
  It has good functionality
  It is ready in specifications, it is implemented in SW toolkits
  It is widely used in the Netconf world
  It spares extra work for implementers
  Something for YANG is absolutely needed

## Slide 4: Undefined Issues for YANG notifications in 28.532 today
A statement is needed that the notification content is based on the YANG model, not stage 2 or the OpenApi model even if the notification is encoded as an OpenApi message.
Path parameter issues:
For a manager using YANG models handling a managed element based on YANG models addressing YANG model content with a URI is possible but awkward.
How will the YANG keys be included in the URI in case of multiple keys?
Will keys specific to YANG e.g., idx for structured attributes be included?
Is the wrapper list for the datatype exist in the URI?
Is the attributes container included? It does not exist on stage 2.
In some cases, stage 2 attributes that are not defined as complex datatypes but really are structured, are mapped using containers. How is that represented in the path?
In case a value is added to an ordered list, how is it indicated whether it is inserted at the beginning, end or the middle of the list?
How is recursive containment encoded? In YANG it is mapped differently then in stage 2 or OpenApi. Will the DN follow the YANG or the stage 2 representations?

## Slide 5: Undefined Issues for YANG notifications in 28.532 today
Operation parameter issues:
Move is missing from the potential operations. In case of ordered lists, it is needed.
value parameter issues:
How is it encoded? XML like Netconf or JSON? For YANG XML is the trivial choice but is it our choice?
If JSON encoding is used, does it follow the YANG-JSON encoding RFC7951 or the OpenApi-JSON-Schema encoding? The latter would be a problem for managers. ORAN wants RFC7951. It needs to be studied what differences exist between the two JSON encodings
Will YANG default values be reported? They are used, but they are not part of e.g., a createMOI or deleteMOI operation

## Slide 6: Why is it a good idea to use YANG-Push ? It does what we need, it works
Can support all 3GPP requirements
It is ready, specified 95%
It is implemented in SW tools already, why do extra work?
It uses the same/similar encoding as Netconf operations
Based on HTTPS/Rest, supports Cloud Native Deployments, scalability, load-balancing

## Slide 7: Why is it a good idea to use YANG-Push ? It has useful features beyond current 3GPP
Fine-grained well defined data selection filter in subscription
Support CM notifications for any YANG model, e g IETF
  We already have some IETF models in 3GPP e.g., ietf-yang-library
  Other SDOs are considering more (ietf-interfaces, other transport)
May Aggregate changes during time period and report in single notification (optional to configure)
Reliability: Indication is provided if notifications are lost or incomplete
Overload protection:
  Dampening period (minimum period between notifications) helps avoid overload on both producer and consumer
  Suspend/Resume: Allows an overloaded producer to suspend a subscription and notify its consumers
Access control RFC8341
  Some of the readable data nodes in the model may be sensitive or vulnerable.
  Same access control used for operations and notifications

## Slide 8: Data Change Notification alternatives for YANG
Option1: YAML for everything – usable only for OpenAPI/YAML SS
Option2: YAML for notifications with embedded YANG based data, NtfSubscriptionControl IOC for configuring subscription
Option3: YANG-Push for notifications, extended NtfSubscriptionControl IOC for configuring subscription
Option4: YANG-Push for notifications, IETF YANG-Push model for configuring subscription
All options need specification work
Our preference is Option4, Option3, Option2
  (Option1 is not applicable for YANG)
Option4 and partly 3 are already implemented in SW tools and they give the best functionality

## Slide 9: Issues for YANG-Push in 3GPP
Why have 2 Data Notification methods
  Something is needed for YANG/Netconf
  As the data model is different solutions will be different anyway
YANG-Push is not based on the stage 1/2/3 methodology
  Neither is HTTP or REST or file transfer and we still use them
  It is infrastructure we should just use and not redefine
  Stage-1 requirements could be defined
YANG-Push has its own Subscription model
  Proposal: Its infrastructure so just use what’s already there in RFCs
  Alternative: Extend and reuse NtfSubscriptionControl, needs extra work for questionable gain

## Slide 10: Thank you!