# 3GPP TSG-SA5 Meeting #140e	S5-216173

# E-meeting, 15-24 November 2021

# Source:	Huawei

# Title:	pCR 28.556 update Policy activation and deactivation procedure

# Document for:	Approval

# Agenda Item:	6.4.11

# 1	Decision/action requested

The group is asked to discuss and agree on the proposal.

# 2	References

[1]	TS 28.556 v0.4.0 Policy management for 5G mobile networks

# 3	Rationale

The policy activation and deactivation can be achieved by using modifyMOIAttributes operation for changing the policyStatus.

# 4	Detailed proposal

It is proposed to apply following changes in [1].

1st modified section

## 4.6	Policy Activation

The Figure 4.6-1 illustrates the procedure for activating a new policy.

Figure 4.6-1 Procedure for activating a policy

- MnS Consumer sends a request to activate a policy instance to MnS Producer (modifyMOIAttributes operation as defined in TS 28.532 [4] is used for changing the policyStatus to ACTIVATED).

- Based on the request, the MnS Producer activate the concrete policy MOI (i.e. instance of policy IOC).

- MnS Producer sends a response to the MnS Consumer.

## 4.7	Policy Deactivation

The Figure 4.7-1 illustrates the procedure for deactivating a policy.

Figure 4.7-1 Procedure for deactivating a policy

- MnS Consumer sends a request to deactivate a policy instance to MnS Producer (modifyMOIAttributes operation as defined in TS 28.532 [4] is used for changing the policyStatus to DEACTIVATED).

- Based on the request, the MnS Producer deactivate the concrete policy MOI (i.e. instance of policy IOC).

- MnS Producer sends a response to the MnS Consumer.