## Slide 1: 3GPP SA5 standardization work related to autonomous networks
Thomas Tovinger, SA5 Chair, Ericsson
Zou Lan, SA5 Vice-Chair, Huawei

## Slide 2: Contents
3GPP & SA5 introduction
Overview of 3GPP SA5 Rel-17 WIs/SIs
3GPP SA5 Autonomous Network related work
    Intent driven management
    Control loops
    Management data analytics
    SON
    Levels of Autonomous Network
    Network slicing
Summary

## Slide 3: 3GPP & SA5 Introduction

## Slide 4: 3GPP standards eco-system
5G Projects
Official Liaisons on specification work:
Certification Bodies
Organizational Partners (OPs)
The 3GPP Organizational Partners (OP) - 7 Standards Organizations - from China, Europe, India, Japan, Korea and the United States.
Participation in 3GPP by companies and organizations becoming Members of one of these 7 OPs.
Inputs on market requirements may come in to the Project via 3GPP Market Representation Partners (MRP).
There is a lot of additional external liaison activity…SDOs, Industry bodies, projects…
Market Representation Partners (MRPs)
450 MHz Alliance, AISG, Bluetooth, Broadband Forum (BBF), CableLabs, International Special Committee on Radio Interference (CISPR), CTIA, Digital Video Broadcasting (DVB) Project, Ecma, International, Expert Group for Emergency Access (EGEA), Eurescom, COST 273, European Radiocommunications Committee (ERC), Fixed Mobile Convergence Alliance (FMCA), GCF, Global TD-LTE Initiative (GTD), GPS Industry Council, GSM Association, HomeRF Forum, IDB Forum, IEEE, Internet Engineering Task Force (IETF), IrDA, International Multimedia Telecomunications Consortium (IMTC), Internet Streaming Media Alliance, ISO-ITU expert group, ISO MPEG / JPEG, ITU-T SG2, JAIN tm (Javatm APIs for Integrated Networks), The Java Community Process (JCP), Liberty Alliance Project, Metro Ethernet Forum (MEF), NENA, NGMN (Next Generation Mobile Networks), oneM2M, OMA (Open Mobile Alliance ), Open Networking Foundation (ONF), Open IPTV Forum, Object Management Group (OMG), PCS Type Certification Review Board (PTCRB), Portable Computer and Communications Association (PCCA), Presence and Availability Management (PAM) Forum, RSA Laboratories, SDR Forum, Sun Micro Systems Inc., Steerco, SyncML Initiative, Trusted Computing Group (TCG), TeleManagement Forum (TMF), TCCA, TIA /TR45, TIA/TR47, ITU, TV-anytime Forum, Voice eXtensible Mark-up Language (VXML) Forum, Wi-Fi Alliance, Wireless Broadband Alliance (WBA), WLAN Smart Card Consortium, Wireless World Research Forum (WWRF), World Wide Web Consortium (W3C)
(Source: extract from https://www.3gpp.org/about-3gpp/15-bodies-with-which-3gpp-has)
700+ companies

## Slide 5: Specification Groups
The TSGs prepare, approve and maintain the 3GPP Technical Specifications and Technical Reports.
They are responsible for the detailed time frame and management of the work’s progress;
  Management of work items;
  Technical Co-ordination;
  Proposal and approval of work items within the agreed scope and terms of reference of the TSG
The TSG Chairman is responsible for the overall management of the technical work within the TSG and its Working Groups.
The WG Chairman is responsible for the overall management of the technical work within the WG and its sub-groups.

## Slide 6: Operators in SA5 (attending the May SA5#137e meeting)
  AT&T
  China Mobile
  China Telecom
  China Unicom
  Deutsche Telecom
  KDDI
  KPN/TNO
  Orange
  T-Mobile USA
  Telecom Italia
  Telefonica
  U S Cellular
  Verizon
  Vodafone

## Slide 7
3GPP 5G Timeline
Release timing
Phases for the normative 5G work:
  Normally planned as 18-month cycles. Pandemic => 2 years
  Phase 1 (Rel-15) addresses the more urgent subset for commercial deployments
  Phase 2 (Rel-16) Completes the 3GPP IMT 2020 submission (ITU-R) and addresses all identified use cases & requirements
  Release 17 and Release 18 are 5G Releases too…
Release 18
Release 17
5G Study
Release 16
Release 15
Phase 2
Phase 1
03/2022
06/2020
06/2018
Notes: 10/31/16

## Slide 8: 3GPP SA5 Autonomous Network related work

## Slide 9: Overview of 3GPP SA5 OAM Rel-17 WIs/SIs

## Slide 10
Intent driven management for mobile networks - Introduction
  Objective: To simplify the management interfaces by using expressions of intent
  Release 17 study: Concept, scenarios and potential solutions
      3GPP Technical Report (TR) 28.812: “Telecommunication management; Study on scenarios for Intent driven management services for mobile networks”
  Release 17 normative work item – in progress:
      3GPP draft Technical Specification (TS) 28.312 (v050): ” Management and orchestration; Intent driven management services for mobile networks”

## Slide 11: Definition and concept - Intent driven management (draft TS 28.312)
Intent driven MnS
Definition
Intent: the expectations including requirements, goals and constraints given to a 3GPP system, without specifying how to achieve them.
Intent categorizes based on user types
Intent from Communication Service Customer (Intent-CSC): For example, Intent-CSC can be 'Enable a V2X communication service for a group of vehicles in certain time'.
Intent from Communication Service Provider (Intent-CSP): For example, Intent-CSP can be 'Provide a network service supporting V2X communications for highway-417 to support 500 vehicles simultaneously'.
Intent from Network Operator (Intent-NOP): For example, Intent-NOP can be 'Provide a radio network service to satisfy the specified coverage requirements and UE throughput requirement in certain area'.
Intent driven closed-loop
Relation between rule, policy and intent
Note: The content of this slide is under discussion in the draft TS 28.312.

## Slide 12
Closed loop communication service assurance - Introduction
  Release 16 (normative) 3GPP TS 28.535 (Requirements) and 28.536 (Stage 2 and 3):
    Concept for open control loops and closed control loops
    Use cases, requirements and a model for closed loop communication service assurance
  Release 17: Continuation work item on Enhanced closed loop SLS assurance (same TSs 28.535/536)

## Slide 13: Definition and concept - Control loops (TS 28.535)
  Control loops
The basic principle: Adjust the value of a measured or observed variable to equal the value of a desired goal
  Open control loops
In an open control loop, the human operator intervenes in one or more of the process steps inside the loop, see Figure 4.2.3.1.
  Closed control loops
In a closed control loop, there is no direct involvement of a human operator or other management entity in the control loop - the control loop is fully automated.
Figure 4.2.4.1: Closed control loop entities
Figure 4.2.3.1: Open control loop entities
Note: The content of this slide is under discussion in the TS 28.535.
Notes: A control loop is a building block for management of networks and services. The basic principle of any control loop is to adjust the value of a measured or observed variable (expressed as for example an attribute) to equal the value of a desired goal (expressed as for example an attribute). The producer of the measurements or observations, the control service, and the controlled entity are all required to create a control loop.
  Open control loops
In an open control loop, the human operator intervenes in one or more of the process steps inside the loop, see Figure 4.2.3.1. The human operator is in control of the steps in the control loop, including decisions taken in the loop. The management system collects, analyses and presents the data to the operator, but the operator decides which action to take. In this case, the completion time for control loop is dependent on availability and reaction time of a human operator or other management entity.
  Closed control loops
In a closed control loop, there is no direct involvement of a human operator or other management entity in the control loop, the control loop is fully automated. As shown in Figure 4.2.4.1 the human operator or management entity is not directly controlling the details inside the process steps but provides control outside the loop. For example, configuring goals for the control loop to make autonomous decisions within the boundaries of the set goal. Once the control loop is configured with the goal, the controlled entity is adjusted according to the set goals.

## Slide 14: Closed control loop governance and monitoring (TS 28.535)
Figure 4.2.5.1 Closed control loop governance and monitoring
Figure 4.3.1: Overview of closed control loop information flows
  Communication service assurance relies on a set of management services that together provide the CSP with the capability to assure the communication service as per agreement (for example an SLS) with a CSC (e.g. enterprise).
  Closed control loop governance describes a set of capabilities to allow MnS consumer to govern closed control loop, including:
      Lifecycle management of closed control loop, including create, modify, activate/deactivate, delete closed control loop.
      Configure goals for closed control loop.
Note: The content of this slide is under discussion in the TS 28.535.

## Slide 15
  Objective: In conjunction with AI and ML techniques to bring intelligence and automation to the network service management and orchestration
  Release 17: Study on concept, use case, requirements and solutions for Management Data Analytics Service (MDAS)
      3GPP TR 28.809: “Study on enhancement of management data analytics”
  Release 17: Continuation (normative) work item for MDAS
      3GPP draft TS 28.104: “Management and orchestration; Management Data Analytics”
Management Data Analytics Service - Introduction

## Slide 16
Management Data Analytics Service Study (TR 28.809)
  An example of MDA process where the ML model and the management data analysis module are residing in the MDAS producer
      There are two kinds of processes for MDA, the process for ML model training and the process for management data analysis.
  32 MDA related use cases in 10 categories are recognized in the study phase.
Figure 5.3-1: Example of MDA process

## Slide 17: 5G SON (Self Organizing Networks) (TS 28.313 / 28.541)
Figure 4.1.1-1: Overview of SON Framework
  5G SON Concepts:
    Centralized SON:
        Cross Domain-Centralized SON
        Domain-Centralized SON
    Distributed SON
    Hybrid SON.
  Management services for SON:
      RACH Optimization (Random Access Optimisation)
      MRO (Mobility Robustness Optimisation)
      ANR management in NG-RAN
      PCI configuration
      Load Balancing Optimization
      NSI resource allocation optimization
      Handover Optimization (separate WI)
      Capacity and Coverage Optimization (Note 1)
      Self-establishment of 3GPP NF (Note 1)
Note 1: The content of these two services is in the WI scope but not yet defined
Notes: Based on the location of the SON algorithm, SON is categorized into four different solutions that are possible for implementing various SON use cases, the solution is selected depending on the needs of the SON use cases.

## Slide 18
Levels of Autonomous Network - Introduction
  In 3GPP Release 17, SA5 has started a normative work item using a Rel-16 study/TR as input, developing the following draft TS:
  3GPP draft TS 28.100: “Management and orchestration; Levels of autonomous network”
  Status summary of this work item:
    Aiming to define the different levels of autonomy of a network, from fully manual to fully automatic
    Currently (version 0.5.0): described a possibility and examples of classifying autonomous level properties of (individual) functions in a 3GPP system (e.g. Fault management).

## Slide 19: Definition and concept – draft TS 28.100
Scenarios
  Network and service planning
  Network and service deployment
  Network and service maintenance
  Network and service optimization
Management scope
Autonomy in NE/NF layer
Autonomy in domain network layer
Autonomy in cross domain network layer
Autonomy in communication service layer
Workflow
Intent handling
Awareness
Analysis
Decision
Execution
  Three Dimensions for evaluating autonomous network levels
Definition:
  Autonomous Network: telecommunication system (including management system and network) with autonomy capabilities which is able to be governed by itself with minimal to no human intervention.
  Autonomous Network Level: describes the level of autonomy capabilities in the autonomous network.
Note: The content of this slide is under discussion in the draft TS 28.100.
Figure 4.3.3-1: Autonomy for different management scope
Figure 4.3.4-1: Categorization of the tasks in the workflow for evaluating autonomous network levels

## Slide 20: 3GPP SA5 External collaboration on E2E network slicing
ETSI NFV
IETF
3GPP SA5
NGMN
5G-ACIA
ETSI ZSM
GSMA
3GPP SA5 has close collaboration on E2E network slicing with the following industry groups/SDOs:
GSMA: Align service profile with GSMA GST
5G-ACIA: Management exposure capability taking requirements related to Connected Industries and Automation Applications
NGMN: Network slicing concept and operators’ requirements
ETSI ZSM: End to end network slicing procedure
IETF: Collaboration on Transport network
ETSI NFV: Collaboration on virtualization aspects

## Slide 21
Summary
  SA5 already has experience of management of automation from the SON work in 4G/LTE, reused and further developed for 5G.
  SA5 now has 10 active work items directly related to autonomous networks.
  Reaching full autonomous network is a step by step approach. SA5 is working on the management features and management services which support different levels of autonomy.
  SA5 is currently collaborating with GSMA, TM Forum, NGMN, 5G-ACIA, ETSI ZSM, ETSI NFV and IETF on autonomous networks related work.
Meeting | Start date | End date
SA5#138-e | 23 Aug 2021 | 31 Aug 2021
  Next SA5 meeting：

## Slide 22
www.3gpp.org
For more Information:
info@3gpp.org
thomas.tovinger@ericsson.com
zoulan@huawei.com
portal.3gpp.org
Thank you!