## Slide 1: Feasibility Study on Network and Service Operations for Energy Verticals A proposed SA5 study item
Erik Guttman erik.guttman@samsung.com Samsung Research Naiara Garcia Ahedo, EUTC

## Slide 2: Background
This study considers how ‘third party customers’ of mobile networks from the “energy utility vertical sector” can be better served if certain management interfaces exist in mobile networks.
SA1 has completed work on the “Smart Energy Infrastructure” service requirements.
There are ‘manageability service requirements’ that can be considered in SA5. We propose to initiate a stage 1 analysis in SA5 to pursue this.
This presentation will introduce the motivation and SA1 requirements as a way to help understand the proposal.

## Slide 3: Performance Monitoring for Proactive Response – to increase availability (1/3)
Considers reporting & alarms from the MNO to a 3rd party.
The problem
  Availability of the energy system depends upon communication services. Availability of the energy system is a critical service.
  Energy utilities use different communication services (mobile wireless access from more than one MNO, fixed, satellite, dedicated fiber, etc.) for many sites to provide redundancy.
  With sufficient performance information that indicates a degradation of service in a cell, region, etc., the energy utility service provider can switch to a redundant communication system with service continuity.
  There are no standards to communicate the required communication performance information, so energy utility service providers have to undertake non-standard integration with each MNO.
The opportunity
  By creating standard interfaces for reporting performance (degradations) in the mobile network, energy utility service providers can achieve improved availability.

## Slide 4: Performance Monitoring for Proactive Response – to increase availability (2/3)
The use case (SA1) [informative only]
  Upward facing arrows
Normative requirements
  The 5G system shall provide information on the current availability of a specific communication service in a particular area (e.g. cell ID) upon request of an authorized entity.
  The 5G system shall provide a means by which an MNO informs a third party of network events (failure of network infrastructure affecting UEs in a particular area, etc.).
  Based on MNO policy, the 5G system shall provide a mechanism to automatically report service degradations, communications loss, and sustained connection loss in a specific geographic area (e.g., a cell sector, a cell or a group of cells) to a third party.
    NOTE 8: These reports use a standard format. The specific values, thresholds, and conditions upon which alarms occur can include the measured values for end-to-end latency, service bit rate, communication service availability, end-to-end latency jitter, etc. for a UE, the UE’s location, and the time(s) during which the degradation occurred.

## Slide 5: Performance Monitoring for Proactive Response – to increase availability (3/3)
    The information in the figure is an example only. The actual information is FFS.
The gaps with the existing standard need to be identified, by means of corresponding use cases and analysis of the information they require.

## Slide 6: Performance Reporting for Proactive Response – to increase serviceability (1/3)
Considers reporting from a 3rd party to an MNO.
The problem
    Availability of the energy system depends upon communication services. Availability of the energy system is a critical service.
    When communication performance in the energy utility network degrades or communication fails, it is essential that problem in the communication system (considered ‘end to end’) is identified, or the incident is resolved.
    The energy utility service provider has extensive insight into their networks and their performance, but this information is not available to the MNO through standard interface.
    Resolution of problems and ending of outages (incidents) requires substantial communication between the energy utility service provider and MNO at a critical time, which is currently not as efficient as it should be in many cases.
    EXAMPLE USE CASE: the energy utility service provider has a communication outage & suspects it is due to a base station problem. The energy utility service provider reports this to the MNO. The MNO can confirm whether it is a known problem or not. If the answer is “yes” then the utility operator knows how to handle the issue & ideally does not need to send a service person to the facility in person to troubleshoot the communication issue.
The opportunity
  By creating standard interfaces for reporting performance (degradations) in the customer network, energy utility service provider can enhance the possibility for the MNO to identify problems and incidents, as well as possibly to eliminate the possibility that these problems or incidents arose in the mobile network.
  This could lead to more efficient problem resolution and incident handling processes by both the MNO and energy utility service provider .

## Slide 7: Performance Reporting for Proactive Response – to increase serviceability (2/3)
The use case (SA1) and output requirements
  Downward facing arrows
    NOTE: This figure from TR 22.867 is informative.
SA1 agreed requirements TS 22.261, 6.23.2
  The 5G system shall provide a mechanism for an authorised third party to report to an MNO service degradations, communication loss, and sustained connection loss.
    NOTE 9: These reports use a standard format. The specific values, thresholds, and conditions upon which alarms occur can include the measured values for end-to-end latency, service bit rate, communication service availability, end-to-end latency jitter, etc. for a UE, the UE’s location, and the time(s) during which the degradation occurred.
    NOTE 10: What the MNO does with such reports is out of scope of 3GPP.

## Slide 8: Performance Reporting for Proactive Response – to increase serviceability (3/3)
This is not (yet) supported in SA5 specifications.
  The information in the figure is an example only. The actual information is FFS.

## Slide 9: Recovery of Electrical Energy Distribution (1/3)
The situation as it is now, the problem:
  When there is an energy outage, this will impact the telecommunication network as well. This can result in communication service outages.
  In many cases, energy distribution system requires telecommunication services to recover rapidly by means of ‘distribution automation’ and other smart energy services.
  Recovery can therefore be prolonged to hours instead of minutes, as manual intervention becomes necessary.
There is no standard and formal means for the energy utility service provider and MNO to exchange energy system recovery information and ‘autonomous power operation’ of the telecommunication network.
  If the MNO knew when the energy utility service provider required telecommunication services for recovery, and where, the MNO could take an active role in the recovery process.
  If the energy utility service provider knew how much autonomous power capacity the telecommunication network had, and where, they could more effectively plan their recovery.

## Slide 10: Recovery of Electrical Energy Distribution (2/3)
SA1 conclusion - 22.104, 9.2
Subject to regulatory requirements and operator policy, the 5G system shall support a mechanism by which an MNO can identify the ability of the MNO's infrastructure to continue operation despite a lack of electrical supply service, specifying which physical regions would be affected in terms of physical topology and the remaining time in which operation is possible.
  NOTE1: This information can facilitate energy distribution system recovery operations.
Subject to regulatory requirements, the 5G system shall support a mechanism by which a third party can, in the event of an energy distribution system service interruption, communicate the energy distribution system recovery status in terms of location and time table to the MNO.
  NOTE2: This information can facilitate MNO operations to facilitate energy system recovery.

## Slide 11: Recovery of Electrical Energy Distribution (3/3)
Why this is not yet supported in SA5 specifications (the gap)
  This support has never been developed
  A model can be developed for exchange between energy utility service provider and MNOs that will be mutually beneficial for energy system recovery operations, e.g.
  The information in the above figure is an example only. The actual information is FFS.