# 3GPP TSG-SA5 Meeting #141e	S5-221215

# E-meeting, 15-24 November 2021

# Source:	Huawei

# Title:	pCR 28.819 update notified of new NF version scenario

# Document for:	Approval

# Agenda Item:	6.5.3

# 1	Decision/action requested

The group is asked to discuss and agree on the proposal.

# 2	References

[1]	TR 28.819 v 0.4.0 Management and orchestration; Study on continuous integration continuous delivery support for 3GPP NFs

# 3	Rationale

Update the description in clause 6.1 to align the requirements and solutions for notified of new NF version scenario.

# 4	Detailed proposal

It is proposed to apply following changes in [1].

1st modified section

## 6.1	Scenario X: The operator is notified of the delivery of a new NF version from the NF supplier

### 6.1.1	Description

Figure 1 A New NF is released

The NF supplier publishes a new release of an NF used by the operator in Figure 1. When a new release is published the operator’s 3GPP management system should become aware of its availability and fetch the newly released version of the NF. There are two possibilities for this use case

- The 3GPP management system fetches the new release of the NF from a location provided by the NF supplier

- The 3GPP management system receives the newly released NF from the NF supplier

Both cases should be supported.

### 6.1.2	Potential Requirements

REQ-New_NF_CICD-1: The 3GPP Management system should be aware of the locations where any authorized NF suppliers provide notification of new releases of the NFs.

REQ-New_NF_CICD-2: The 3GPP Management system should be able to receive the new release of the NF from an authorized NF supplier.

REQ-New_NF_CICD-3: The 3GPP Management system should be able to fetch the new release of the NF from the location provided by an authorized NF supplier

### 6.1.3 Possible solutions

#### 6.1.3.1 Alternate 1

As part of the business agreement to purchase the license to use the NF, the NF supplier indicates to the operator where to subscribe to receive NF software updates. The operator’s 3GPP Management system subscribes to the said address to receive notifications of new NF versions. When the vendor internal processes are completed, and an updated new release of the NF is available for the operator to test and deploy, the vendor provides a notification to the operator. The notification may include information such as authentication, payment details and the requests of data for feedback, the location on where to fetch the new NF version and the corresponding NF information , the NF information  may include details such as:

- The NF type - example: AMF, SMF.

- An globally unique identifier (e.g., VnfdId) for the new release of the NF and the corresponding release model information

- An identifier (e.g., DN) of the NF which needs to be updated, if any.

- A list of newly added optional features in the new release and the corresponding variables to enable/disable those features

- The tests to be run on the NF as provided by the vendor – with an an address to fetch those tests (e.g., the location in the VNF package)

- Vendor information

- An address where to send feedback to the NF supplier related to operator testing and use of the NF.

.