3GPP TSG-SA5 Meeting #141-e 	S5-221318

# e-meeting, 17 -26 January 2022

# Source:	Ericsson

# Title:	Adding use case for operator defined trigger

# Document for:	Approval

Agenda Item:	7.5.3

# 1	Decision/action requested

Include the proposed changes in TR 28.826.

# 2	References

[1]		3GPP TR 28.826: " Study on Nchf charging services phase 2 improvements and optimizations"

# 3	Rationale

New use case on charging request optimization.

# 4	Detailed proposal

First change

## 5.2	Charging request optimization

### 5.2.1	General

The number of requests from the network function to the CHF is controlled by the number events that require immediate triggering. This means that being able to have less immediate triggers will also minimize the number of requests. There is today a possibility to generate management intervention trigger immediately for events from management requiring reporting of unit usage immediately.

### 5.1.2	Use cases

#### 5.1.2.1	Use Case #1a operator defined trigger

An operator has set up some own defined triggers related to events generated by the network or management systems, these events doesn’t require immediate reporting, just that the event is recorded, and the units counted before and after.

### 5.1.3	Potential charging requirements

REQ-CH_REQ-01: Possibility to support other than immediate trigger for own defined management or network triggers.

### 5.1.4	Key issues

The following key issues are identified:

-	Key Issue #1b: What trigger to use.

-	Key Issue #1c: What information to be included with the trigger, if any.

End of changes