## Slide 1: DP on external API for Capability Exposure
Source: Alibaba Group, AsiaInfo
S5-222679

## Slide 2: Options for Capability Exposure - Motivation
So far, there is an ongoing discussion on how to expose the MnS to the external customer in the case that the external customer can consume exposed MnS directly from OSS. Two possible options are listed below:
  Exposed MnS is exposed directly via MnS producer for exposed MnS, for example NSMF, NSSMF, etc
  Exposed MnS is exposed via a dedicated proxy (e.g. EGMF)
The objective of this discussion paper is to converge on this aspect.

## Slide 3: Exposure in SA2 – NEF
In SA2, a dedicated function named Network Exposure Function is used for exposing any information from 5GC to AF that is external to the Network Operator. NEF has the following functionalities:
  Exposure of capabilities and events:
  - NF capabilities and events may be securely exposed by NEF for e.g. 3rd party, Application Functions, Edge Computing as described in clause 5.13.
  Secure provision of information from external application to 3GPP network:
  - It provides a means for the Application Functions to securely provide information to 3GPP network, e.g. time synchronization service information and service specific information. In that case the NEF may authenticate and authorize and assist in throttling the Application Functions.
  Translation of internal-external information:
  - It translates between information exchanged with the AF and information exchanged with the internal network function. For example, it translates between an AF-Service-Identifier and internal 5G Core information such as DNN, S-NSSAI
Observation
  SA5 may leverage the same design principle and specifies a dedicated function (e.g. EGMF) for managing the NF capability exposure, secure provision of information from external application to 3GPP management system, and also translation of internal-external information.

## Slide 4: Exposure via dedicated exposure function
External API: used for external customer to discovery and consumer exposed MnS from exposure function, exposure function collects the MnS from MnS producer within the 3GPP management system and expose to external customer.
  External customer can reuse the operation from generic management service (defined in TS 28.532) to request for exposed MnS from exposure function.
  Apart from the generic operation, enhancement is needed, for example, the external customer needs to carry the authorization information (e.g. token) for consuming the MnS discovery service for NSC or exposed MnS;
Internal API: Used for MnS producer to offer service (e.g. MnS, discovery related information) to exposure function based on the request from external customer.
  Internal API can reuse the operation from generic management service.
The exposure function has the following group of MnS producers that within OAM:
  Offer discovery service for external customer
  Offer authentication and authorization service to external customer
  Perform access control, and expose MnS with the access permission to the external customer
  Negotiation for customer specific information (e.g. with BSS)
MnS producer
3GPP management system
External Consumer A
exposed MnS A
exposed MnS B
External Consumer B
External Consumer C
(For example Generic Fault Supervision)
Discovery service
Internal APIs
MnS producer for NSC
Authentication and Authorization service producer for NSC
MnS discovery service producer for NSC
Custom specific information management service producer for NSC

## Slide 5: Proposal
Focus on the external API from the group of MnS producers within the exposure function, and study the impact on the existing Component A, B and C based on the group of MnS producers within the exposure function.