## Slide 1: DP on mapping of network slice operations and intent operations
Source: AsiaInfo

## Slide 2: Motivation
The intent operations have been defined in TS28.312，including creating intent, deleting intent ,querying intent, modifying intent, the motivation of discussion paper determines which existing intention operations can be used, and which intentions operations need to be created based on network slice operations.

## Slide 3: TS 28.312 intent operations
intent operations are defined in TS 28.312 clause 4.2.2,including :
  Create an intent, a MnS Consumer request to create a new intent on the MnS producer.
  Activate an intent, MnS Consumer request to activate an intent on the MnS producer when the intent is suspended.
  De-activate an intent, MnS consumer request to de-activate an intent on the MnS producer for a temporary suspension.
  Delete an intent, MnS Consumer request to remove an intent on the MnS producer.
  Modify an intent, MnS Consumer request to modify the content of the intent (e.g. expectation targets) on the MnS producer.
  Query an intent, MnS Consumer request to return the content and state (e.g. active, inactive) of the intent on the MnS producer.

## Slide 4: TS 28.531 network slice operations
network slice operations are defined in TS 28.531 clause 5.1,including :
  Network slice instance allocation
  Network slice instance subnet allocation
  Network slice instance deallocation
  Network slice subnet instance deallocation
  Obtaining network slice subnet instance information
  Network slice feasibility check
  Network slice instance activation
  Network slice instance deactivation
  Network slice instance modification
  Network slice subnet instance activation
  Network slice subnet instance deactivation
  Network slice subnet instance modification
  Network slice subnet configuration
  Exposure of network slice management data
  Exposure of network slice management capability
  Network slice subnet instance management capability exposure
  Network slice subnet feasibility check
  Network slice resource capacity planning
  Network slice subnet management with assigned priority
  Modification of network slice related requirements

## Slide 5: mapping of network slice operations and intent operations
Network slice operations | intent operations
Network slice instance allocation | Create an intent
Network slice instance subnet allocation | Create an intent
Network slice instance deallocation | Delete an intent
Network slice subnet instance deallocation | Delete an intent
Obtaining network slice subnet instance information | query an intent
Network slice feasibility check | N/A
Network slice instance activation | Activate an intent
Network slice instance deactivation | De-activate an intent
Network slice instance modification | Modify an intent
Network slice subnet instance activation | Activate an intent
Network slice subnet instance deactivation | De-activate an intent
Network slice subnet instance modification | Modify an intent
Network slice subnet configuration | Modify an intent
Exposure of network slice management data | query an intent
Exposure of network slice management capability | N/A
Network slice subnet instance management capability exposure | N/A
Network slice subnet feasibility check | N/A
Network slice resource capacity planning | Create an intent/Modify an intent
Network slice subnet management with assigned priority | Modify an intent
Modification of network slice related requirements | Create an intent/Modify an intent

## Slide 6: Proposal
Based on above the mapping relationship of network slice operations and intent operations , there are also some current and proposed slicing operations for which no equivalent intent operation yet has been defined, So the proposal is that the study may focus on defining intent operation on feasibility check and management capability exposure