# 3GPP TSG-SA5 Meeting #144e	S5-224124

# E-meeting, 27 June – 1 July 2022

# Source:	Huawei

# Title:	pCR 28.903 adding key issue for application lifecycle management

# Document for:	Approval

# Agenda Item:	6.9.7.1

# 1	Decision/action requested

The group is asked to discuss and agree on the proposal.

# 2	References

[1]	3GPP TR 28.903-020 “Study on alignment with ETSI MEC for Edge computing management”

# 3	Rationale

This pCR compares the application lifecycle management procedure using NEV MANO and MEC MEO (MEAO), and provide potential requirement for ECSP management system.

# 4	Detailed proposal

In the 1st change, it is proposed to add related references in clause 2 of TR 28.903-020 [1].

In the 2nd change, it is proposed to add a new key issue (Application lifecycle management) in the new clause 5.x of TR 28.903-020 [1].

1st change

# 2	References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

-	References are either specific (identified by date of publication, edition number, version number, etc.) or non-specific.

-	For a specific reference, subsequent revisions do not apply.

-	For a non-specific reference, the latest version applies. In the case of a reference to a 3GPP document (including a GSM document), a non-specific reference implicitly refers to the latest version of that document in the same Release as the present document.

[1]	3GPP TR 21.905: "Vocabulary for 3GPP Specifications".

[2]	The NBI requirements from GSMA OPG - https://www.gsma.com/futurenetworks/wp-content/uploads/2021/06/OPG-Telco-Edge-Requirements-2021.pdf

[3]	ETSI GS MEC 010-2 (v 2.2.1) (2022-02): " Multi-access Edge Computing (MEC); MEC Management; Part 2: Application lifecycle, rules and requirements management".

[4]	ETSI ISG MEC 003, "Multi-access Edge Computing (MEC); Framework and Reference Architecture".

[5]	3GPP TS 23.558: "Architecture for enabling Edge Applications".

[x]	3GPP TS 28.538: "Management and orchestration; Edge Computing Management (ECM)".

[y]	ETSI GS NFV-IFA 013 V3.4.1 "Network Functions Virtualisation (NFV) Release 3; Management and Orchestration; Os-Ma-nfvo reference point -Interface and Information Model Specification".

2nd change

# 5	Issue investigations and potential solutions for alignment with ETSI MEC

## 5.X	Key Issue#x: Application lifecycle management

### 5.X.1	Description

3GPP TS 28.538 [x] specifies the EAS lifecycle management procedure by interworking with ETSI NFV MANO by invoking InstantiateNsRequest or UpdateNsRequest operation as specified in ETSI NFV IFA013 [y]. An NFV Network Service (NS) as defined by ETSI NFV is a composition of Network Functions (NF) (VNF or PNF).

With ETSI MEC [3], MEO (when ETSI NFV is not involved) or MEAO (when ETSI NFV is involved) provides the application instance lifecycle management interface, which is similar to VNF LCM interface. The consumer of MEO or MEAO does not need to take creation of NS into consideration when requesting creation of an application instance.

The main issue related to application LCM is the following:

1, when and how ECSP management system create an NS when receiving the creating EAS request from ASP.

2, whether the application instance lifecycle management interface produced by MEO or MEAO could be used for EAS lifecycle management

### 5.X.2	Potential solutions

TBD

End of changes