# 3GPP TSG-SA5 Meeting #	S5- 225048

# August 2022, E-meeting

# Source:	Nokia

# Title:	pCR 28.908 Requirements on Mobility of AIML Context

# Document for:	Approval

# Agenda Item:	6.7.5.8

# 1	Decision/action requested

The group is asked to discuss and agree on the proposal.

# 2	References

[1] 	3GPP TR 28.908-010 “Study on Artificial Intelligence/Machine Learning (AI/ ML) management”.

# 3	Rationale

In several network automation use-cases, the characteristics of the respective AI/ML-enabled function need to be distinguished depending on the different contexts of the AI/ML-enabled function This pCR is to add the UC and potential requirements on support for different AIML Contexts.

# 4	Detailed proposal

Start of modification

# 5	Use cases, potential requirements and possible solutions

## 5.7	AI/ML context

### 5.7.1	Description

AIMLContext represents the status and conditions related to the AIMLEntity (cf. TS 28.105[4]). This may include the network context as defined in TS 28.104 [2] as well as other conditions that may be applicable to the AIMLEntity but are not part of network characteristics e.g. the time of day, season of the year. As part of AI/ML model performance management there is identification of the problem that the AI/ML model is facing. As described in TS 28.104[2], the differences in the network context, i.e., network status, under which data is collected to produce analytics, significantly affect the produced analytics. Similarly, the changes in the AI/ML context, e.g., the characteristics of the data related to the network status and conditions used for AI/ML model training, testing and deployment may affect the AI/ML entity performance, thus may represent a problem for the AI/ML entity. Thus management capabilities are needed to enable awareness of the AI/ML context in terms of the identification as well as monitoring and reporting of changes in AI/ML context as part of the identification of the problem that the AI/ML entity is facing.

### 5.7.2	Use cases

#### 5.7.2.1	AI/ML context monitoring and reporting

AI/ML context related to AI/ML model training, testing and deployment needs to be identified by characterizing the input data used by the AI/ML model is targeted to work. As an example, such characterization may be done based on the statistical properties of data. Monitoring of such AI/ML context serves to detect the changes and anomalies in the AI/ML context. Some anomalies may be considered as a problem that AI/ML entity is facing as it may lead to its performance degradation. Therefore, the consumer of the related AI/ML service needs to be informed about such observed AI/ML context change.

#### 5.7.2.N	Mobility of AIML Context

In several network automation use cases, the respective MLinference function cannot cover the complete network in one MLEntity instance. An MLEntity may be trained for a specific local context, and similarly, a different context may be applicable for inference, so the MLEntity may be characterized by different trainingContext and an expecetdInferenceContext. However, the network scopes where the data used for training and inference is collected does not always necessarily overlap with the network scopes in which the function makes decisions. The context of MLEntities or ML inferencefunction may need to distinguish between context for generating decisions or insights, the context from which it generates measurements or data as well as the context in which it is prepared before being active for inference. So the characteristics of the respective MLinference function need to be distinguished depending on the different contexts of the AI/ML inferencefunction. As such besides the validity scope defined by the trainingContext and an expecetdInferenceContext, the MLEntity should also be characterized by specific measurement scopes, where the input measurements are collected. And these may also be separately defined for the 2 use cases.

#### 5.7.2.M	Standby mode for AI/ML Functionality

Where the respective AI/MLinferencefunction cannot cover the complete network in one MLEntity instance, multiple instances of MLEntities may be required, one for each specific network scope, such as a cell. When a network automation use case requires several MLEntities instances, where each has its own limited validity scope (a geographical area or a subnetwork), transfers of machine learning context, i.e. “handovers” between the MLEntities covering different validity scopes (not necessarily identical to cell coverage area), are needed. Accordingly, the AI/MLinferencefunction or the MLEntities therein may have different roles, either as active or standby decision makers.

Consider the use case where a different MLEntity instance is needed for each Base station, i.e. the validity scope defined by the expecetdInferenceContext is a specific gNB. An instance of this is predictive ML-driven handover where an MLEntity  is trained to decide the optimal handover point and target cell based on the UE measurements. When the UE hands over to a cell in another gNB, a new MLEntity  instance fitting the new validity scope needs to be deployed in the UE. This is illustrated by Figure 5.N.1.a) where the UE uses MLEntity instance 1 in both cells 1 & 2 but when the UE hands over to cell 3, which is outside the validity area of MLEntity instance 2 needs to be deployed to the UE.

However, the deployment may require uploading the required MLEntity instance into the UE and initializing the MLEntity, for example to collect and feed the necessary input data to setup the required internal states, such as in Long-Short Term Memory (LSTM) Recurrent Neural Networks (RNNs). Accordingly, it may take significant time before the new MLEntity becomes active and operational. Moreover, if the UE hands over back to cell 2 after a short stay in cell 3 (pingpong), the UE needs to immediately re-deploy MLEntity instance 1, compounding the problem further.

To minimize this risk, there should be a "prepared scope" defined for each MLEntity, which is the scope within which the MLEntity  is deployed and initialized but not activated for inference.

- b)

Figure 5.N.1: Example mobility of AI/ML context - a) validity scopes b) validity and standby scopes

This is illustrated by Figure 5.N.1 8b) where besides the validity areas, standby areas are defined for each MLEntity  instance, e.g. MLEntity  1 is active in cells 1 and 2 but standby in cell 3. This implies that the AI/MLEntity  1 should be availed to the UE in cell 3 even if the UE cannot use MLEntity  instance 1 in cell 3. To support this, it must be possible to configure both, the validity areas and the standby areas for MLEntities and to define their role in them, i.e., either active, or prepared.

### 5.7.3	Potential requirements

REQ-MLCTX1 The producer AI/ML-related MnS including for training and inference should have a capability to identify and monitor the AI/ML context, as well as to inform the consumer about observed changes in AI/ML context ,

REQ-MLCTX-2 The 3GPP Management system should have a capability for an authorized consumer to configure or read the measurement scope of an MLEntity for AI/ML training or for AI/ML inference.

REQ-MLCTX-3 The 3GPP Management system should have a capability for an authorized consumer to read the MLEntity's inference cache scope that defines the network scope within which the MLEntity is activated to be in standby mode in preparation for elevating to active mode.

### 5.A.4	Possible solutions

TBD

End of modifications