# 3GPP TSG SA WG5 Meeting #145-e	S5-225174

# Auguest 15 – August 24, 2022, e-Meeting

# Source:	Samsung

# Title:	Discussion Paper on EES initiated EAS deployment

# Document for:	Endorsement

Agenda Item:	6.5.3.1

# 1	Decision/action requested

The group is asked to discuss and approve the proposals.

# 2	References

[1] 	3GPP S5-224387 “Reply LS on FS_eEDGEAPP, Solution for Dynamic EAS instantiation”

[3] 	3GPP TR 23.700-98 “Study on Enhanced architecture for enabling Edge Applications;”

[4] 	3GPP TS 23.558 “Architecture for enabling Edge Applications”

# 3	Discussion

As defined in [3], the EES may trigger the EAS instantiation due to an EAS discovery failure i.e no EAS is available or instantiated that matches the requirements in EAS discovery request.

SA5 has responded to SA6 in [1] stating that “SA5 currently do not have mechanism for EES to trigger/request EAS instantiation yet. SA5 is working the definition of related solutions as part of eECM WI”. The basic requirement for SA5 is to enable EES to initiate EAS deployment. This DP intend to find a solution for the same. Following are the possible alternative solutions:

Alternative 1: EES provides EAS Discovery performance measurements to facilitate EAS Instantiation

.

This solution involves EES sending EAS Discovery failure performance measurements to ECSP. ECSP decides, based on internal policy, when/if to initiate EAS Deployment towards provisioning MnS producer as specified in TS 28.538. The new performance measurement need to be defined

- EAS Discovery procedures fails at EES

- EES provides EAS Discovery performance measurements to facilitate EAS Instantiation

  - ECSP, acting as Performance Assurance MnS Consumer, creates a PerfMetricJob MOI to request for productions and delivery of EAS Discovery failure measurements per location.

  - ECSP send the required performance measurements. ECSP will use the existing mechanism of Performance Assurance in 3GPP TS 28.532 and TS 28.622.

  - Depending on this measurements ECSP can decide if they have to instantiate an EAS, with specific capabilities, on a particular location

  - ECSP initiate EAS deployment process as specified in TS 28.538

Alternative 2: EES notifies ECSP for the need of an EAS instantiation

This solution involves EES sending EAS Discovery failure notification to ECSP. ECSP  decides, based on internal policy, when/if to initiate EAS Deployment towards provisioning MnS producer as specified in TS 28.538. Either a new notifications need to be defined or the existing eventNotify notification need to be enhanced to indicate EAS Discovery failure information including target location etc.

- EAS Discovery procedures fails at EES

- EES notifies ECSP for the need of an EAS instantiation

  - Using new notification

    - ECSP, acting as Provisioning MnS Consumer subscribes for EAS Discovery Failure Notification. It uses NtfSubscriptionControl fragment as defined in TS 28.622

    - ECSP send the subscribed notification.

    - Depending on the information provided in the notification ECSP can decide if it have to instantiate an EAS, with specific capabilities, on a particular location.

    - ECSP initiate EAS deployment process as specified in TS 28.538

  - Using existing notifyEvent notification

    - ECSP, acting as Provisioning MnS Consumer subscribes for notifyEvent Notification. It uses NtfSubscriptionControl fragment as defined in TS 28.622

    - ECSP send the subscribed notification.

    - Depending on the information provided in the notification ECSP can decide if it have to instantiate an EAS, with specific capabilities, on a particular location.

    - ECSP initiate EAS deployment process as specified in TS 28.538

# 4	Proposals

It is proposed to endorse alternative 1 to be defined in the TS 28.538.

End of modified section