3GPP TSG-SA5 Meeting #145-e 	S5-225244

# e-meeting, 15 - 24 August 2022

# Source:	Huawei

# Title:	Add issues for use case 4

# Document for:	Approval

Agenda Item:	6.8.5.1

# 1	Decision/action requested

For approval

# 2	References

[1]	3GPP TR 28.834 v0.2.0 Study on Management of Cloud Native Virtualized Network Functions

# 3	Rationale

This contribution describes technical issues which relate to use case 4 in [1].

# 4	Detailed proposal

The flowing changes are proposed to [1].

1st change

# 2	References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

-	References are either specific (identified by date of publication, edition number, version number, etc.) or non-specific.

-	For a specific reference, subsequent revisions do not apply.

-	For a non-specific reference, the latest version applies. In the case of a reference to a 3GPP document (including a GSM document), a non-specific reference implicitly refers to the latest version of that document in the same Release as the present document.

- 3GPP TR 21.905: "Vocabulary for 3GPP Specifications".

- ETSI GR NFV-EVE019: "Report on VNF generic OAM functions".

- ETSI GR NFV-IFA 029: "Report on the Enhancements of the NFV architecture towards
Cloud-native and PaaS".

- ETSI GR NFV-IFA 008: "Network Functions Virtualisation (NFV) Release 4; Management and Orchestration; Ve-Vnfm reference point - Interface and Information Model Specification".

- ETSI GR NFV-IFA 011: "Network Functions Virtualisation (NFV) Release 4; Management and Orchestration; VNF Descriptor and Packaging Specification".

[x]	3GPP TS 28.526: "Life Cycle Management (LCM) for mobile networks that include virtualized network functions; Procedures".

[y] 3GPP TS 28.533: "Management and orchestration; Architecture framework".

2nd change

## 5.4	Use cases# 4: Scaling of cloud-native VNF

### 5.4.1	Description

As a pre-condition to this use case, the network is running normally. The 3GPP management system has subscribed to VNF instance lifecycle notifications from VNFM.

The use case begins when the 3GPP management system decides to scale a VNF.

The 3GPP management system requests VNFM to scale the VNF (as defined in ETSI GR NFV-IFA 008[4]). VNFM inspects the relevant VNF Descriptor (as defined in ETSI GR NFV-IFA 011[5]) to find the VNF components (VNFCs).

VNFM will add or remove VNFC instances as needed for the desired scaling level of the VNF. When the VNFCs have been added or removed, VNFM sends a notification to the 3GPP management system to notify that the VNF has been scaled. This notification includes information on the changes to VNFCs.

### 5.4.2		Issues

TS 28.526 [x] describes the procedures to be used by the 3GPP management system to request scaling. However, TS 28.526 [x] is written in terms (for example Network Manager and Element Manager) which are not compatible with the 5G architecture as described in TS 28.533 [y].

### 5.4.3		Requirements

None.

End of changes