## Slide 1: DP on Failure and Restart for Charging (SA5 #146)
Chen Shan Huawei

## Slide 2: SA5 5G Charging Architecture
Converged Charging System
  5G Charging architecture specified in TS 32.240 describes the interaction between CHF and CTF(s).
  Services, operations and procedures of charging using Service Based Interface specified in the TS 32.290 describes the service operations between NF consumers and NF producer for Charging.
Figure 4.2.3.1: Logical ubiquitous charging architecture and information flows for 5G systems – service based representation
Source: TS 32.240 V18.0.0
Table 6.2.1-1: NF services provided by the CHF
Source: TS 32.290 V18.0.0
Figure 4.2.1: Reference Architecture for the Nchf Interface; SBI representation
Source: TS 32.290 V18.0.0

## Slide 3: NF Consumer and NF Producer for Charging
Based on 3GPP SA5 Charging Specifications
Service Name | NF Consumer | NF Producer | Description | Specification
Nchf_ConvergedCharging | SMF | CHF | 5G data connectivity charging | TS 32.255, TS 32.290
 | AMF | CHF | 5G connection and mobility charging | TS 32.254, TS 32.290
 | NEF | CHF | Network exposure charging | TS 32.256, TS 32.290
 | IMS Nodes | CHF | 5G IMS charging | TS 32.260, TS 32.290
 | SMSF | CHF | Short message charging | TS 32.274, TS 32.290
 | 5GDDNMF | CHF | Prose charging | TS 32.278, TS 32.290
 | MMS Nodes | CHF | multimedia messaging service charging | TS 32.270, TS 32.290
Nchf_SpendingLimitControl | PCF | CHF | Spending limit control | TS 23.503, TS 29.594
Nnrf_NFManagement_NFRegister | CHF | NRF | Register the chf profile in the NRF | TS 32.290, TS 23.510

## Slide 4: Failure and Restart
Problem:
  The Consumer(e.g. SMF) in the charging data request is not reachable using the original NotifyURI because of the consumer change (e.g. Failure and Restart) .
Solution provided by CT4
  TS 29.500 Clause 6.5.3.2 Stateless NF as service consumer
  Based on the current charging specifications, the capabilities description in the clause 6.5.3.2 are not supported now.
3. An NF service producer may become aware of a NF service consumer change, via receiving an updated binding information (i.e. when the binding entity corresponding to the binding level is changed) in a HTTP request message, or via an Error response to a notification, via link level failures (e.g. no response from the NF), or via a notification from the NRF that the NF service consumer has deregistered. The HTTP error response may be a 3xx redirect response pointing to a new NF service consumer.
4. When becoming aware of an NF service consumer change, and if the new NF service consumer is not known, the NF service producer shall select a new NF service consumer as specified in clause 6.6 of 3GPP TS 23.527 [38]. If binding information is available and the binding mechanism is supported by the NF service producer, the reselection should be based on the binding information, as specified in clause 6.6.2 of 3GPP TS 23.527 [38], in clause 6.3.1.0 of 3GPP TS 23.501 [3] and in clause 4.17.12.4 of 3GPP TS 23.502 [4]. If binding information is not available or the binding mechanism is not supported by the NF service producer, the reselection is performed as specified in clause 6.6.3 of 3GPP TS 23.527 [38].
5. When becoming aware of an NF service consumer change, the NF service producer or SCP shall replace the authority part of the Notification/Callback URI with the new NF service consumer information and shall use that URI in subsequent communications, as specified in clause 6.6 of 3GPP TS 23.527 [38].
6. When the NF service consumer is changed, and if the new NF service consumer does not support handling notifications as specified in the above bullet 5, the new NF service consumer should update the NF service producers with the new Notification URI. For explicit subscriptions, this is achieved by updating the existing subscription or creating a new subscription, depending on the NF service producer's API. For implicit subscriptions, this is carried out via a service update request message.

## Slide 5: Binding Mechanism
Binding Mechanism Description in SA2 and CT4
  TS 29.500 clause 6.12.4 Binding for explicit or implicit subscription requests
  A NF Service Consumer may provide a Binding Indication:
  - in a service request creating an explicit or an implicit subscription, or in a notification response, by including a 3gpp-Sbi-Binding header (see clause 5.2.3.2.6) in an HTTP request or response respectively; or
  - for a default notification subscription in its NF profile in NRF (see clause 6.1.6.2.4 of 3GPP TS 29.510 [8]).
How to handling the problem in Charging aspect?
  The Consumer in the charging data request is not reachable using the original NotifyURI because of the consumer change (e.g. Failure and Restart) .
Notification in the CHF
  TS 32.290 clause 5.2.2.5 Nchf_ConvergedCharging_Notify Operation
    The Nchf_ConvergedCharging_Notify service operation provides means for CHF to notify the NF(CTF) to update or terminate charging of the PDU Session.
    The following procedures using the Nchf_ConvergedCharging_Notify service operation are supported:
    - CHF determines re-authorization.
    - CHF determines abort of charging.

## Slide 6: Suggestion
Based on the SBA/eSBA specified in the 3GPP CTs specifications, the CHF can be as the NF consumer and NF producer following the basic technical realization of Service Based Architecture.
  Based on 3GPP SA5 Charging Specifications for most charging scenarios, the CHF has been the roles as the NF producer, expect as the NF consumer for NRF.
  From the Failure and Restart description is the general principle of Technical Realization of Service Based Architecture specified in TS 29.500, TS 23.527, in the charging aspect, the Failure and Restart mechanism also should be followed.
Question: can CHF be NRF discovery charging service consumer, e.g. SMF, PCF？
Question: LS sends to CT4 in order to clarify that CHF supports and follow the failure and restart technical realization of Service Based Architecture if needed?

## Slide 7: Thank you!