## Slide 1: Network-as-a-Service (NaaS) Ecosystem And 3GPP SA5 work on capability exposure
Source: Telefónica, AT&T, Deutsche Telekom

## Slide 2: Outline
Introduction
CAMARA project overview
NaaS ecosystem map
Conclusions and recommendations

## Slide 3: Outline
Introduction
CAMARA project overview
NaaS ecosystem map
Conclusions and recommendations

## Slide 4
Customer Experience
Response to business needs (who and what for the APIs are going to be used?).
Enhance agility in the relationship with our customers.
Developer-oriented.
Reliability
Tokenization criteria and Auth 2.0 authentication.
End-to-end traceability of all Architecture layers to ensure performance.
Stability of back-end systems.
Implementation and standardization of error codes.
[Useful]
[Stable]
[Performance]
[Safe]
Scalability
Demand planning.
Definition of evolution roadmap.
[Future proof]
[Reusable]
Implementation
Simple to implement and easy to use.
Well documented
Developed under market standards.
Specific. Avoiding free interpretation
[Market standards]
[Simple]
[User friendly]
[Specific]
What is needed to achieve a successful API?

## Slide 5
Tenets for NaaS success
Moving from “standard-first”…
…to “develop-first”…
…opening the source code
SCALE
To be massively adopted by the developers and reach their ecosystems
GLOBAL REACH
To be made available across all networks, on a global footprint. Tech and telco needs standard APIs to justify their investment decision.
SIMPLE
Hiding unnecessary complexity, focusing on 3P business and operational needs
It is clear that standards are key for NaaS to gain traction in industry. However, traditional telco standards are not fast enough. Recommendation:
For this reason, we launched CAMARA, the open source community that develops the NaaS APIs

## Slide 6
Joint initiative between GSMA (reference telco association) and Linux Foundation (reference cloud association)
Mission: to foster the definition, development and testing/validation of NaaS APIs
API definitions and reference implementations are free to use (Apache 2.0 license)
  Github: https://github.com/camaraproject
CAMARA project

## Slide 7: Outline
Introduction
CAMARA project overview
NaaS ecosystem map
Conclusions and recommendations

## Slide 8: GSMA – LF: Ways of Working
API lifecycle: stages
Role of GSMA and Linux Foundation across the API lifecycle

## Slide 9: CAMARA Reference Architecture
CSP internal APIs: implemented in telco resources, including NW, cloud and OAM resources.
NW APIs: 3GPP (RAN, SA2), IETF, O-RAN, ONF, ..
Cloud APIs: ETSI NFV, k8s, …
OAM APIs: TMF Open APIs, 3GPP SA5, …
CSP external APIs: these are the CAMARA APIs. They are made available for consumption to invoker (3rd party) applications.
Design principles: open, global and user-friendly
CAMARA API invokers: App Service Providers (ASPs) and enterprise customers
Transformation Function: keeps information on correspondences between external APIs and internal APIs, and executes workflows to enforce these mappings
Decouples customer-facing calls from operator-facing processes.
Featured with scalability and observability capabilities.
Implemented with a modern cloud-native architecture, based on microservices.
API GW: policies the interaction between CSP and CAMARA API invokers.
Single entry-point for invokers to gain quick & easy access to CAMARA APIs
CAMARA invokers

## Slide 10: CAMARA Reference Architecture
CAMARA invokers
CSP internal APIs: implemented in telco resources, including NW cloud and OAM resources
NW APIs: 3GPP (RAN/SA2), IETF, O-RAN, ONF,…
Cloud APIs: ETSI NFV, CNCF, …
OAM APIs: TM Forum ODA, 3GPP SA5,…
CSP external APIs: these are the CAMARA APIs. They are made available for consumption to invoker (3rd party) applications.
Design principles: open, global and user-friendly
CAMARA invokers: Application service providers (ASPs) and enterprise customers
Transformation function: keeps information on correspondences between service APIs and internal APIs, and executes workflows to enforce these mappings
Decouples customer-facing calls from operator-facing processes
Featured with scalability and observability capabilities -> implemented with a modern cloud-native architecture, based on microservices.
API Gateway: policies the interaction between the CSP and CAMARA invokers
Single entry-point for invokers to gain quick & easy access to CAMARA APIs

## Slide 11: CAPIF as potential ref solution for API GW
To offer consistent experience for service API consumption in a global footprint, it is important to look for a reference solution for API GW. In this regard, CAMARA proposes CAPIF [ref]. Three reasons:
It implements needed capabilities: API onboarding, discovery, access control (OAuth2.0), auditing, accounting, logging,…
It is standard solution, with wide acceptance at industry
It is not tied to 3GPP APIs; CAPIF can be used as an API GW solution regardless of API semantics.
[ref] https://github.com/camaraproject/WorkingGroups/raw/main/Commonalities/documentation/SupportingDocuments/API-exposure-reference-solution.docx

## Slide 12: CAMARA governance structure
Steering Committee
Commonalities WG
API families
WG
API backlog WG
QoD API
Edge Cloud API
“X” API
….
Transversal technical WGs
API specific technical WGs
Governing body
Responsible for all aspects of oversight
Ways of working definition, creating/removing new/existing WGs, re-prioritization, etc.
API Projects
(one for each API family)
Priorities & roadmap
CAMARA API design guidelines
AuthN/Z solution
User consent mgmt
Documentation templates
….
Feedback
Guidance

## Slide 13: CAMARA API families – Status Quo
13
13
Quality on Demand (QoD) – mobile network
Edge Cloud – mobile network
Simple Edge Discovery API
Application Mgmt API
Traffic Influence API
Device Location API – mobile network
Device Status API – mobile network
SIM Swap – mobile network
Number verification (IP Auth) – mobile network
OTP validation – mobile network
Carrier Billing Check Out
Quality on Demand (QoD) API – WiFi/home
Device identifier API – mobile network
Anonymised subscriber identifier API – mobile network
Leading
partner
It provides the invoker with the ability to act on a mobile session between two endpoints (UE and AS), setting the performance of all traffic flows with one of these QoS profiles:
QoS_L -> throughput prioritized up to certain ”X” Mbps.
QoS_M -> throughput prioritized up to certain “Y” Mbps.
QoS_L -> throughput prioritized up to certain “Z” Mbps.
QoS_E -> latency stays stable under congestion.

## Slide 14: QoD API (mobile) – Example scenario
14
14
3rd party is a company that provides video streaming service to mobile subscribers (UEs) -> B2B2C customer.
To provision and operate this service, the 3rd party has a platform with different built-in applications. One of these application is ”traffic management”.
“Traffic management” application
Acts on congestion scenarios, to prevent certain UEs to suffer from performance degradation.
Consume QoD API, to modify the QoS of UE<-> AS traffic flows, on demand.
Modification consists in changing best-effort tag (default performance) to other tags (enhanced performance).

## Slide 15: Outline
Introduction
CAMARA project overview
NaaS ecosystem map
Conclusions and recommendations

## Slide 16
CSP internal APIs
CSP external APIs

## Slide 17: The role of SA5 – IT Process APIs
TMForum acts as general entry-point to operator’s IT stack (OSS, OCS, BSS).
TMForum is conveniently assisted by 3GPP SA5 for those cases where IT Process APIs trigger FCAPS mgmt operations on 4G/5G resources (e.g., NFs, sub-networks) and services.

## Slide 18: The role of SA5 – Transformation Function
GSMA and TM Forum will both provide support for the implementation of the transformation function via non-prescriptive guidelines and recommendations.
GSMA OPAG (Operator Platform Group) focuses on the mapping of CAMARA “Service APIs” to CSP internal APIs (i.e., technical APIs and/or IT process APIs)
TM Forum focuses on the mapping of CAMARA “OAM APIs” to CSP internal APIs.
It not always doable to map CAMARA “OAM APIs” into TM Forum Open APIs; for those cases, SA5 can provide non-prescriptive guidelines and recommendations on how CAMARA “OAM APIs” can be mapped to SA5 APIs (MnSs).

## Slide 19: Outline
Introduction
CAMARA project overview
NaaS ecosystem map
Conclusions and recommendations

## Slide 20: Industry-wide conclusions
The controllable and on-demand exposure of CSPs capabilities will pave the way for transforming telco networks into programmable service enablement platforms, facilitating network-application integration. This is a win-win for both CSPs and 3rd parties:
  CSP: new revenue streams and CAPEX amortization (monetizing investment made in fiber, edge computing and 4G+5G)
  3rd parties: flee from traditional best-effort service delivery, tapping now into exposed network capabilities to provide enhanced user experiences and contribute to digital ecosystem with new services.
CAMARA paves the way for industry-wide adoption of NaaS. 5 main reasons
  Gather the most relevant stakeholders from the Telco, Cloud and Technology Sectors into an open and growing community, supported by GSMA and Linux Foundation.
  Evolve the standardization process towards a contribution-driven “develop-first” style for APIs -> more agile standardization process, closer to that of IT/cloud than to traditional telco.
  APIs are designed according to what B2B and B2B2B customers are asking CSPs: APIs which are simple, easy-to-use and developer-oriented, providing similar customer experience such as the one existing in hyperscaler/OTT marketplaces.
  Work with customers and developer ecosystems to set requirements and priorities for service APIs, and validate their value through trials and use cases.
  It does not start from scratch: it builds on APIfication technologies (cloud-native) and assets (dev tools, repositories, test automation) extensively applied in IT environments
NaaS is a top priority for Tier-1 CSPs that are CAMARA members (see slide 6)
  Working hand in hand with industry partners to make sure this happen.

## Slide 21: SA5 level conclusions (as per endorsed S5-222574)
Specification, development of testing of CSP external APIs is an activity on-going in CAMARA.
  Some attempts made in the past to have these APIs worked out in SDO, and the experience was bad.
  There is a need to involved B2B and B2B2C customers from the very beginning, to make sure we meet their expectations, and these customers participate in CAMARA.
  CAMARA APIs build on internal APIs that are beyond 3GPP scope (ETSI MEC,…), so it is not appropriate for 3GPP to lead this activity. Coordination with SDOs via liasons, if needed, can be done through GSMA Operator Platform Group (OPG):
3GPP work should focus on solutions enabling the exposure of APIs.
  CAMARA focus -> NBI. Semantics of CSP external APIs (i.e., customer APIs), including ‘service’ APIs + ‘OAM’ APIs.
  GSMA focus -> Transformation Function. Non-prescriptive guidelines and recommendations on how to map ‘service’ APIs into CSP internal APIs.
  TMF focus -> Transformation Function. Non-prescriptive guidelines and recommendations on how to map ‘OAM’ APIs into CSP internal APIs.
  3GPP focus -> API GW. Mechanisms allowing on-demand, secure and auditable exposure of APIs. No other SDO has grabbed this flag yet.
new

## Slide 22: Authors’ view on selected topics
EMGF:
It is an artificially created block that intended to replicate NEF logic at OAM layer, but the reality is that it goes against the SBMA nature of 3GPP SA5 (not to define internal business logic). Authors’ belief is that EGMF as a stand-alone concept will not fly in 3GPP normative specs (and hence neither in operator's production networks).
Exposure through OSS vs BSS:
Authors’ position is that a CSP shall have one single-entry point to expose CSP capabilities, no matter the size nor nature of the 3rd parties (e.g., enterprise customers and ASPs). This single-entry point maps to ‘API GW’ in slide 9, and to ‘NaaS platform’ in slide 16. CAMARA recommendation is to using CAPIF as reference solution (see slide 11).
It is up to each CSP to decide where to place this single-entry point in their systems. Therefore, whether exposure is done through OSS or BSS is not a matter that requires standardization.
Scope of exposure topic
Out of scope of 3GPP: WHAT needs to be exposed (NBI and Transformation Function). This means that concepts such as filtering, combination, etc reported in TR 28.824 will need to be kept out of 3GPP discussions, since there are other SDOs dealing with them. These inludes CAMARA (NBI) and GSMA /TM Forum (Transformation Function).
  Exceptions: For certain cases, SA5 can play a role on Transformation Function as highlighted in slide 18.
In scope of 3GPP: HOW needs to be exposed (API GW). This means that 3GPP work shall deal with the exposure enablers.
.

## Slide 23: Recommendations to 3GPP SA5 (1/4)
3GPP SA5 work on ‘capability exposure’ topic articulated into three activities:
Activity #1: Promote collaboration with SA6 on CAMARA ‘API GW’ component.
Activity #2: Provide operators with internal solutions for a secure capability exposure in multi-tenant environments.
Activity #3: Provide non-prescriptive guidelines and recommendations on how CAMARA “OAM APIs” can be mapped to SA5 APIs (MnSs).

## Slide 24: Recommendations to 3GPP SA5 (2/4)
Activity #1: Promote collaboration with SA6 on CAMARA ‘API GW’ component.
Rationale: CAMARA notes that all operator capabilities, no matter their nature, should be made available through one single-entry point. This means that the CSPs shall have a single ‘API GW’ to expose whatever capability they want. However, the reality shows that what we have today are per-WG exposure solutions, for example: NEF (SA2), EGMF (SA5) and CAPIF/NSCE (SA6). This leads to
hyper-fragmentation in 3GPP standardization landscape, which sends out a bad message to industry
Siloed solutions that do not match to each other, which make it unclear for an operator how to integrate (and make a combined use of) them.
Recommended SA5 action plan:
To specify the functionalities that are required to expose operator capabilities, with focus on management capabilities. These functionalities include for example access control, auditability, API discovery and registry, etc.
To agree with CAMARA recommendation on using ‘CAPIF’ as reference solution for API GW (slide 11).
Compare specified functionalities against CAPIF features, and identify existing gaps.
Communicate identified gaps to SA6, so that they can enhance CAPIF with necessary extensions to bridge these gaps.
  SA5 can make suggestions on what these extensions might be. Nevertheless, the final decision is on SA6 side.

## Slide 25: Recommendations to 3GPP SA5 (3/4)
Activity #2: Provide operators with internal solutions for a secure capability exposure in multi-tenant environments.
Rationale: in NaaS, each tenant (ASP or Enterprise customer) requires consuming different capabilities from CSP network. In this multi-tenant environment, it is mandatory for operator to implement advanced solutions that guarantee:
resource controllability separation
provision of seggregated yet customized management spaces to different tenants.
Recommended SA5 action plan:
To discuss and agree on how SBMA concepts (MnS producers/consumer, discovery) fit with multi-tenancy.
To specify granular access control solutions fulfilling i) and ii). These solutions shall provide the ability to give tailored permissions to tenants in shared resource environments, ensuring these permissions do not conflict.
  These solutions can leverage MSAC outcomes, and may translate into enhancements/extensions to NRM (28.541).

## Slide 26: Recommendations to 3GPP SA5 (4/4)
Activity #3: Provide non-prescriptive guidelines and recommendations on how CAMARA “OAM APIs” can be mapped to SA5 APIs (MnSs)
Problem description: TM Forum will draft non-prescriptive guidelines and recommendations on mapping between CAMARA ”OAM APIs” and CSP internal APIs. This allows guiding less qualified operators and partners in their implementation of transformation function. However, as highlighted in slide 18, there may be cases wherein CAMARA ‘OAM APIs’ cannot be mapped to TM Forum Open APIs, but to SA5 instead. For those cases, SA5 can step in and draft the guidelines and recommendations on mapping towards SA5 APIs (MnSs).
Recommended SA5 action plan:
Brainstorm “OAM APIs” that can be interesting for ASPs (B2B2C market) and/or Enterprise customers (B2B market).
Identify which of these “OAM APIs” cannot be mapped to TM Forum APIs, but SA5 APIs (MnSs) instead. Provide guidelines and recommendations on how these mappings might look like, linking their feasibility to 3GPP Releases.
  Some mappings require the availability of SA5 features that are only available from a certain 3GPP Release onwards.
For identified “OAM APIs”, work out a serious proposal for “OAM API” and submit it to CAMARA API backlog.
  Serious means here that “OAM API” shall comply with the CAMARA API design guidelines documented here: https://github.com/camaraproject/WorkingGroups/blob/main/Commonalities/documentation/API-design-guidelines.md